## Slide 1: Memory Hierarchy
Chapter 9, Ramachandran and Leahy

## Slide 2: Recall: In a paged memory system
IF
ID/RR
EX
MEM
WB
Instruction
in
Instruction
out
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
What can we do?
  Increase cycle time
  Take 2 cycles in IF
Two memory accesses for every instruction: - access PTE
- access instr
Both bad!

## Slide 3: In a paged memory system
IF
ID/RR
EX
MEM
WB
Instruction
in
Instruction
out
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
TLB saves the day…
  PC  TLB  memory is only one memory access
  So we’re back in business….
Two memory accesses for every instruction: - access PTE
- access instr

## Slide 4: Are we really?
What’s the CPU clock cycle speed?
What’s the memory access time?
It’s roughly a 100:1 ratio!
~1ns
~100ns

## Slide 5: What happens to the pipeline?
IF
ID/RR
EX
MEM
WB
Instruction
in
Instruction
out
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
With a 100:1 ratio, what happens in the IF stage on a memory fetch?
99 bubbles!! On every instruction!!
Not sustainable.
FAIL!

## Slide 6: The register file and TLB…
They’re “kinda” memories, right?
Why are they not a problem?
TLB + Reg file  Static RAM (SRAM) technology
Memory  Dynamic RAM (DRAM) technology
SRAM  6 transistors per cell  faster  bulkier
DRAM  1 transistor per cell  slower  denser
Upshot: You can have size or speed but not both!
This also means “memory access” cannot always be part of the CPU clock cycle time

## Slide 7: What principle makes TLB work?
Locality
  Sequentiality of instructions in the program
  Sequentiality of data structures like arrays and structs
  “Recent” translations are stashed away from in-memory page tables into high-speed hardware
  Subsequent translations become faster  no need to go to memory for most PTEs
  What if we apply the same principle to the data and instructions we need?

## Slide 8: The principle is locality
Spatial locality
Temporal locality
Instr
I0
I1
I2
I3
…
Data
D0
D1
D2
D3
…
Adjacent memory locations
Loops
Revisit

## Slide 9: How do we put these two ideas together?
Locality
Small & fast or large & slow storage
 The concept of “cache”
TLB is a special instance of caching “addresses”

## Slide 10: The model
CPU
Cache
Main memory
How do you use
  Spatial locality?
  Temporal locality?
Small & fast
Large & slow

## Slide 11: Terminologies
Hit | Hit ratio h | h + m = 1
Miss | Miss ratio m | 
Cycle time | Tc cache access time | 
 | Tm memory access time | 
Memory access time | Same for SRAM Different for DRAM | 
Memory cycle time |  | 
Miss penalty | Tm | 
Effective memory access time (EMAT) | EMAT = Tc + Tm * m | 

## Slide 12: Current-day memory hierarchy
EMATi = Ti + Mi * EMATi+1
Hardware territory
OS territory

## Slide 13: Calculating EMAT
CPU
L1- cache
Main memory
L2- cache
h1 = 0.95; Th1 = 2 ns
h2 = 0.80; Th2 = 10 ns
Tm = 100 ns
EMAT?
EMATi = Ti + Mi * EMATi+1
EMAT1 = 2ns + 0.05 * EMAT2
EMAT2 = 10ns + 0.20 * EMAT3
EMAT3 = 100ns
-------
EMAT1 = 3.5ns
X
X
X

## Slide 14: Calculate the EMAT?
You have a one-level cache that has a hit rate of 90% and an access time of 10ns; your main memory has an access time of 100 ns.
11ns
110ns
12ns
20ns
10
EMATi = Ti + Mi * EMATi+1
EMAT1 = 10ns + 0.10 * EMAT2
EMAT2 = 100ns
-----
EMAT1 = 10ns + 0.10 * 100ns
EMAT1 = 20ns
Today’s number is 30,333

## Slide 15: Cache Organizations
Direct mapped
Fully associative
Set associative

## Slide 16: Direct mapped cache
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Given a memory address,
What is the numerical value of cache index?
1-bit cache tag
3 2 1 0
 Example: 4-bit memory address
Cache
Main Memory
3-bit cache index
(log2 of cache size)

## Slide 17: Types of misses
Compulsory (first time a block is brought in)
Capacity (cache is full)
Conflict (vying for space in a full set in the cache)
Compulsory > Capacity > Conflict
Another way to think about Conflict misses: Conflict misses are misses that would not occur if the cache were fully associative with LRU replacement. Fully associate caches can’t have conflict misses by definition.

## Slide 18: Example
0
1
2
3
4
5
6
7
mem loc 0
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory references: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
misses
hits
miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
These were compulsory misses.
This is the first time the address is begin brought into the cache.

## Slide 19: Example
0
1
2
3
4
5
6
7
mem loc 0 8
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory references: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
misses
hits
miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
This is also a compulsory miss.
This is the first time address 8 has been brought into the cache.

## Slide 20: Example
0
1
2
3
4
5
6
7
mem loc 0 8
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory references: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
misses
hits
miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
This is now a conflict miss.
There are two memory addresses mapped to the same cache cell.

## Slide 21: Example
0
1
2
3
4
5
6
7
mem loc 0 8 0
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory references: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
misses
hits
miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
This is now a conflict miss.
This is now a conflict miss.
There are two memory addresses mapped to the same cache cell.

## Slide 22: Example
0
1
2
3
4
5
6
7
mem loc 0 8 0
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
Memory references: 0, 1, 2, 3, 1, 3, 0, 8, 0, 9, 10
misses
hits
miss
1
001
3 2 1 0
 4-bit memory address
index = memory_address
mod cache_size
3-bit index
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
9 MOD 8 is 1

## Slide 23: How do we disambiguate data?
0
1
2
3
4
5
6
7
mem loc 0 8
mem loc 1
mem loc 2
mem loc 3
empty
empty
empty
empty
data
tag
1
0
0
0
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
3 2 1 0
 4-bit memory address
This remaining bit determines if cache data is for memory address 0 or 8, etc.
3-bit index
We use the rest of the memory address as the tag to label the data in the cache

## Slide 24: How do we know data is valid?
0
1
2
3
4
5
6
7
loc 8
loc 1
loc 2
loc 3
empty
empty
empty
empty
data
tag
1
1
1
1
valid
0
0
0
0
1
0
0
0
X
X
X
X
Valid
Tag
Data
At power-up, a cache may contain garbage!
Tags help disambiguate, not validate
Meta data
Real data
Fields in a Direct Mapped Cache

## Slide 25: What type of locality affects direct mapped cache performance?
Spatial locality
Temporal locality
Virtual locality
Spatial and temporal locality
20

## Slide 26: What does the cache entry contain?
You have a 64 entry direct-mapped cache for a memory with 16-bit addresses and 16-bit words (like LC-3).
1 bit valid flag, 6 bit tag, 10 bit data
1 bit valid flag, 10 bit tag, 16 bit data
1 bit valid flag, 10 bit tag, 6 bit data
2 bit valid flag, 12 bit tag, 16 bit data
30
One bit is required for the valid flag
The cache index is going to be 6 because log2(64)=6, so tag will be 16-6=10 bits
Memory word is 16 bits, so data has to be a 16 bits (or a multiple)

## Slide 27: Hardware
Cache
Tag
Cache Index
Valid
Tag
Data
.
.
.
.
.
.
=
hit
Data
To
CPU
31 ? ? 0
1K entries
?
?
?
?
?
log2 cache size
= 10 bit index
32 – 10 = 22 bit tag
Example: 32-bit addresses, 32-bit words

## Slide 28: Hardware
Cache
Tag
Cache Index
Valid
Tag
Data
.
.
.
.
.
.
=
hit
Data
To
CPU
31 10 9 0
1K entries
?
?
?
?
?
log2 cache size
= 10 bit index
32 – 10 = 22 bit tag
10
22
22
1
32
Where did this 32 come from?
Cache data is usually the width of the memory-to-cpu bus

## Slide 29: Interpreting memory addresses
Cache Tag
Cache Index
index = memory addr mod cache size
  MemAddr = 8  index = 0
  MemAddr = 0  index = 0
number of tag bits = memory addr size – cache index size
Why not the other way around?  use the low bits for cache tag?
Memory address

## Slide 30: Index first, tag last?
0
1
2
3
4
5
6
7
loc 0
empty
empty
empty
empty
empty
empty
empty
data
tag
1
0
0
0
valid
0
0
0
0
0
X
X
X
X
X
X
X
Access location 0
0
1
2
3
4
5
6
7
loc 0 1
empty
empty
empty
empty
empty
empty
empty
data
tag
1
0
0
0
valid
0
0
0
0
1
X
X
X
X
X
X
X
Access location 1
loc 2 3
0
1
2
3
4
5
6
7
loc 0 1
empty
empty
empty
empty
empty
empty
data
tag
1
0
0
0
valid
0
0
0
0
1
1
X
X
X
X
X
X
Access location 3
Cache occupancy if we switch index and tag is
BAD!!  loss of spatial locality
0
1
2
3
4
5
6
7
loc 0 1
empty
empty
empty
empty
empty
empty
data
tag
1
1
0
0
valid
0
0
0
0
1
0
X
X
X
X
X
X
Access location 2
loc 2

## Slide 31: Example
Let us consider the design of a direct-mapped cache for a realistic memory system.
  Assume that the CPU generates a 32-bit byte-addressable memory address.
  Each memory word contains 4 bytes.
  A memory access brings in a full word into the cache.
  The direct-mapped cache is 64K bytes in size (this is the amount of data that can be stored in the cache), with each cache entry containing one word of data.
  Compute the additional storage space needed for the valid bits and the tag fields of the cache.
Cache
Tag
Cache Index
31 17 16 2 1 0
Byte
offs
V Tag Data
49 48 32 31 0
-1- -16- -32-
-16- -14- -2-
Memory address
Consider only word address for lookup
Consider only real data
 64k/4=214 rows in cache
Meta data
(overhead)
Cache
4 bytes
…
…
…
Use for lookup
214 * (1 + 16) bits additional

## Slide 32: Memory address interpretation when single cache block contains multiple bytes

## Slide 33: A direct-mapped cache
Has a many-to-one mapping between a memory location and a cache location
Allows a memory location to be en-cached wherever there is space in the cache
Is so-called because there is a directory associated with the contents of the cache
Is usually much smaller than any other type of cache organization
Today’s number is 69,727
40

## Slide 34: In a direct-mapped cache with a t-bit tag
There is a 1-bit tag comparator for each cache line
There is a t-bit tag comparator for each cache line
There is a 1-bit tag comparator for the entire cache
There is a t-bit tag comparator for the entire cache
What is a comparator?
50

## Slide 35: Pipelined processor with caches
PC
I-Cache
ALU
DPRF
ALU-1
BUF
F
E
R
A
B
Decode
logic
BUF
F
E
R
ALU-2
D-Cache
BUF
F
E
R
DPRF
BUF
F
E
R
IF
ID/RR
EXEC
MEM
WB
data

## Slide 36
Data goes straight from cache in one cycle

## Slide 37
Data goes straight from cache in one cycle
Data has to come from memory in many cycles

## Slide 38
Data goes straight from cache in one cycle
Data has to come from memory in many cycles
Data is written to cache AND to memory

## Slide 39
Data goes straight from cache in one cycle
Data has to come from memory in many cycles
Data is written to cache AND to memory
Data is written to cache and will be written back to cache later

## Slide 40: Write-through operation
CPU
Main memory
Address
Address
Data
Data
Address
Data
Address
Data
Address
Data
Address
Data
Write Buffer
This is additional hardware – we need it to allow the CPU to proceed while the memory is finishing its write cycle

## Slide 41: Write back cache
Cache
Tag
Cache Index
Valid
Tag
data
.
.
.
.
.
.
=
hit
Data
To
CPU
.
.
Dirty
Additional meta data.
The data gets written back when someone needs the cache row.

## Slide 42: Read miss stalls
I1: ld r1,a; r1 <- memory at a
I2: add r3,r4,r5; r3 <- r4 + r5
I3: and r6,r7,r8; r6 <- r7 & r8
I4: add r2,r4,r5; r2 <- r4 + r5
I5: add r2,r1,r2; r2 <- r1 + r2
We can treat a read-miss in MEM in a similar fashion as we did previously with registers and the busy bits
MEM can reset the busy bit for r1 when it sees the read complete for I1 (instead of waiting for WB as we did before)

## Slide 43: Execution time with caches
Execution time = N * CPIAvg * cycle time
CPIeff = CPIAvg + Memory-stallsAvg
Execution time = N * CPIeff * cycle time
Execution time = N * (CPIAvg + M-stallsAvg) * cycle time
Memory-stallsAvg = misses per instructionAvg * miss-penaltyAvg
Total memory stalls = N * Memory-stallsAvg

## Slide 44: The effective CPI is…
Average CPI = 1.5
Average cache miss per instruction = 3%
Miss penalty = 20
1.8
2.1
21.5
7.5
No clue
CPIeff = 1.5 + (3% of 20) = 1.5 + 0.6 = 2.1 CPI
60

## Slide 45: Example
Consider a pipelined processor that has an average CPI of 1.8 without accounting for memory stalls.
  I-Cache has a hit rate of 95%
  D-Cache has a hit rate of 98%.
Assume that memory reference instructions account for 30% of all the instructions executed.
  80% are loads
  20% are stores
On average
  read-miss penalty is 20 cycles and the
  write-miss penalty is 5 cycles.
Compute the effective CPI of the processor accounting for the memory stalls.

## Slide 46: Solution
Cost of instruction misses: = I-cache miss rate * read miss penalty = (1 – 0.95) * 20 = 1 cycle per instruction
Cost of data read misses: = % memory reference instructions * fraction that are loads * D-cache miss rate * read miss penalty = 0.3 * 0.8 * (1 – 0.98) * 20 = 0.096 cycles per instruction
Cost of data write misses: = % memory reference instructions * fraction that are stores * D-cache miss rate * write miss penalty = 0.3 * 0.2 * (1 – 0.98) * 5 = 0.006 cycles per instruction
CPIeff = CPIavg + cost of I-cache misses + cost of D-cache misses = 1.8 + 1 + (0.096 + 0.006) = 2.902

## Slide 47: How to improve cache efficiency
Further exploit spatial locality
  Bring more from memory into cache at a time
Better organization
  Exploit working set concept

## Slide 48: Exploting Spatial Locality
Word 0
Word 1
Word 2
Word 3
Word 0
Word 1
Word 2
Word 3
Word 0
Word 1
Word 2
Word 3
Word 0
Word 1
Word 2
Word 3
.
.
.
Block 0
Block 1
Block 2
Block 3
0x00
0x04
0x08
0x0C
On miss bring in a whole block!

## Slide 49: Interpreting memory address
Cache Tag
Cache Index
Block Offset
t n b
b = log2 B
L = S/B
n = log2 L
t = a – (b+n)
S = Size of cache; B = Block size; L = lines in cache
This is really just the word number within the block

## Slide 50: Multi-word cache organization

## Slide 51: Write miss with multiple word cache
The missing block is first copied from memory into the cache; only then do we update the specific word being written

## Slide 52: Multiple word cache example
Direct-mapped cache
  32-bit byte-addressable memory address
  Each memory word contains 4 bytes
  Block size = 4 words (16 bytes)
  A memory access brings in a block
  64K byte cache.
  Write back cache with a dirty bit per word
tag
index
0
15
31
16
12 bits
log2 (64K/16)
16 bits
32 – 12 – 4
Blk off
4 3
4 bits
(log2 16)
16
32
32
32
32
0
1
2
…
4094
4095
word 0
tag
valid
1
1
0001
0021
dirty
word 1
word 2
word 3
1
0

## Slide 53: Implementing a multi word cache

## Slide 54: Increased block size?
Miss rate
blocksize
Increasing
total size
of cache
Exploits more spatial locality
Reduces miss rate
Where does it go from here?

## Slide 55: Increased block size?
Miss rate
blocksize
Increasing
total size
of cache
There is a point where things get worse
When the working set changes, larger blocks have to be fetched
Memory can only transfer so fast and it can become the bottleneck

## Slide 56: Working set considerations
WS 1
WS 2
WS 3
Cache
Memory
Unused
Working set considerations
Direct mapping can cause inefficient use of cache with overlapping working sets

## Slide 57: What would be best?
Allow any memory block to be brought into any cache block
This is similar to be able to bring in a virtual page into any available physical page frame
 Fully associative mapping

## Slide 58: Address interpretation in FA cache
Cache Tag
Index
No splitting memory addresses into “index” and “tag”
It all becomes tag!
Cache Tag

## Slide 59: Fully associative cache circuitry
Hardware complexity:
  How many comparators?
  How big is each comparator?

## Slide 60: Cache organizations
Fully associative cache 
  Too much hardware complexity
  Most flexible
Direct mapped cache 
  Least hardware complexity
  Least flexible
Can we do better? Is there a compromise?
Yes! It's called a set-associative cache
Turns out direct-mapped and fully-associative caches are degenerate cases of a set-associative cache!

## Slide 61: Generalization?
…
Direct Mapped
Fully Associative
n rows
…
1
2
3
4
n
Equivalent to n parallel caches
…
1
…
2
…
p
…
n / p rows
p parallel caches
Set Associative

## Slide 62
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
V
Tag
data
V
Tag
data
V
Tag
data
(a) Direct-mapped cache
(b) 2-way set associative
V
Tag
data
V
Tag
data
V
Tag
data
V
Tag
data
0
1
2
3
(c) 4-way set associative
Memory block in exactly one place
Memory block in one of two places
Memory block in one of four places

## Slide 63: Synonyms
Unfortunate but…
  Four different ways of saying the same thing
    Cache line
    Cache block
    Cache entry
    Cache element
  All mean the same thing…the basic unit of data transferred into/out of the cache at a time
  The textbook has a couple of typos in which it implies cache set is also a synonym; that’s wrong based on current usage as well as the text on 9-14 and 9-34!
A cache set is a “row” in the cache. The number of blocks per set is determined by the type of the cache
  Direct mapped: n sets, 1 element
  P-way set associative: n/p sets, p elements
  Fully associative: 1 set, n elements

## Slide 64
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
4
5
6
7
V
Tag
data
V
Tag
data
V
Tag
data
(a) Direct-mapped cache
(b) 2-way set associative
V
Tag
data
V
Tag
data
V
Tag
data
V
Tag
data
0
1
2
3
(c) 4-way set associative
16 sets
4 sets of 4 elements
8 sets of 2 elements

## Slide 66: Example: 4-way set associative cache
4-way set associative cache
32-bit memory, byte-addressable
Cache size of 64 Kbytes.
Each memory word contains 4 bytes
Cache block size is 16 bytes.
Write-through policy
One valid bit per block.
Compute the total amount of storage for implementing the cache (i.e. actual data plus the meta-data)
(1+18+128) * 1K * 4 / 8
= 75,264 bytes
tag
index
off set
…
v t data
…
v t data
…
v t data
…
v t data
18
10
4
64K/4/16 = 1k
1K
1
16*8 = 128
18
128
4
Hardware complexity?
4 18-bit comparators

## Slide 67: In a fully associative cache, …
…with 64K bytes of data, 64 bytes / block and a t-bit tag
There are four t-bit tag comparators
There are 64 t-bit tag comparators
There are 1k t-bit tag comparators
There is one t-bit tag comparator for the entire cache
70
FA caches have one comparator for each block/line/entry in the cache. That means 64K/64 = 1K is the number of comparators.
Today’s number is
11,111

## Slide 68: In a 4-way set associative cache, …
…with 64K bytes of data, 64 bytes / block, with a t-bit tag
There are four t-bit tag comparators
There are 64 t-bit tag comparators
There are 1k t-bit tag comparators
There is one t-bit tag comparator for the entire cache
80

## Slide 69: What about cache replacement policy?
0
1
2
3
4
5
6
7
V
Tag
data
V
Tag
data
LRU
C0
C1
What kind of cache is this?
How many LRU bits do we need?
What happens on every memory access
So what do we do with a 4-way set associative cache?
2-way set associative
Just one.
Set LRU to 0/1 if we read from/store in C0/C1

## Slide 70: LRU replacement in a 4-way cache
0
1
2
3
V
Tag
data
V
Tag
data
V
Tag
data
V
Tag
data
c1 -> c3 -> c0 -> c2
c0 -> c2 -> c1 -> c3
c2 -> c3 -> c0 -> c1
c3 -> c2 -> c1 -> c0
LRU
C0
C1
C2
C3
Do we need a state machine for each cache line?
Using as many state machines as the number of rows in the cache is a lot of hardware
Each state machine  4! States  5 bit state register

## Slide 71: What happens on a context switch?
TLB?
Cache?
Note: If the OS brings in a page from disk directly to a physical page frame and bypasses the cache, it must flush any cache locations for the previous contents. This isn’t a context switch issue, it’s an issue that if I/O bypasses the cache, then any cache entries referencing the I/O buffer are definitely invalid.
Flush user portion
Nothing! We’re using physical addresses
One
caveat

## Slide 72: On a process context switch
The cache entries for the process being suspended are flushed.
The cache and TLB entries for the process being suspended are flushed
The TLB entries for the process being suspended are flushed
None of the above
What does bathroom plumbing have to do with computer science?
Today’s number is 11,111
90

## Slide 73: When a page is evicted from a page frame in memory
The cache entries for the evicted page are flushed.
The cache and TLB entries for the evicted page are flushed
The TLB entries for the evicted page are flushed
None of the above
Still fixated on bathroom plumbing, huh?
100
The caches we’ve studied so far hold physical addresses (address translation has already occurred before the cache gets involved), then no flush is needed on page replacement. If the cache holds virtual addresses, then flushing cache entries from the page is required.

## Slide 74: Putting cache and VM together
CPU
TLB
Memory
Cache
Disk
Instr/
Data
PA
VA
Page
fault
VPN
Page offset
PFN
Page offset
Tag
Index
Block offset
Policy in Hardware
Policy in OS
TLB miss
cachemiss

## Slide 75: Adding some speed
CPU
TLB
Memory
Cache
Disk
Instr/
Data
PA
VA
Page
fault
VPN
Page offset
PFN
Page offset
Tag
Index
Block offset
Policy in Hardware
Policy in OS
cachemiss
TLB miss PA (VPN)
We can have the TLB try cache first

## Slide 76: Putting cache and TLB together
TLB
VA
Cache
PA
Instruction or
Data
CPU
TLB access is in the critical path of cache access  increased clock cycle time
Can we remove TLB from the critical path?

## Slide 77: Recall how TLB and Cache work together
CPU
TLB
Cache
PA
VA
VPN
Page offset
PFN
Page offset
Tag
Index
Block offset

## Slide 78: Recall
CPU
TLB
Cache
PA
VA
VPN
Page offset
PFN
Page offset
Tag
Index
Block offset
These are the same
Tag
=?
Hit

## Slide 79: Make the cache index the same size as the page offset?
CPU
TLB
Cache
PA
VA
VPN
Page offset
PFN
Page offset
Tag
Index
Block offset
Index
Block offset
These are the same
What if we arrange to make the Index + Block offset the same width as Page offset?
Then we can get the cache index from the VA to start the cache read without waiting for the TLB!
Tag
=?
Hit

## Slide 80: Now Index is the same for VA and PA!
CPU
TLB
Cache
PA
VA
VPN
Page offset
PFN
Page offset
Tag
Index
Block offset
What if we arrange to make the Index + Block offset the same width as Page offset?
Then we can get the cache index from the VA to start the cache read without waiting for the TLB!
Index
Block offset
These are the same
Tag
=?
Hit
These are the same

## Slide 81: Cache and TLB can start in parallel!
CPU
TLB
Cache
PA
VA
VPN
Page offset
PFN
Page offset
Tag
Index
Block offset
What if we arrange to make the Index + Block offset the same width as Page offset?
Then we can get the cache index from the VA to start the cache read without waiting for the TLB!
Index
Block offset
These are the same
Tag
=?
Hit
These are the same

## Slide 82: Virtually indexed physically tagged cache
Page offset
VPN
TLB
Cache
=?
PFN
Tag
Data
Hit
Index
Virtual
Physical
How to get TLB out of the critical path
TLB & cache access in parallel

## Slide 83: In a virtually indexed physically tagged cache
The TLB and cache are accessed in parallel
The TLB and cache are accessed sequentially
The TLB and cache are accessed at random
None of the above
110

## Slide 84: Is there a limitation?
Page offset
VPN
TLB
Cache
=?
PFN
Tag
Data
Hit
Index
Determines the max size of cache

## Slide 85: Page coloring example
VPN/PFN 19 bits
Page Offset 13 bits
Tag 15 bits
Offset
6 bits
Index 11 bits
These 4 bits must remain unchanged through VPN to PFN translation
Work out Example 10 on your own and
check the solution
OS guarantees some bits of VPN will remain unchanged
Bigger index  Larger cache

## Slide 86: Page coloring impacts
Require the low bits of the VPN and PFN to be identical (4 low order bits in this example)
  This allows the use of these bits as part of either the virtual or physical address, just like we use the offset
What does that impact?
  A virtual page can only occupy a subset of page frames in which the low bits of the VPN match the low bits of the PFN.
  We refer to this as page coloring which means the page replacement algorithm must keep track of the “color” of the VPNs and PFNs (namely those low bits) to ensure virtual pages are only loaded into like-colored page frames.
  It could make it harder to fit a working set into physical memory, but it’s often workable because processes tend to use contiguous pages so the VPNs of the pages are spread evenly among the colors
  In this example using the low 4 bits of the VPN/PFN, we get 16 different “colors” of page/page frame. So a page with a VPN ending in 00102 can only be placed in a page frame with a number that ends in 00102

## Slide 87: Simple memory system
CPU
Main memory
(32 bits wide)
Address
Address (32 bits)
Data (32 bits)
Data
DRAM & bus access time per word: 78ns
Access time for 4 words: ~300ns
Cache
(128 bits blocks)

## Slide 88: Memory system matching cache blocksize
CPU
Cache
(128 bits blocks)
Main memory
(128 bits wide)
Address
Address (32 bits)
Data (128 bits)
Data
DRAM & bus access time per block: 78ns
Access time for 4 words: 78ns
Downside: 128 bit busses

## Slide 89: Interleaved memory
CPU
Memory Bank M0
(32 bits wide)
Block
Address
Memory Bank M1
(32 bits wide)
Memory Bank M2
(32 bits wide)
Memory Bank M3
(32 bits wide)
Data
(32 bits)
(32 bits)
Cache
All banks receive an address in one mem cycle
Each bank transfers in successive memory cycles
Transfer time << memory access time

## Slide 90: Example
4-way interleaved memory
DRAM access time: 70 cycles.
Memory bus cycle time: 5 cycles
Compute the block transfer time for a block size of 4 words. Assume all 4 words are first retrieved from the DRAM before the data transfer to the CPU.

## Slide 91: Example solution sketch
Start memory fetches at 0, 5, 10, 15ns
Bank 4 memory fetch finishes at 85ns
Data transfers to CPU/cache occur at 70, 75, 80, 85ns
0 10 20 30 40 50 60 70 80 90 100
Bank 3
Bank 4
Bank 1
Bank 2

## Slide 92: Interleaved memory is useful because
It increases the cache block size
It reduces the cache block size
It allows concurrent fetches of data blocks from memory without requiring wider busses
It decreases the size of the cache index
120

## Slide 93
Two-cycle addressing using the same 15 addressing pins:
Present row address and RAS’
Present column address and CAS’

## Slide 94: Relative sizes & latencies, ca. 2009
Type of Memory | Typical Size | Approximate latency in CPU clock cycles to read one word of 4 bytes
CPU registers | 8 to 32 | Usually immediate access (0-1 clock cycles)
L1 Cache | 32 (Kilobyte) KB to 128 KB | 3 clock cycles
L2 Cache | 128 KB to 4 Megabyte (MB) | 10 clock cycles
Main (Physical) Memory | 256 MB to 4 Gigabyte (GB) | 100 clock cycles
Virtual Memory (on disk) | 1 GB to 1 Terabyte (TB) | 106 to 107 clock cycles (not accounting for the software overhead of handling page faults)

## Slide 95: Relative sizes & latencies, ca. 2022
Type of Memory | Typical Size | Approximate latency in CPU clock cycles to read one word of 4 bytes
CPU registers | 8 to 32 | Usually immediate access (0-1 clock cycles)
L1 Cache | 32 KB to 4MB | 1-3 clock cycles
L2 Cache | 32 KB to 32 MB | ~10 clock cycles
L3 Cache | 1 MB to 768 MB | ~30 clock cycles
Main (Physical) Memory | 256 MB to 8 TB | ~100 clock cycles
Virtual Memory (on disk) | 1 GB to 8 TB? | 106 to 107 clock cycles (not including the software overhead of handling page faults)

## Slide 96: Summary of Chapter 9 terminology
Category | Vocabulary | Details
Principle of locality (Section 9.2) | Spatial | Access to contiguous memory locations
 | Temporal | Reuse of memory locations already accessed
Cache organization | Direct-mapped | One-to-one mapping (Section 9.6)
 | Fully associative | One-to-any mapping (Section 9.12.1)
 | Set associative | One-to-many mapping (Section 9.12.2)
Cache reading/writing (Section 9.8) | Read hit/Write hit | Memory location being accessed by the CPU is present in the cache
 | Read miss/Write miss | Memory location being accessed by the CPU is not present in the cache
Cache write policy (Section 9.8) | Write through | CPU writes to cache and memory
 | Write back | CPU only writes to cache; memory updated on replacement
Cache parameters | Total cache size (S) | Total data size of cache in bytes
 | Block Size (B) | Size of contiguous data in one data block
 | Degree of associativity (p) | Number of homes a given memory block can reside in a cache
 | Number of cache lines (L) | S/pB
 | Cache access time | Time in CPU clock cycles to check hit/miss in cache
 | Unit of CPU access | Size of data exchange between CPU and cache
 | Unit of memory transfer | Size of data exchange between cache and memory
 | Miss penalty | Time in CPU clock cycles to handle a cache miss
Memory address interpretation | Index (n) | log2L bits, used to look up a particular cache line
 | Block offset (b) | log2B bits, used to select a specific byte within a block
 | Tag (t) | a – (n+b) bits, where a is number of bits in memory address; used for matching with tag stored in the cache

## Slide 97: Summary of Chapter 9 terminology
Category | Vocabulary | Details
Cache entry/cache block/cache line | Valid bit | Signifies data block is valid
 | Dirty bits | For write-back, signifies if the data block is more up to date than memory
 | Tag | Used for tag matching with memory address for hit/miss
 | Data | Actual data block
Performance metrics | Hit rate (h) | Percentage of CPU accesses served from the cache
 | Miss rate (m) | 1 – h
 | Avg. Memory stall | Misses-per-instructionAvg * miss-penaltyAvg
 | Effective memory access time (EMATi) at level i | EMATi = Ti + mi * EMATi+1
 | Effective CPI | CPIAvg + Memory-stallsAvg
Types of misses | Compulsory miss | Memory location accessed for the first time by CPU
 | Conflict miss | Miss incurred due to limited associativity even though the cache is not full
 | Capacity miss | Miss incurred when the cache is full
Replacement policy | FIFO | First in first out
 | LRU | Least recently used
Memory technologies | SRAM | Static RAM with each bit realized using a flip flop
 | DRAM | Dynamic RAM with each bit realized using a capacitive charge
Main memory | DRAM access time | DRAM read access time
 | DRAM cycle time | DRAM read and refresh time
 | Bus cycle time | Data transfer time between CPU and memory
 | Simulated interleaving using DRAM | Using page mode bits of DRAM