## Slide 1: Performance and Pipelines
CS 2200 Summer 2023

## Slide 2: Metrics
If we’re going to try to make processors better, we’re going to have to take measurements
Common Metrics:
Space  memory footprint
Time  execution time
Instruction frequency
  Static
  Dynamic
Benchmarks

## Slide 3: What determines execution time?
We’ll use the abbreviation CPI for ”Cycles Per Instruction” so we can talk about the number of clock cycles each instruction takes.
Execution time = (∑ CPIj) * clock cycle time, where 1 ≤ j ≤ n
That’s a pretty tough sum to compute because modern computers can execute billions of instructions per second
Execution time = n * CPIAvg * clock cycle time, where n is the number of instructions (executed not static instruction count)

## Slide 4
What’s the execution time?
1 GHz processor; 10K instructions; CPIAvg = 3
3 msec
1 GHz
0.03 msec
300 µsec
30K
10
Not enough information to compute
10
10-9 sec/cy
104 inst
3 cy/inst
= 3 x 10-5 sec
= .00003 sec
= .03 msec
= 30 µsec
Today’s Number 30,030

## Slide 5: Instruction Frequency
Static instruction frequency refers to number of times a particular instruction occurs in compiled code.
  Impacts memory footprint
  If a particular instruction appears a lot in a program, can try to optimize amount of space it occupies by clever instruction encoding techniques in the instruction format.
Dynamic instruction frequency refers to number of times a particular instruction is executed when program is run.
  Impacts execution time of program
  If dynamic frequency of an instruction is high then can try to make enhancements to datapath and control to ensure that CPI taken for its execution is minimized.

## Slide 6
Static instruction frequency…
Refers to the type of instruction in the instruction-set
Refers to the frequency of occurrence of instructions in compiled code
Refers to the frequency of occurrence of instructions that actually get executed
Refers to the clock frequency of the processor
Is the basis for datapath design
20

## Slide 7
Dynamic instruction frequency…
Refers to the type of instruction in the instruction-set
Refers to the frequency of occurrence of instructions in compiled code
Refers to the frequency of occurrence of instructions that actually get executed
Refers to the clock frequency of the processor
Is the basis for datapath design
30

## Slide 8
ADD instruction occurs twice in a program that contains a total of 1000 instructions in the compiled code. All 1000 instructions get executed during a program run. One of the ADD instructions is in a 5-instruction loop that gets executed 1000 times.
What is the static frequency of ADD?
Two
0.2%
(1000/5995) * 100%
(1001/5995) * 100%
(1/5000) * 100%
(1001/5000) * 100%
40

## Slide 9
ADD instruction occurs twice in a program that contains a total of 1000 instructions in the compiled code. All 1000 instructions get executed during a program run. One of the ADD instructions is in a 5-instruction loop that gets executed 1000 times.
What is the dynamic frequency of ADD?
Two
0.2%
(1000/5995) * 100%
(1001/5995) * 100%
(1/5000) * 100%
(1001/5000) * 100%
50
ADDs executed:
1 + 1000 = 1001
Total executed:
1000 inst – 5 inst
+ 1000 * 5 = 5995

## Slide 10: Benchmarks
Benchmarks are a set of programs that are representative of the workload for a processor.
The key difficulty is to be sure that the benchmark program selected really are representative of the prospective workload.
Standard benchmark suites (SPEC, LINPACK, Whetstone, Dhrystone, and many more) are used to try to compare “apples” with “apples” by summarizing performance across a set of programs
  E.g. SPEC uses perl, gcc, AI apps, compression, imaging apps, modeling apps, etc. to represent a common workload
A radical new design is hard to benchmark because there may not yet be a compiler or much code.

## Slide 11: Composite execution times
Total execution time: This metric is the cumulative total of the execution times of the individual programs
Arithmetic mean: This metric may bias the summary value towards a time-consuming benchmark program (e.g. P1 = 100; P2 = 1; AM = 50.5).
Geometric mean: This metric removes the bias present in arithmetic mean (e.g. P1 = 100; P2 = 1; GM = sqrt(100*1) = 10).
Weighted arithmetic mean: This metric takes into account the relative frequency of execution of the programs in the benchmark mix (e.g. P1 = 100; P2 = 1; fP1 = 0.1; fP2 = 0.9; WAM = 10.9).
Harmonic mean (HM): It is computed by taking the arithmetic mean of the reciprocals (e.g. P1 = 100; P2 = 1; HM = 1/( ( (1/100) + (1/1) )/2 ) = 1.9801)
Bias to high
Bias to low
In the middle

## Slide 12: Summary of metrics
Name | Notation | Units | Comment
Memory footprint | - | Bytes | Total space occupied by the program in memory
Execution time | (∑ CPIj) * clock cycle time, where 1 ≤ j ≤ n | Seconds | Running time of the program that executes n instructions
Arithmetic mean | (E1+E2+…+Ep)/p | Seconds | Average of execution times of constituent p benchmark programs
Weighted Arithmetic mean | (f1*E1+f2*E2+…+fp*Ep) | Seconds | Weighted average of execution times of constituent p benchmark programs
Geometric mean | pth root (E1*E2* …*Ep) | Seconds | pth root of the product of execution times of p programs that constitute the benchmark
Static instruction frequency |  | % | Occurrence of instruction i in compiled code
Dynamic instruction frequency |  | % | Occurrence of instruction i in executed code
Speedup (MA over MB) | EB/EA | Number | Speedup of Machine A over B
Speedup (improvement) | EBefore/EAfter | Number | Speedup After improvement
Improvement in Exec time | (Eold-Enew)/Eold | Number | New Vs. old
Amdahl’s law | Timeafter = Timeunaffected + Timeaffected/x | Seconds | x is amount of improvement

## Slide 13: Using a benchmark
Some caveats:
  Based on the biases of composite functions, we have to be very cautious using a single composite metric
  Processor performance isn’t determined just by the clock cycle rating of the processor – memory organization and memory—processor—bus bandwidths are also key
  Some processors do well on certain benchmark programs and other do well on other programs
  A composite index can be useful when we want to compare two processors without knowing the exact kind of workload they are going to run, but
  We must be very cautious about the over use of metrics
  Don’t forget the cliché “Lies, damned lies, and statistics”

## Slide 14: Reasons to be skeptical of a benchmark
The vendor gave you the benchmark results (in polite company, we call this a conflict of interest)
The vendor wrote the benchmark suite
The benchmark suite doesn’t seem to have any elements that represent your workload (e.g. you run web server farms and the benchmark represents only computationally intensive scientific calculations)
The equipment being benchmarked is different from the equipment you want to evaluate (maybe a little different, maybe a lot different)
The benchmark uses a different compiler suite than you plan to use
The cost of mistakenly choosing the wrong equipment is very high

## Slide 15
In creating a composite performance metric, using an arithmetic mean
Reduces biases included in the geometric mean
May bias the summary towards time-consuming programs in the benchmark
Yields a cumulative total of the execution times of the individual programs
Takes into account the relative frequency of the execution of the programs in the benchmark
60

## Slide 16: Using SPEC CPU benchmarks
There’s a 2017 version now available
SPEC actually publishes four composite metrics: SPECspeed_int, SPECspeed_fp, SPECrate_int, and SPECrate_fp
We’re going to look at SPECrate_int which measures mostly multi-threaded integer performance (e.g. those of interest for a software development server).
Let’s take a look. Note how much more information is presented than just a simple composite number. This is a hint about how many variables they’re trying to control, nearly an impossible task.

## Slide 17: Comparing two real systems
 | Intel Platinum 8490H | AMD EPYC 9654
Clock | 1.9 GHz (up to 3.5GHz) | 2.4 GHz (up to 3.7GHz)
Cores (cpus) | 120 | 192
System | HPE DL380 (2 chips) | HPE DL365 (2 chips)
SPECrate2017_int | 948 | 1620
CPU Cost (9/2021) | $17,000 (list) | $11,805 (list)
So which one would you recommend? Both are similar HPE server chassis: DL380 or DL365

## Slide 18: The need for speed!
So how do we improve performance?
Reduce execution time (of course)
How?
The execution time equation tells us:
Execution time = N * CPI * Cycle Time
How can we reduce the left-hand side?
Reduce one or more of the right-hand factors

## Slide 19: How can we measure improvement?

## Slide 20
It takes me 8 minutes to walk to class from my office. I can run twice as fast as I walk. If I walk half the distance and run the remaining half, how much time will I take to reach class from my office?
8 mins
4 mins
6 mins
2 mins
How does this relate to CS 2200?
Today’s number is 19,654
70
8 = d/v n = ½ d/v + ½ d/2v
8v = d
n = 4v/v + 4v/2v
n = 4 + 2
n = 6

## Slide 21: Amdahl’s Law
My office walk: 6 = 4 * 1/2 + 4
This is perhaps a little easier way to think about these problems

## Slide 22: Improving an instruction
A processor spends 20% of its time on ADD instructions. An engineer proposes to improve the speed of the ADD instruction by 4 times. What is the speedup achieved by this modification?
The improvement only applies for the ADD instruction, so 80% of the execution time is unaffected by the improvement.
Time = .2 / 4 + .8 = 0.85
Speedup = 1 / .85 = 1.18 (or 18% improvement)

## Slide 23
A processor spends 10% of its time on ADD instructions. An engineer proposes to improve the speed of the ADD instruction by 3 times. What is the speedup achieved by this modification?
62%
15%
18%
7%
80
Original normalized execution time = 1
New execution time = (time spent in ADD/4)
+ remaining time
= 0.1 / 3 + .9
= 0.933
Speedup = execution time before
/execution time after
= 1 / 0.933 = 1.07 = 7%
Today’s number is 71,771

## Slide 24: Summary of metrics
Name | Notation | Units | Comment
Memory footprint | - | Bytes | Total space occupied by the program in memory
Execution time | (∑ CPIj) * clock cycle time, where 1 ≤ j ≤ n | Seconds | Running time of the program that executes n instructions
Arithmetic mean | (E1+E2+…+Ep)/p | Seconds | Average of execution times of constituent p benchmark programs
Weighted Arithmetic mean | (f1*E1+f2*E2+…+fp*Ep) | Seconds | Weighted average of execution times of constituent p benchmark programs
Geometric mean | pth root (E1*E2* …*Ep) | Seconds | pth root of the product of execution times of p programs that constitute the benchmark
Static instruction frequency |  | % | Occurrence of instruction i in compiled code
Dynamic instruction frequency |  | % | Occurrence of instruction i in executed code
Speedup (MA over MB) | EB/EA | Number | Speedup of Machine A over B
Speedup (improvement) | EBefore/EAfter | Number | Speedup After improvement
Improvement in Exec time | (Eold-Enew)/Eold | Number | New Vs. old
Amdahl’s law | Timeafter = Timeunaffected + Timeaffected/x | Seconds | x is amount of improvement

## Slide 25
Execution time?
Code 1 is better than Code 2 since it has fewer instructions
Code 2 is better than Code 1 since it has fewer instructions
Code 1 is better than Code 2 since it takes fewer total clock cycles to execute
Code 2 is better than Code 1 since it takes fewer total clock cycles to execute
I cannot count
90
CPI of Instruction Classes | Code 1 Uses | Code 2 Uses
R-type = 2 | 3 | 10
I-type = 10 | 3 | 1
J-type = 3 | 5 | 2
S-type = 4 | 2 | 3
13 inst
6+30 +15+8 =
59 cycles
16 inst
20+10+6+12 =
48 cycles

## Slide 26: Architecture change?
We have a computer with three types of instructions that have the following CPI:
An architect determines that he can reduce the CPI for B to 3 but will need to slow the clock speed of the processor. What is the maximum permissible slowing of the clock that will make this change worthwhile.
Assume that all the workloads for this processor use 30% of A, 10% of B, and 60% of C types of instructions
Type | CPI
A | 2
B | 5
C | 1

## Slide 27: How do we answer that?
Execution time of the old machine:
ETo = N * (FAo * CPIAo + FB * CPIBo + FC * CPICo) * Co
(where Fx and CPIx are the dynamic frequencies and CPIs of each type of instruction, respectively)
ETo = N * (0.3 * 2 + 0.1 * 5 + 0.6 * 1) * Co = N * 1.7 * Co
Execution time for the new machine:
ETn = N * (0.3 * 2 + 0.1 * 3 + 0.6 * 1) * Cn = N * 1.5 * Cn
For the design to be viable,
ETn < ETo
N * 1.5 * Cn < N * 1.7 * Co
Cn < 1.7/1.5 * Co
Cn < 1.13 * Co
Maximum permissible increase in clock cycle time = 13%

## Slide 28: Combining two instructions?
Instruction | CPI
Add | 2
Shift | 3
Others | 2
Add/Shift | 4
If the sequence ADD followed by SHIFT appears in 20% of the dynamic frequency of a program, what is the speedup of the program with all {ADD, SHIFT} replaced by the combined instruction?
[HINT: For every 10 instructions in the original program, 2 instructions are the ADD/SHIFT combo. Thus the number of instructions in the new program shrinks to 90% of the original program.]

## Slide 29: A solution
ETo = N * (FADD * 2 + FSHIFT * 3 + Fothers * 2) * C = N * (0.1 * 2 + 0.1 * 3 + 0.8 * 2) * C = 2.1NC
With the combo instruction replacing {ADD SHIFT}, the number of instructions in the new program shrinks to 0.9N in the new program. The frequency of the combo instruction is 1/9 and the other instructions are 8/9.
ETn = (0.9 * N) * (FCOMBO * 4 + Fothers * 2) * C = (0.9* N ) * (1 / 9 * 4 + 8 / 9 * 2) * C = 2NC
Speedup = old execution time / new execution time = 2.1NC / 2NC = 1.05
Note: textbook example 5.5 on p. 168 has an error. Above is the corrected solution

## Slide 30
You improve your application’s algorithm so that it runs in 29 seconds instead of 38 seconds. What is the improvement in execution time?
24%
31%
131%
124%
100
Improvement in Execution time
(Eold-Enew)/Eold
(38 – 29) / 38 = .2368…
= 24%
38 – (24% of 38) ~= 29

## Slide 31
You improve your application’s algorithm so that it runs in 29 seconds instead of 38 seconds. What is the Speedup?
24%
31%
131%
124%
110
Speedup (improvement)
EBefore/EAfter
38 / 29 = 1.3103
= 31% speedup
29 * 1.31 ~= 38

## Slide 32: Don’t forget these metrics
Space  memory footprint
Time  execution time
Instruction frequency
  Static
  Dynamic
Benchmarks

## Slide 33: Pipelining

## Slide 34: Going faster…
Latency vs Throughput
CPI
IPC
Pathway to pipelined processor design

## Slide 35: Bill's Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)

## Slide 36: Bill's Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)

## Slide 37: Bill's Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)

## Slide 38: Bill's Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)

## Slide 39: Bill's Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)

## Slide 40: Bill's Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
Net result: One complete sandwich every five cycles.

## Slide 41: Bill's Mega-Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order
"What'll Ya Have?"
Manager
Net result: One complete sandwich every cycle! (Once you fill the pipeline.)
A 5x speedup!

## Slide 42: Interpreting an instruction
Fetch
Decode
Execute
Instruction
in
Instruction
out
I1

## Slide 43: Interpreting an instruction
Fetch
Decode
Execute
Instruction
in
Instruction
out
I1

## Slide 44: Interpreting an instruction
Fetch
Decode
Execute
Instruction
in
Instruction
out
I1

## Slide 45: Interpreting an instruction
Fetch
Decode
Execute
Instruction
in
Instruction
out
I2

## Slide 46: Interpreting an instruction
Fetch
Decode
Execute
Instruction
in
Instruction
out
I2

## Slide 47: Interpreting an instruction
Fetch
Decode
Execute
Instruction
in
Instruction
out
I2

## Slide 48: One at a time…
F
instructions
I4
D
E
F
I3
D
E
F
I2
D
E
F
I1
D
E
I5
.
.
.
.
………….
……….
1 2 3 4 5 6 7 8 9 ………………….
time
Waterfall

## Slide 49: Three at a time?
Fetch
Decode
Execute
Instruction
in
Instruction
out
I1
I2
I3

## Slide 50: Overlapping execution
F
instructions
time
I4
D
E
F
I3
D
E
F
I2
D
E
F
I1
D
E
I5
.
.
.
.
………………….
………………….
1 2 3 4 5 6 7 8 9 ………………….
Waterfall

## Slide 51: What do we need in the datapath?
Fetch
Decode
Execute
Instruction
in
Instruction
out
I1
I2
I3

## Slide 52
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
1024x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
WrREG
IR
LdIR
Z
LdZ
=0?
Z: 1
-
bit
boolean
to control logic
OP: 4
-
bit
opcode
to control logic
10
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
Rz: 4
-
bit register number to control logic
Ry: 4
-
bit register number to control logic
Rx: 4
-
bit register number to control logic
IR[31..28]
IR[3..0]
IR[23..20]
IR[27..24]
1
1
LC
-
2200 Datapath

## Slide 53: What units are used?
Macro State Units in Use
FETCH IR, ALU, PC, MEM
DECODE IR
EXECUTE (ADD) IR, ALU, Reg-file
EXECUTE (LW) IR, ALU, Reg-file MEM, Sign extender
Good News on the register file:
Only writing is exclusive
Reading can be done by any simultaneously

## Slide 54: Imitation: The Sincerest Form of Flattery
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order
Points to note:
Work done by each station is roughly equal
Every sandwich goes through every station, regardless of what you want or don’t want
Order form and partially assembled sandwich is passed from one station to the next
Each station does part of the work for assembling a sandwich

## Slide 55: How do we mimic sandwich assembly?
Unequal division of labor
Violates first principle in sandwich assembly line
Fetch
Decode
Execute

## Slide 56: Bill's Cost-Cutting Measure
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order

## Slide 57: Bill's Cost-Cutting Measure
Station 1 station II station III
(place order) (select bread) (cheese, meat, veggies)
3rd order 2nd order 1st order
Disaster!
  Station III needs 3 cycles to do its job!
  Thus, one sandwich every 3 cycles, not one every cycle!
  Increased waiting times!
  Two workers who only work about a third of the time

## Slide 58: Bill's Mega-Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order

## Slide 59
Bill used 5 stages rather than 3 in his sandwich pipeline because…
He copied the instruction pipeline
He could only find 5 workers
He is solving the unemployment problem
He wants to make sure that the amount of work done by each station is roughly the same
He is a nice guy
You are making us hungry…
120

## Slide 60: How do we mimic sandwich assembly?
Get to the basics!
What needs to happen for every instruction?
  Fetch into IR and increment PC
  Decode instruction and read register contents
  Perform arithmetic/logic (maybe)
  Perform address computation (maybe)
  Fetch/store memory operand (maybe)
  Write to register (maybe)
Fetch
Decode
Execute
1
2
3
4
5
Each step is roughly the same amount of work

## Slide 61: How can we know what registers to read?
What does the “bread guy” care about?
How does the “bread guy” know what bread?
It’s the order form!
What’s the equivalent of the order form in the instruction pipeline
IR
 This is where symmetry of instruction format becomes important!

## Slide 62: LC-2200 Instruction set
R-type instructions (add, nand):
bits 31-28: opcode
bits 27-24: reg X; bits 23-20: reg Y
bits 19-4: unused (should be all 0s); bits 3-0: reg Z
I-type instructions (addi, lw, sw, beq):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: Imm. Offset
J-type instructions (jalr):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: unused
O-type instructions (halt):
bits 31-28: opcode; bits 27-0: unused

## Slide 63: Every instruction goes through
IF
ID/RR
EX
MEM
WB
Instruction
in
Instruction
out
I4
I3
I2
I1
I5
Some stages don’t do anything for some instructions
Each stage works on a different instruction
IF - fetch instruction into IR and increment PC
ID/RR - decode and read register contents
EX - perform arithmetic/logic (maybe)
- perform address computation (maybe)
MEM - fetch/store memory operand (maybe)
WB - write to register (maybe)

## Slide 64: How do we electrically isolate each stage?
IF
ID/RR
EX
MEM
WB
Instruction
in
Instruction
out
I4
I3
I2
I1
I5
Think of our sandwich assembly line
Each station passes two things to the next
  The order form
  A partially assembled sandwich
What’s analogous in our data path
  Is the IR equivalent to the order form?
  What is a “partially assembled data sandwich”?

## Slide 65: Electrical isolation between stages
Registers act as a wall to isolate the actions of each combinational logic cloud!
On each clock tick, the registers send their output to drive the next stage of combinational logic
register
register
register
register
Combo logic
Combo logic
Combo logic
Combo logic
Clock

## Slide 66: What’s in these pipeline boxes?
IF
ID/RR
EX
MEM
WB
Instruction
in
Instruction
out
How do we separate our pipeline boxes?
The boxes are really just combinational logic clouds
So we already know how to separate them…
IF
ID/RR
EX
MEM
WB

## Slide 67: This is where buffers come from…
There is combinational logic in each cloud for performing the actions of that stage
The buffers are merely clocked registers for passing the partially assembled results
Instruction
in
Instruction
out
IF
ID/RR
EX
MEM
WB
BUFFER
BUFFER
BUFFER
BUFFER

## Slide 68: Again: What does each stage do?
IF - fetch instruction into IR and increment PC
ID/RR - read register contents
EX - perform arithmetic/logic (maybe)
- perform address computation (maybe)
MEM - fetch/store memory operand (maybe)
WB - write to register (maybe)
Instruction
in
Instruction
out
IF
ID/RR
EX
MEM
WB
BUFFER
BUFFER
BUFFER
BUFFER

## Slide 69: Again: What does each stage need?
Conclusion: we need a little datapath in each stage
Instruction
in
Instruction
out
IF
ID/RR
EX
MEM
WB
BUFFER
BUFFER
BUFFER
BUFFER
STAGE Units in Use
FETCH ALU, PC, MEM
ID/RR Reg-file, decode logic
EXEC ALU
MEM MEM
WB Reg-file

## Slide 70: A shiny new data path!
PC
I-MEM
ALU
DPRF
ALU
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
STAGE Units in Use
FETCH ALU, PC, MEM
ID/RR Reg-file, decode logic
EXEC ALU
MEM MEM
WB Reg-file

## Slide 71: Two register files? Not.
PC
I-MEM
ALU
DPRF
ALU
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
We use a register file in two stages

## Slide 72: Do you remember this device?
Input
A Output
A Address
.
.
.
0
1
2
13
14
15
B Output
B Address
Clock
Dest Address
Write

## Slide 73: Two register files? Not.
PC
I-MEM
ALU
DPRF
ALU
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
We use a register file in two stages, but conveniently
  ID/RR uses read parts (A addr, B addr B, A output, B output)
  WB uses write parts (Dest addr, Input)
So we can happily share the same register file on each clock cycle

## Slide 74: Example of sharing the register file
PC
I-MEM
ALU
DPRF
ALU
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
I1: ADD R1, R2, R3 R1  R2 + R3
I4: ADD R5, R6, R7 R5  R6 + R7
I5
I4
I3
I2
I1

## Slide 75: But what about those buffers?
PC
I-MEM
ALU
DPRF
ALU
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
What goes in those buffers? Same? Different?
The different stages seem to need different information
What was that sandwich analogy?

## Slide 76
Comparing the instruction pipeline to Bill’s sandwich pipeline, the buffers between stages serve the same function as
A partially assembled sandwich
Order form passed between stations
Combination of the above two
No comparison
What is a buffer?
You’re making us hungry again…
130
Today’s number is 30,332

## Slide 77: So what makes up our partially assembled data sandwich?
PC
I-MEM
ALU
DPRF
ALU
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
The IR (or parts thereof) is the order form
The data sandwich is the partial execution results
Do the buffers have to all carry the same information? Or can they be different?
FBUF
DBUF
EBUF
MBUF

## Slide 78: What does each stage need in the buffers?
PC
I-MEM
ALU
DPRF
ALU
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
Name | Output of Stage | Contents
FBUF | IF | Primarily contains instruction read from memory
DBUF | ID/RR | Decoded IR and values read from register file
EBUF | EX | Primarily contains result of ALU operation plus other parts of the instruction depending on the instruction specifics
MBUF | MEM | Same as EBUF if instruction is not LW or SW; If instruction is LW, then buffer contains the contents of memory location read
FBUF
DBUF
EBUF
MBUF

## Slide 79: Our non-pipelined LC-2200
FETCH
DECODE
EXECUTE
Instruction
in
Instruction
out
I1
At each point, the processor is in exactly one macro state

## Slide 80
What “macro state” is a pipelined processor in at any point in time?
Fetch
Decode
Execute
All of the above
140

## Slide 81: Anatomy of an ADD instruction
IF stage (cycle 1)
ID/RR stage (cycle 2)
EX stage (cycle 3)
MEM stage (cycle 4)
WB stage (cycle 5)

## Slide 82: Actions for an ADD instruction
Stage | Actions | Comments
IF | MEM[PC]  FBUF.IR PC + 1  PC | Instruction is fetched from memory and placed in FBUF (which is essentially the IR)
ID/RR | DPRF[FBUF.IR.Ry]  DBUF.A DPRF[FBUF.IR.Rz]  DBUF.B FBUF.IR.Opcode  DBUF.Opcode FBUF.IR.Rx  DBUF.Rx | Read register Ry into DBUF.A Read register Rz into DBUF.B Copy opcode from FBUF to DBUF Copy Rx from FBUF to DBUF
EX | DBUF.A + DBUF.B  EBUF.Result DBUF.OPCODE  EBUF.Opcode DBUF.Rx  EBUF.Rx | Perform addition Copy opcode from DBUF to EBUF Copy Rx from DBUF to EBUF
MEM | EBUF  MBUF | Copy EBUF to MBUF
WB | MBUF.Result  DPRF[MBUF.Rx] | Write the result of addition into register Rx

## Slide 83
Considering only the Add instruction,
quantify the sizes of the various buffers
between the stages of the above pipeline.
FBUF?
DBUF?
EBUF?
MBUF?

## Slide 84: How does this pipeline work for ADD?
IF | ID/RR | EX | MEM | WB
struct FBUF { struct IR { int Opcode:4; int Rx:4; int Ry:4; int junk:16; int Rz: 4; } IR } FBUF; | struct DBUF { int Opcode:4; int Rx:4; int A:32; int B:32; } DBUF; | struct EBUF { int Opcode:4; int Rx:4; int Result:32; } EBUF; | struct MBUF { int Opcode:4; int Rx:4; int Result:32; } MBUF;
MEM[PC]  FBUF.IR | Read registers | Addition | NOP | Write register
Mem

## Slide 85: How does this pipeline work for ADDI?
IF | ID/RR | EX | MEM | WB
struct FBUF { struct IR { int Opcode:4; int Rx:4; int Ry:4; int imm:20; } IR } FBUF; | struct DBUF { int Opcode:4; int Rx:4; int A:32; int imm:20; } DBUF; | struct EBUF { int Opcode:4; int Rx:4; int Result:32; } EBUF; | struct MBUF { int Opcode:4; int Rx:4; int Result:32; } MBUF;
MEM[PC]  FBUF.IR | Read registers | Addition | NOP | Write register
Mem

## Slide 86: How do you generalize design of pipeline buffers?
Look at each instruction in the ISA
Decide what needs to be carried over from one stage to the next
Opcode other fields

## Slide 87: Design the DBUF register for LC-2200
Don’t optimize by overloading the different fields of the register
Decide what fields need to be in DBUF for each instruction in the ISA
ADD/NAND | ADDI | BEQ | And so on…
struct DBUF { int Opcode:4; int Rx:4; int A:32; int B:32; } DBUF; | struct DBUF { int Opcode:4; int Rx:4; int A:32; int imm:20; } DBUF; | struct DBUF { int Opcode:4; int A:32; int B:32; int imm:20; int PC:32; } DBUF; | 

## Slide 88: Now take the UNION of the requirements
ADD/NAND | ADDI | BEQ | And so on…
struct DBUF { int Opcode:4; int Rx:4; int A:32; int B:32; } DBUF; | struct DBUF { int Opcode:4; int Rx:4; int A:32; int imm:20; } DBUF; | struct DBUF { int Opcode:4; int A:32; int B:32; int imm:20; int PC:32; } DBUF; | 
struct DBUF { int Opcode:4; int Rx:4; int A:32; int B:32; int imm:20; int PC:32; } DBUF;

## Slide 89: Now take the UNION of the requirements
In the ID/RR stage, fill in fields commensurate with the instruction in FBUF.IR
Leave unneeded fields unfilled
What fields would we fill in for JALR Rx, Ry # Ry  PC; PC  Rx
struct DBUF { int Opcode:4; int Rx:4; int A:32; int B:32; int imm:20; int PC:32; } DBUF;

## Slide 91
For the JALR instruction, what fields in DBUF are not filled in?
JALR Rx, Ry Ry  PC; PC  Rx
Rx specifier
Contents of PC
A (contents of Ry)
B (contents of Rx)
Immediate value
Both C and E
150
(FWIW, Ry is going to be needed in DBUF, but we could stick it in place of Rx, since it's going to be the register that's modified in WB; none of the other instructions modify their Ry)

## Slide 92
For the BEQ instruction, the fields in DBUF not filled in…
BEQ Rx, Ry, offset If (Rx == Ry) PC PC + offset
A (contents of Ry)
B (contents of Rx)
PC
Immediate value
Rx specifier
160

## Slide 93: Pipeline Hazards
Structural hazards
  Datapath/resource limitations
Data hazards
  Program limitations
Control hazards
  Program limitations

## Slide 94: Bill's Mega-Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order
"What'll Ya Have?"
And sometimes fries on the side
Stay on the same order!
Stay on the same order!
Customers behind
No work for one cycle
Customers ahead
Pipeline Stall

## Slide 95: Bill's Mega-Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order
"What'll Ya Have?"
And sometimes fries on the side
Pipeline resumed
No work for one cycle

## Slide 96
If the cheese person has to add fries to some orders, then the pipeline…
Continues to produce 1 sandwich per clock cycle
Produces more than 1 sandwich per clock cycle
Produces less than 1 sandwich per clock cycle
170

## Slide 97: Bill's Mega-Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order
"What'll Ya Have?"
And sometimes fries on the side
This is a structural hazard – not enough resources
The effect:
Introduces “bubbles” into the pipeline
Reduces efficiency

## Slide 98: Structural Hazard
IF
ID/RR
EX
MEM
WB
B
UF
F
E
R
B
UF
F
E
R
B
UF
F
E
R
B
UF
F
E
R
BEQ
I4
I2
I1
I0
Potentially need two arithmetic ops
  A – B (always needed)
  PC + offset (sometimes needed)
Where is this going to mean trouble?

## Slide 99: Structural Hazard
IF
ID/RR
EX
MEM
WB
B
UF
F
E
R
B
UF
F
E
R
B
UF
F
E
R
B
UF
F
E
R
BEQ
Feedback lines
Cycle 1
I4
I2
I1
I0

## Slide 100: If BEQ branches, we will need to use the ALU twice!
IF
ID/RR
EX
MEM
WB
BUF
F
ER
BUF
F
ER
BUF
F
ER
BUF
F
ER
BEQ
Feedback lines
Cycle 2
STAY
STAY
I5
I2
I1
I4
Tell the first two stages to wait

## Slide 101: Pipeline resumes with a bubble
IF
ID/RR
EX
MEM
WB
BUF
F
ER
BUF
F
ER
BUF
F
ER
BUF
F
ER
BEQ
Feedback lines
Cycle 3
I5
NOP
I2
I4
EX passed a bubble to MEM

## Slide 102: But life goes on
IF
ID/RR
EX
MEM
WB
BUF
F
ER
BUF
F
ER
BUF
F
ER
BUF
F
ER
I4
Feedback lines
Cycle 4
I6
BEQ
NOP
I5
EX passed a bubble to MEM

## Slide 103: Bill's Mega-Sandwich Shop
Station 1 station II station III station IV station V
(place order) (select bread) (cheese) (meat) (veggies)
New (5th order) 4th order 3rd order 2nd order 1st order
"What'll Ya Have?"
And sometimes fries on the side
Cheese guy
Fries guy
But we can also add more “hardware”!

## Slide 104: Throw hardware at it!
PC
I-MEM
ALU
DPRF
ALU-1
B
U
F
F
E
R
A
B
Decode
logic
B
U
F
F
E
R
ALU-2
D-MEM
B
U
F
F
E
R
DPRF
B
U
F
F
E
R
IF
ID/RR
EXEC
MEM
WB
data
So we add another ALU to the EX stage

## Slide 105
Pipeline structural hazards are caused by…
Branch instructions in the program
Load instructions in the program
Data dependencies in the program
Hardware limitations in the datapath
180

## Slide 106: Data Hazard
RAW
I1: R1 <- R2 + R3
I2: R4 <- R1 + R5
WAR
I1: R4 <- R1 + R5
I2: R1 <- R2 + R3
WAW
I1: R1 <- R4 + R5
I2: R1 <- R2 + R3
True dependency
Anti dependency
Output dependency

## Slide 107: Dealing with a RAW dependency
I1: R1 <- R2 + R3
I2: R4 <- R1 + R5
I2
I1
IF
ID/RR
EX
MEM
WB
IF
ID/RR
EX
MEM
WB
I2
I1
Cycle 1
Cycle 2
At this point, R1 hasn’t even been computed
If we don’t stall the pipeline here, the execution of I2 will result in a semantic inconsistency

## Slide 108: Fix – introduce bubbles
IF
ID/RR
EX
MEM
WB
We need some hardware help to know when to introduce bubbles
So we’re going to add a “busy” bit to the register file
ID/RR sets it and WB clears it
NOP
NOP
B
B
B
B
B
B
B
B
Register file
I1
I2

## Slide 109: RAW Hazard – Cycle 1
I1: R1 <- R2 + R3
I2: R4 <- R1 + R5
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I2
I1
Reg-file
R1 not ready to be read

## Slide 110: RAW Hazard – Cycle 2
I1: R1 <- R2 + R3
I2: R4 <- R1 + R5
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I2
NOP
Reg-file
R1 not ready to be read
I1

## Slide 111: RAW Hazard – Cycle 3
I1: R1 <- R2 + R3
I2: R4 <- R1 + R5
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I2
NOP
Reg-file
R1 not ready to be read
I1
NOP

## Slide 112: RAW Hazard – Cycle 4
I1: R1 <- R2 + R3
I2: R4 <- R1 + R5
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I2
NOP
Reg-file
R1 is ready to be read
NOP
NOP
Needed three bubbles total

## Slide 113: A question…
I1: R1 <- R2 + R3
I2: R4 <- R4 + R3
I3: R5 <- R5 + R3
I4: R6 <- R1 + R6
IF
ID/RR
EX
MEM
WB
I1
Say we insert 2 instructions between “definition” and “use” of a register
Does this help to reduce “bubbles”?

## Slide 114
With 2 instruction separation between “definition” and “use,” we will…
Continue to have 3 bubbles in the pipeline
Reduce the number of bubbles to 0
Reduce the number of bubbles to 1
Reduce the number of bubbles to 2
190

## Slide 115: Two instruction separation
I1: R1 <- R2 + R3
I2: R4 <- R4 + R3
I3: R5 <- R5 + R3
I4: R6 <- R1 + R6
IF
ID/RR
EX
MEM
WB
I1
We can restructure the program to reduce “bubbles”
This is something we expect modern compilers to be able to do for us.

## Slide 116: Waterfall Diagram
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | I1 | - | - | - | -
2 | I2 | I1 | - | - | -
3 | I3 | I2 | I1 | - | -
4 | I4 | I3 | I2 | I1 | -
5 | - | I4 | I3 | I2 | I1
6 | - | I4 | NOP | I3 | I2
7 | - | - | I4 | NOP | I3
8 | - | - | - | I4 | NOP
9 | - | - | - | - | I4
Time
Stages
I1: R1 <- R2 + R3
I2: R4 <- R4 + R3
I3: R5 <- R5 + R3
I4: R6 <- R1 + R6

## Slide 117: If we can’t restructure our program?
Can we throw hardware at the problem and eliminate bubbles?

## Slide 118: Register forwarding
Let’s add an RP (read-pending) signal associated with each register to indicate an instruction is stalled in ID/RR for this register value
While B is a flip-flop, RP is a signal line
It’s a little more complicated than the next diagram shows. (ID/RR will advertise which register is needed on four address lines and the first pipeline stage that has that Rx value can gate its result onto the forwarding bus.)
[This is an oversimplification of the required circuitry and the description in the textbook doesn’t quite match the slides.]
Register file
B
B
B
B
B
B
B
B
RP
RP
RP
RP
RP
RP
RP
RP

## Slide 119: Forwarding example
IF
ID/RR
EX
MEM
RW
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I2
I1
Reg-file
R1 not ready to be read
R1 value forwarded
from EX stage
I1: R1 <- R2 + R3
I2: R4 <- R1 + R5
Forwarding logic in ID/RR:
If RP == 1 then
use forwarded value
else
read entry from DPRF

## Slide 120: Bubbles introduced by RAW
Number of unrelated instructions Between I1 and In | Number of bubbles Without forwarding | Number of bubbles With forwarding
0 | 3 | 0
1 | 2 | 0
2 | 1 | 0
3 or more | 0 | 0
I1: R1 <- R2 + R3
…
In: R4 <- R1 + R5

## Slide 121: What if an instruction intervenes?
I1: R1 <- R2 + R3
I2: R4 <- R4 + R3
I3: R6 <- R1 + R6
IF
ID/RR
EX
MEM
WB
I1
I2
I3
Now we need to forward from MEM to ID/RR

## Slide 122: What if two instructions intervene?
I1: R1 <- R2 + R3
I2: R4 <- R4 + R3
I3: R4 <- R4 + R3
I4: R6 <- R1 + R6
IF
ID/RR
EX
MEM
WB
I1
I2
I4
Now we need to forward from WB to ID/RR
I3

## Slide 123: And LW instructions are special
I1: LW R1, 0(R2)
I2: R4  R1 + R5
IF
ID/RR
EX
MEM
WB
I1
I2
I3
Even with data forwarding, we have to insert a bubble!
Why? We don’t get the data until I2 gets to MEM!
NOP

## Slide 124: So LW changes the table
Number of unrelated instructions Between I1 and I2 | Number of bubbles Without forwarding | Number of bubbles With forwarding
0 | 3 | 0
1 | 2 | 0
2 | 1 | 0
3 or more | 0 | 0
RAW Hazard
I1: R1 <- R2 + R3
…
I2: R4 <- R1 + R5
Number of unrelated instructions Between I1 and I20 | Number of bubbles Without forwarding | Number of bubbles With forwarding
0 | 3 | 1
1 | 2 | 0
2 | 1 | 0
3 or more | 0 | 0
RAW Hazard
I1: LW R1, 0(R2)
…
I2: R4 <- R1 + R5

## Slide 125: Generalized register forwarding
We need forwarding data lines from ALL stages
IF
ID/RR
EX
MEM
RW
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
Reg-file
R1 not ready to be read
And we have two registers to be fed

## Slide 126: An example of implementation
DPRF
(16)
B
MUX
MUX
B
A
DBUF
32
32
ID/RR
EX
MEM
WB
RPB
RPA
Logic
Logic
Logic
Forwarding buses (data)
32
We really need two pairs of busses: one for A and one for B
(regno)
RPBWB
RPAWB
RPBM
RPAM
RPBEX
RPAEX
4
Ry
Rz
Ry
Rz

## Slide 127: What’s going on?
This is a rough outline of what happens in the preceding diagram:
ID/RR puts the registers numbers used for A and B on the two forwarding register busses
The other stages compare any results for their destination register with the register numbers on the two register busses
If the destination register matches a register on a register forwarding bus, the stage opens the driver to allow the destination value it has onto the appropriate A and/or B forwarding data bus and signals ID/RR that a match has been found on the A or B operand via RPA/RPB.
There is circuitry (sort of like interrupt priority) that makes sure the first stage that matches on the forwarding register bus is the one that gets to use the forwarding data bus (Why?)
If the RPA/RPB signals are sent, multiplexors in the ID/RR stage select the the data from the corresponding A or B forwarding data bus instead of the register file

## Slide 128
Control and data forwarding lines not shown

## Slide 129: Other data hazards
WAR I1: R2  R1 + R3 I2: R1  R4 + R5
Fortunately, this isn’t a problem since we’ve already read the registers for I1 into DBUF before I2 starts.
WAW I1: R1  R2 + R3 I2: R1  R4 + R5
Currently, the B bit set by I1 will stall I2

## Slide 130: But why do we see WAW anyway?
Shouldn’t the compiler get rid of useless writes?
There are unexpected code sequences
  Exception handling code
Check out Sec 5.13.2 page 200 and Sec 5.15.4 if you’re curious

## Slide 131: What hazards?
I1: R1  R2 + R3
I2: R1  R1 + R4
I3: R5  R1 + R6
RAW
RAW
WAW
Can’t let I2 move forward until I1 is retired from pipeline
Otherwise I3 could get the wrong value (from I1 instead of I2)
Fortunately, the existing behavior of WAW hazards will cause I2 to stall until I1 completes its write in WB.

## Slide 132: Control hazard
Cycle IF* ID/RR EX MEM WB
1 BEQ
2 ADD
3 NAND
4 LW
* We do not actually know what the instruction is in the Fetch Stage
Is there any analog in the sandwich pipeline?

## Slide 133: Conservative handling of branches
Wait until branch outcome is known
  Stall the pipeline  send NOPs from IF state
Resume normal execution when branch outcome is known
  Result of comparison (A-B) is known
  If there is need to branch, PC gets the target address of the branch
Two cases
  Branch TAKEN (i.e. A==B)
  Branch NOT TAKEN (i.e. A!=B)

## Slide 134: Conservative branch handling
Cycle 1
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I4
I3
BEQ
I2
I1
Note: IF stage does not know yet

## Slide 135: Branch handling
Decode stage knows
Cycle 2
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
I4
BEQ
I3
I2
STAY
NOP

## Slide 136: Branch handling
A-B calcu-
lated
Cycle 3
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
BEQ
I4
I3
NOP

## Slide 137: Branch handling (taken)
Cycle 3
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
BEQ
I4
I3
NOP
A-B is calculated as zero and branch is going to be taken
PC+offset is being calculated
STAY
NOP

## Slide 138: Branch handling (taken)
Cycle 3
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
BEQ
I4
I3
NOP
A-B is calculated as zero and branch is going to be taken
PC+offset is being calculated  value is clocked into PC at end of EX
STAY
NOP
X

## Slide 139: Branch handling (taken)
Cycle 4
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
It
BEQ
I4
NOP
We used updated PC to fetch the target of branch
NOP

## Slide 140: Branch handling (taken)
Cycle 5
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
It
BEQ
NOP
Normal pipeline operation resumed
NOP
It+1

## Slide 141: Branch handling (taken)
Cycle 5
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
It
BEQ
NOP
Upshot: Two pipeline bubbles
NOP
It+1

## Slide 142: Branch handling
A-B calcu-
lated
Cycle 3
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
BEQ
I4
I3
NOP

## Slide 143: Branch handling (NOT taken)
Cycle 3
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
BEQ
I4
I3
NOP
A-B calculated as non-zero; branch not taken
PC is already pointing to the sequential path

## Slide 144: Branch handling (NOT taken)
Cycle 4
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
BEQ
I4
NOP
A-B calculated as non-zero; branch not taken
Normal pipeline operation resumed
I6

## Slide 145: Branch handling (NOT taken)
Cycle 4
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I5
BEQ
I4
NOP
Upshot: one pipeline bubble
I6

## Slide 146
With conservative handling of branches there will always be at least…
1 bubble in the pipeline
2 bubbles in the pipeline
3 bubbles in the pipeline
0 bubbles in the pipeline
Today’s winning number is 97,531
200

## Slide 147
With conservative handling of branches there will always be at most…
1 bubble in the pipeline
2 bubbles in the pipeline
3 bubbles in the pipeline
0 bubbles in the pipeline
210

## Slide 148: Code for our examples
Presume the following sequence of instructions:
BEQ L1
ADD
LW
….
L1 NAND
SW
The instruction executed following the BEQ will either be ADD or it will be NAND depending on BEQ

## Slide 149: Perfect pipeline
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ |  | - | -
3 | NAND | ADD | BEQ | - | -
4 | SW | NAND | ADD | BEQ | -
5 | - | SW | NAND | ADD | BEQ
6 | - | - | SW | NAND | ADD
7 |  |  | - | SW | NAND
8 |  |  |  | - | SW
9 |  |  |  |  | 
Unfortunately stalls ruin a perfect pipeline

## Slide 150: Conservative Branch Handling
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | (ADD) | NOP | BEQ | - | -
4 | NAND | NOP | NOP | BEQ | -
5 | SW | NAND | NOP | NOP | BEQ
6 | - | SW | NAND | NOP | NOP
7 | - | - | SW | NAND | NOP
8 |  |  | - | SW | NAND
9 |  |  |  | - | SW

## Slide 151: Cycle 2: Still Don’t Know If We Branch
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | (ADD) | NOP | BEQ | - | -
4 | NAND | NOP | NOP | BEQ | -
5 | SW | NAND | NOP | NOP | BEQ
6 | - | SW | NAND | NOP | NOP
7 | - | - | SW | NAND | NOP
8 |  |  | - | SW | NAND
9 |  |  |  | - | SW
Only at the end of EX stage is the target address of BEQ known
What should cycle 2 do?
 ID/RR tells IF to stall after fetching
 IF sends NOP to ID/RR at end of cycle

## Slide 152: Cycle 3: Branch taken…
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | (ADD) | NOP | BEQ | - | -
4 | NAND | NOP | NOP | BEQ | -
5 | SW | NAND | NOP | NOP | BEQ
6 | - | SW | NAND | NOP | NOP
7 | - | - | SW | NAND | NOP
8 |  |  | - | SW | NAND
9 |  |  |  | - | SW
IF sends another NOP into ID/RR at cycle 3 end
EX sets PC to PC saved in FBUF + offset so NAND is fetched
Assume BR is taken
A – B
PC  PC + offset

## Slide 153: Cycle 4: Branch Taken
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | (ADD) | NOP | BEQ | - | -
4 | NAND | NOP | NOP | BEQ | -
5 | SW | NAND | NOP | NOP | BEQ
6 | - | SW | NAND | NOP | NOP
7 | - | - | SW | NAND | NOP
8 |  |  | - | SW | NAND
9 |  |  |  | - | SW
Only at the end of the EX stage was the target addr of BEQ known
We have these two NOPs introduced by BEQ stalling the pipeline
Assume BR is taken

## Slide 154: Cycle 9: Finished
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | (ADD) | NOP | BEQ | - | -
4 | NAND | NOP | NOP | BEQ | -
5 | SW | NAND | NOP | NOP | BEQ
6 | - | SW | NAND | NOP | NOP
7 | - | - | SW | NAND | NOP
8 |  |  | - | SW | NAND
9 |  |  |  | - | SW
Cycles 5-9, the pipeline runs normally (i.e. no more stalls)
Finish here with stalls

## Slide 155: Cycle 4: Branch Not Taken
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | (ADD) | NOP | BEQ | - | -
4 | LW | ADD | NOP | BEQ | -
5 |  | LW | ADD | NOP | BEQ
6 | - |  | LW | ADD | NOP
7 | - | - |  | LW | ADD
8 |  |  | - |  | LW
9 |  |  |  | - | 
EX on cycle 3 allows IF and ID/RR to proceed normally on cycle 4
Finish here with stalls

## Slide 156: What's the CPI difference?
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | (ADD) | NOP | BEQ | - | -
4 | NAND | NOP | NOP | BEQ | -
5 | SW | NAND | NOP | NOP | BEQ
6 | - | SW | NAND | NOP | NOP
7 | - | - | SW | NAND | NOP
8 |  |  | - | SW | NAND
9 |  |  |  | - | SW
Branch taken: 9 total cycles / 3 instructions = 3 CPI
Not taken: 8 total cycles / 3 instructions = 2.66 CPI

## Slide 157: Strategies for improving branches
Branch prediction
Delayed branch

## Slide 158: Branch prediction
Cycle IF* ID/RR EX MEM WB
1 BEQ
2 ADD BEQ
3 LW ADD BEQ
* We do not actually know what the instruction is in the Fetch Stage
Assume branch is not taken

## Slide 159: Branch Prediction
IF
ID/RR
EX
MEM
WB
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
LW
BEQ
ADD
SQUASH
SQUASH
Our prediction was wrong! Branch will be taken
Squash the instructions at IF and ID/RR
X
X
NOP
NOP

## Slide 160
Given the following sequence of instructions:
BEQ L1
ADD
LW
….
L1 NAND
SW
Using the branch prediction approach, what is the observed CPI for the 3 instructions (BEQ, ADD, LW) or (BEQ, NAND, SW) in each case?
2.33 not taken / 3 taken
3 not taken / 2.33 taken
2.66 not taken / 3 taken
2 not taken / 3 taken
220

## Slide 161: Happy path – prediction true!
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | LW | ADD | BEQ | - | -
4 | - | LW | ADD | BEQ | -
5 | - | - | LW | ADD | BEQ
6 | - | - | - | LW | ADD
7 | - | - | - | - | LW
What if prediction turns out false?
7 cycles / 3 instructions – 2.33 CPI

## Slide 162: Branch prediction failed
Cycle Number | IF | ID/RR | EX | MEM | WB
1 | BEQ | - | - | - | -
2 | ADD | BEQ | - | - | -
3 | LW | ADD | BEQ | - | -
4 | NAND | NOP | NOP | BEQ | -
5 | SW | NAND | NOP | NOP | BEQ
6 | - | SW | NAND | NOP | NOP
7 | - | - | SW | NAND | NOP
8 |  |  | - | SW | NAND
9 |  |  |  | - | SW
Squash ADD and LW and replace with NOPs; basically we degrade to the conservative approach
9 cycles / 3 instructions – 3 CPI

## Slide 163: Branch prediction heuristics
How do we (quickly) guess which way a branch will go?
Can often tell by comparing target with current PC
  Loops usually branch backwards (target < PC)
    Guess the branch will be taken
  Conditionals usually branch forwards (target > PC)
    Guess the branch won’t be taken
Some ISAs have 2 different families of branch instructions so that the compiler can signal whether it thinks the branch will be taken or not taken
Or we could keep a history…

## Slide 164: Branch Target Buffer
PC Instr
1000 BEQ
…
1300 BEQ
…
1500 BEQ
…
1600 BEQ
…
1800 BEQ
…
PC of branch instruction | Taken/Not Taken | PC of branch target
1000 | T | 1200
1300 | N | xxxx
1500 | T | 1100
1600 | N | xxxx
1800 | N | xxxx
Past history

## Slide 165: Delayed branching
Ignore the problem in hardware (i.e. no automatic generation of NOPs in fetch stage)
Give the NOP instructions to the compiler
  E.g. the instruction after a branch is always executed
Let the compiler worry about it
  Compile in a NOP instruction after every branch instruction
Why is this a good idea?
The compiler may be able to optimize…

## Slide 166: Example using MIPS-style branch delays
; Add 7 to each element of a ten-element array
; whose address is in a0
addi $t1, $a0, 40; When a0=t1 we are done
loop:
beq $a0, $t1, done
nop ; branch delay slot
lw $t0, 0($a0)
addi $t0, t0, 7
sw $t0, 0($a0)
addi $a0, $a0, 4
beq $zero, $zero, loop
nop ; branch delay slot
done: halt

## Slide 167: Delayed branch – before optimization
; Add 7 to each element of a ten-element array
; whose address is in a0
addi $t1, $a0, 40; When a0=t1 we are done
loop:
beq $a0, $t1, done
nop ; branch delay slot
lw $t0, 0($a0)
addi $t0, t0, 7
sw $t0, 0($a0)
addi $a0, $a0, 4
beq $zero, $zero, loop
nop ; branch delay slot
done: halt
Let’s assume one delay slot

## Slide 168: Delayed branch – during optimization
; Add 7 to each element of a ten-element array
; whose address is in a0
addi $t1, $a0, 40; When a0=t1 we are done
loop:
beq $a0, $t1, done
nop ; branch delay slot
lw $t0, 0($a0)
addi $t0, $t0, 7
sw $t0, 0($a0)
addi $a0, $a0, 4
beq $zero, $zero, loop
nop ; branch delay slot
done: halt
OK if LW is redundantly executed on loop exit

## Slide 169: Delayed branch – during optimization
; Add 7 to each element of a ten-element array
; whose address is in a0
addi $t1, $a0, 40; When a0=t1 we are done
loop:
beq $a0, $t1, done
nop ; branch delay slot
lw $t0, 0($a0)
addi $t0, $t0, 7
sw $t0, 0($a0)
addi $a0, $a0, 4
beq $zero, $zero, loop
nop ; branch delay slot
done: halt

## Slide 170: Delayed branch – after opt
; Add 7 to each element of a ten-element array
; whose address is in a0
addi t1, a0, 40 ; When a0=t1 we are done
loop:
beq $a0, $t1, done
lw $t0, 0($a0) ; branch delay slot
addi $t0, $t0, 7
sw $t0, 0($a0)
beq $zero, $zero, loop
addi $a0, $a0, 4 ; branch delay slot
done: halt

## Slide 171
Name | Pros | Cons | Use cases
Stall the pipeline | Simple strategy, no hardware needed for squashing instructions | Loss of performance | Early pipelined machines such as IBM 360 series
Branch Prediction (branch not taken) | Results in good performance with small additional hardware since the instruction is anyhow being fetched from the sequential path already in IF stage | Needs ability to squash instructions in partial execution in the pipeline | Most modern processors such as Intel Pentium, AMD Athlon, and PowerPC use this technique; typically they also employ sophisticated branch target buffers; MIPS R4000 uses a combination 1-delay slot plus a 2-cycle branch-not-taken prediction
Branch Prediction (branch taken) | Results in good performance but requires slightly more elaborate hardware design | Since the new PC value that points to the target of the branch is not available until the branch instruction is in EX stage, this technique requires more elaborate hardware assist to be practical | -
Delayed Branch | No need for any additional hardware for either stalling or squashing instructions; It involves the compiler by exposing the pipeline delay slots and takes its help to achieve good performance | With increase in depth of pipelines of modern processors, it becomes increasingly difficult to fill the delay slots by the compiler | Older RISC architectures such as MIPS, PA-RISC, SPARC

## Slide 172: Summary of hazards
Instruction | Type of Hazard | Potential Stalls | With Data forwarding | With branch prediction (branch not taken)
ADD, NAND | Data | 0, 1, 2, or 3 | 0 | Not Applicable
LW | Data | 0, 1, 2, or 3 | 0 or 1 | Not Applicable
BEQ | Control | 1 or 2 | Not Applicable | 0 (success) or 2 (mispredict)

## Slide 173: Program discontinuities
IF
ID/RR
EX
MEM
WB
BUF
F
ER
BUF
F
ER
BUF
F
ER
BUF
F
ER
I4
I6
I3
I2
I5
External interrupt can occur at any time
Any one of the 5 instructions may cause an exception
Any one of the the 5 instructions may be a TRAP instruction
When do we take the interrupt?
STOP, DRAIN, go to INT state
  Slow to respond to external events
Look for external INT in a specific stage (e.g. EX state)
  DRAIN preceding instructions
  FLUSH subsequent instructions

## Slide 174: Superscalar pipelines

## Slide 175: Different Pipeline Depths

## Slide 176: Intel Core Microarchitecture: An example pipeline
CISC style instructions
RISC style instructions
Really complex instruct-tions and excep-tions