## Slide 1: Networking
Ramachandran & Leahy Chapter 13

## Slide 2: What do you mean by network?
A computer connected to a network is called a host
The connection is made using a device called a Network Interface Card or NIC
What exactly is “the network"?
It's a big collection of interconnected networks that all use the same protocols to communicate, hence "the internet"

## Slide 3: The traditional way
What is the Internet? Consider the postal system…
Chandra sends a birthday letter to her grandmother
Chennai, India
Mailpattie, Tamil Nadu
Atlanta

## Slide 4: The modern way
Now consider an email from Joe to his grandmother
Atlanta
Yuba City, CA
Atlanta
Sacramento

## Slide 5: Commonality
What do those two paradigms have in common?
Universally understood addresses!
  A country and a postal code
    The staff at the Atlanta regional post office probably have no idea where Mailpatti, Tamil Nadu, India is.
    But they know how to get mail to India and specifically to deliver mail for the postal code for the state of Tamil Nadu via its capital Chennai
    Once the mail gets to Chennai, the staff there know how to get it to Mailpatti, even if it must take a bullock cart
  An IP address
    The routers at the ISP in Atlanta probably have no idea where Yuba City, CA is, but they know how to get packets to the internet core
    The internet core does know which ISP services the IP addresses in Yuba City, CA
    The message goes to a mail server at the ISP and waits for Alex's grandmother to dial up her internet connection
Key point
  No individual has to know where all the addresses are located, but at each hop they know where to forward an item to get it a hop closer

## Slide 6: IP network connections
P1
Protocol
stack
User
OS
Network
P2
Protocol
stack
User
OS
msg
pkt1
pkt2
pktn
…
pkt1
pkt2
pktn
…
msg
hdr
Big deal: Note that the Protocol Stacks are in the hosts, not in the middle of the Network
payload

## Slide 7: Contrast: Datagram or VC network
Internet (Datagram)
data exchange among computers
  “elastic” service, no strict timing req.
many link types
  different characteristics
  uniform service difficult
“smart” end systems (computers)
  can adapt, perform control, error recovery
simplicity inside network layer, complexity at “edge”
ATM (Virtual Circuits)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
complexity inside network layer, simplicity at edge

## Slide 8: Why does IP need a protocol stack?
Arbitrary message sizes
Out of order delivery
Packet loss
Bit errors
Queuing delays

## Slide 9: Internet Protocol Stack
Physical
Link
Network
Transport
Application
Layer 1
Layer 2
Layer 3
Layer 4
Layer 5

## Slide 10: The OSI Model
The OSI model is like the relational database model: It's great for studying networks, but has had very poor performance in real life
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model
Application
Transport
We'll start here

## Slide 11: Getting from here to there…

## Slide 12: Transport (session) protocol
We’re going to talk about these protocol types
Stop and wait
Pipelined transmission
Reliable pipelined transmission

## Slide 13: Who invented the Internet?
Vannevar Bush
George W. Bush
George H. W. Bush
Al Gore
J. C. R. Licklider
Robert Kahn & Vinton Cerf
Famous scientist, but think Manhattan project
All politicians, but they did provide money so give 'em a little credit
Packet switched networking, 1965
Devised IP suite to unify various networks, 1973

## Slide 14: Stop and wait (for ack)
Timeline of sender
Pkt0
2τ
ACK0
Pkt1
2τ
ACK1
Pkt2
2τ
ACK2
Pkt3
. . .

## Slide 15: Latency

## Slide 16: One round trip
Round Trip Time

## Slide 17: Lost packet

## Slide 18: Lost ack

## Slide 19: More details
How much buffer does the stack need at the sender?
  Just 1
How much buffer does the stack need at the receiver?
  Just 1
How do I know at the receiver that a packet I'm getting is not a duplicate
  Include a sequence number
How big should a sequence number be?
  It might only need to be 1 bit if there's only one message in flight

## Slide 20: Assumptions
In our stop-and-wait protocol, we make some assumptions
  Packet loss is possible
  Packets don't get reordered or arbitrarily delayed (how can they if only one packet is in flight)
  So we can get away with a 1 bit sequence number
However, there are more fundamental assumptions in a packet-switched network
  Packet loss is possible (i.e. best-effort delivery)
  Packets may be reordered or arbitrarily delayed
  Packets may be damaged in transit
Our 1-bit sequence number isn't going to hold up with more than one packet in flight
  So we use monotonically increasing sequence numbers

## Slide 21: Working at top speed!
Remember Latency?
240 ms to Chennai
RTT = 240ms
4 packets per second throughput?
No matter how fast the network?

## Slide 22: How many packet buffers does the sender need for stop-and-wait protocol?
1
2
Designer's choice
No way to predict in advance
Today’s number is 70476
10

## Slide 23: Pipelined protocol
Timeline of sender
Pkt0
Pkt1
Pkt2
Pkt3
. . .
Blast a bunch of packets one after another
What could go wrong?

## Slide 24: Reliable pipelined protocol
Sometimes all the packets don't make it the way!
We have to keep track

## Slide 25: Reliable pipelined protocol
2τ
Timeline of sender
. . .
Pkt0
Pkt1
Pkt2
Pkt3
Ack0
Ack1
Ack2
Ack3
Pkt4
Pkt5
Pkt6
Pkt7
Now we get 4 packets every 240ms = 16 packets/sec

## Slide 26: Reliable pipelined protocol
Buffers at sender
Buffers at receiver

## Slide 27: How many?
How many packet buffers does the sender need to implement a reliable pipelined protocol?
1
2
One buffer for each packet in the pipeline
Protocol designer's choice
20

## Slide 28: What might a packet look like?
struct header_t {
int destination_address; /* destination address */
int source_address; /* source address */
int num_packets; /* total number of packets in
the message */
int sequence_number; /* sequence number of this
packet */
int packet_size; /* size of data contained in
the packet */
int checksum; /* for integrity check of this
packet */
};
struct packet_t {
struct header_t header; /* packet header */
char *data; /* pointer to the memory buffer
containing the data of size
packet_size */
};

## Slide 29: Transport (& session) layer concerns
Arbitrary message size
Out of order delivery
Packet loss
Bit errors
Queuing delays
How do we address these?

## Slide 30: Transport (& session) layer concerns
Arbitrary message size
Out of order delivery
Packet loss
Bit errors
Queuing delays
 Big segments use multiple packets
 Sequence numbers
 Positive ACK and buffers
 Checksum for packet
 But how to handle this one?

## Slide 31: Network congestion
Networks tend to grow
Network connections get overcommitted
Packets are queued, but get so stale they must be dropped
Because of the sequence number, we can ignore heavily delayed packets if they ever make it
10Gb/sec
10Gb/sec
10Gb/sec
10Gb/sec
100 Gb/sec
Access Networks
Regional networks

## Slide 32: Reliable protocol with windowing
Increasing sequence numbers
Active window of
sequence numbers
Packets sent and acknowledged
Packets sent but not
yet acknowledged
Packets that are in the active
window that can
be sent without waiting for any
further ACKS
Packets that cannot yet
be sent since they
are outside the active window
Congratulations! You've now been introduced to TCP from the IPv4 protocol

## Slide 33: Transport protocols on the Internet
Transport protocol | Features | Pros | Cons
TCP | Connection-oriented; self-regulating; data flow as stream; supports windowing and ACKs | Reliable; messages arrive in order; well-behaved due to self-policing | Complexity in connection setup and tear-down; at a disadvantage when mixed with unregulated flows; no guarantees on delay or transmission rate
UDP | Connection-less; unregulated; message as datagram; no ACKs or windowing | Simplicity; no frills; especially suited for environments with low chance of packet loss and applications tolerant to packet loss; | Unreliable; message may arrive out of order; may contribute to network congestion; no guarantees on delay or transmission rate

## Slide 34: Choice of transport protocols
Application | Key requirement | Transport protocol
Web browser | Reliable messaging; in order arrival of messages | TCP
Instant messaging | Reliable messaging; in order arrival of messages | TCP
Voice over IP | Low latency | Usually UDP
Electronic Mail | Reliable messaging | TCP
Electronic file transfer | Reliable messaging; in order delivery | TCP
Video over Internet | Low latency | Usually UDP; may be TCP
File download on P2P networks | Reliable messaging; in order arrival of messages | TCP
Network file service on LAN | Reliable messaging; in order arrival of messages | TCP; or reliable messaging on top of UDP
Remote terminal access | Reliable messaging; in order arrival of messages | TCP

## Slide 35: Now let's look lower
IP lives at the network layer
Let’s look specifically at IP as a layer 3 as well as its relationship to the Transport (Session) layers
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model

## Slide 36: The Story of IP
No public internet
Islands of connectivity
  Data link layer networks all over, even in 1983
    Ethernet
    802.11 wireless
    Token Ring
    AppleTalk
    RS232 serial
    ATM
    And plenty more
So can we build a network of networks?

## Slide 37: The Story of IP
Build a network layer that can address and interconnect all sorts of different data link networks
After a decade of innovation and another decade of growth
IP for everybody (version 4 that is) with two built-in transport protocols, TCP and UDP
The internet

## Slide 38: IP datagram (packet) format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
Header length
(bytes/4)
Upper layer protocol
to deliver payload to
Total datagram
length (bytes)
“Type” of data
Used for
fragmentation/
reassembly
Max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 39: TCP Segment Header
Source port
Dest port
32 bits
data
(TCP payload)
Sequence number
Acknowledgement number (if ACK flag set)
Data
offs
Checksum
options (if any)
Window size
000
URG
ECE
ACK
PSH
RST
SYN
FIN
CWR
NS
Urgent ptr
Source port number
Packet checksum
Dest port number
First byte number sent
Last byte
number received
Last byte position
Of urgent data
(URG flag set)
Size of sliding
window
Flags: NS CWR URG ECE
ACK PSH RST SYN FIN

## Slide 40: Visible relations between layers
Layers 2 through 5 are manifested in the packets we send on the network
(Layers 1, 6, and 7 are too, but showing them makes this too complicated)
Let’s see how…
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model

## Slide 41: Encapsulated packets
The network protocol is designed in layers
Thus, the lower level packets encapsulate (enclose) the higher level packets
IP (Layer 3) Header
-----------------
IP Data
Ethernet (Layer 2) Header
-----------------
Ethernet Payload
-----------------
Ethernet Trailer
TCP (Layer 4-5) Header
-----------------
TCP Payload
Data Link
Network
Transport/Session
Ethernet (Layer 2) Header
-----------------
Ethernet Payload
-----------------
Ethernet Trailer
IP (Layer 3) Header
-----------------
IP Data
TCP (Layer 4-5) Header
-----------------
TCP Payload
Remember: Layer 2 doesn’t have to be ethernet and layer 4-5 doesn’t have to be TCP

## Slide 42: IPv4 Header

## Slide 43: TCP Segment Header

## Slide 44: IP Addressing
32 bits / 4 octets / four-decimal dotted quad
  Did you know that 130.207.7.31 becomes 0x82CF071F?
  Each of those four numbers is decimal for a single byte
And we need a mask
We use it to divide the IP address into a "network" part and a "host" part
  It's a 32-bit number that starts with 1s and ends with 0s
  The network part is "under" the ones in the mask
There are exactly 33 valid masks, FWIW

## Slide 45: Subnet and CIDR Notation
Two different notations, same meaning:
  130.207.254.64 255.255.255.192
  130.207.254.64/26
In this example, the network part is the first 26 bits, host is last 6
If you're doing this every day, you learn to do it in your head; if not, use a subnet calculator, e.g. http://www.subnet-calculator.com/cidr.php
Cisco equipment sometimes uses the former notation; many other modern tools use the latter
130
207
254
64
10000010
11001111
11111110
255
255
255
11111111
11111111
11111111
Note /26
leading 1 bits
01
000000
192
11
000000
Network
Host
1 1 0 0 1 1 1 1
1
2
8
6
4
3
2
1
6
8
4
2
1
192 + 15 = 207
Notes: 45

## Slide 46: What gets assigned an IP address?
Some people think that IP addresses are assigned to hosts (i.e. computers)
That’s a misconception
IP addresses are assigned to network interfaces, so a computer may have more than one.
To be able to participate on the internet, a computer just needs one network interface giving rise to the misconception that IP addresses are assigned to computers
Computers that route traffic between networks (a.k.a. routers) always have more than one IP address

## Slide 47: What does it mean to be on the same network?
In the IP world, it’s simple
  If network bits from two addresses are equal, the two are on the same network
  “On the same network” means the data link layer will be used to deliver traffic between the two addresses, not the network layer
Source IP address | Destination IP address | Mask | On the same network?
130.207.7.23 | 130.207.254.16 | /16 (255.255.0.0) | Yes
192.168.1.2 | 192.168.2.2 | /24 (255.255.255.0) | No
0x81880507 | 0x818910F1 | /15 (255.254.0.0) | Yes
172.16.32.12 | 10.0.5.2 | /16 (255.255.0.0) | No

## Slide 48: Are these two IP addresses on the same network?
143.215.14.243 and 143.214.14.242 if the mask for each is /24
Yes
No
Can’t tell
All of the above
30
Keeping the first 24 bits of the two addresses, we get
143.215.14.0
and
143.214.14.0
Are they the same number?
Nope.

## Slide 49: Are these two IP addresses on the same network?
143.215.14.243 and 143.214.14.242 if the mask for each is /15
Yes
No
Can’t tell
None of the above
40
Keeping the first 15 bits of the two addresses, we get
143.214.0.0 (215=110101112; first 7 bits are 110101102)
and
143.214.0.0 (214=110101102; first 7 bits are 110101102)
Are they the same number?
Yes!
Today’s number is 12,861

## Slide 50: Subnets
Remember those Islands of Connectivity? And that mask?
  We call each of those “Islands” a subnet
The rule for IP routing:
  If you’re on the same network, punt to the data link layer to deliver
  Otherwise, use your IP routing table to forward it to another IP host on your network
How can you tell if you're on the same network?
  The mask tells you how many leading bits are the “network part” of the IP address.
  If the network part of the destination address matches the network part of (one of) your interface address(es), you’re on the same network.
  Each node on the network only needs to know the mask for its own IP address (think about it), so masks don’t need to be passed in packets
So all hosts on a data link level network must be assigned IP addresses that have the same network part (and hence the same mask).

## Slide 51: Connecting the Islands
Data link layer networks connected by IP hosts
Now where do the masks come in?
Clue: All the masks here are /24.
The blue blobs are indeed different IP networks
The three routers pass traffic between the three outer networks
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.2
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Notes: Need some examples

## Slide 52: Traveling between the Islands
For example, 223.1.1.2 can talk to 223.1.3.2:
223.1.1.2 sends its packet for 223.1.3.2 to 223.1.1.3 via layer 2
The top router knows how it’s connected to the other two routers and so sends the packet from 223.1.1.2 to 223.1.7.1
The bottom right router knows it has a connection to 223.1.3.0/24 so it sends the packet from 223.1.1.2 to 223.1.3.2.
We’d say this route has “2 hops”
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.2
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Notes: Need some examples

## Slide 53: IP Classes – History Lesson
  In the dark ages, subnet masks could be derived from the network address
  Now that’s called “classful” addressing
  These can still show up as a default mask if you don't specify one
Class | Prefix | Range | Mask | Purpose
A | 0… | 0.0.0.0-127.255.255.255 | 8 | 
B | 01… | 128.0.0.0-191.255.255.255 | 16 | 
C | 011… | 192.0.0.0-223.255.255.255 | 24 | 
D | 0111… | 224.0.0.0-239.255.255.255 | - | multicast
E | 1111… | 240.0.0.0-255.255.255.255 | - | reserved

## Slide 54: CIDR: Classless Inter-Domain Routing
  We ran out of IPv4 addresses in 1995!
  This was the very clever solution
  Turns out you only really need to know the network mask if you’re connected to that network!
  Now we simply specify the mask for the local subnet on each network interface
Notes: Special networks need to go later

## Slide 55: IP Routing Table for an Edge Device
Destination | Gateway | Flags | Interface
0.0.0.0/0 | 128.61.5.1 | UG | 
128.61.5.0/24 | 0.0.0.0 | U | enp0s1
128.61.5.1/32 | 0.0.0.0 | U | enp0s1
127.0.0.1/8 | 127.0.0.1 | UH | 
If the destination is on our network, send the packet to the data link layer (Note this shows up in the routing table)
Look through the routing table and choose the match with the longest prefix (largest mask); send the packet to that gateway
Question: Which line does 128.61.5.82 match? How about 130.207.5.9? 127.87.5.12?
The interesting part comes later: How to create the routing table

## Slide 56: Our Example Network
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.2
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Internet
223.1.15.2
Let’s look at this router’s routing table
Notes: Need some examples

## Slide 57: IP Routing Table for a Router
Destination | Gateway | Flags | Interface
0.0.0.0/0 | 223.1.7.1 | UG | 
223.1.1.0/24 | 0.0.0.0 | U | enp2s1
223.1.7.0/24 | 0.0.0.0 | U | enp0s1
223.1.9.0/24 | 0.0.0.0 | U | enp1s1
223.1.2.0/24 | 223.1.9.1 | UG | 
223.1.3.0/24 | 223.1.7.1 | UG | 
223.1.7.1/32 | 0.0.0.0 | U | enp0s1
127.0.0.1/8 | 127.0.0.1 | UH | 
There is more than one possible set of values for this table, but this set is sufficient
How do you think this network shows up to the internet? 221.1.0.0/20 (e.g. 221.1.0 – 221.1.15.0)

## Slide 58: Questions: IP Routing rules
If the network address part of the interface address and destination addresses are the same, then
Pass the packet to layer 2 for delivery
Send the packet to the next-hop router based on the IP routing table
Return an Acknowledgement to the source address
Send a Reset packet to the next-hop router
Today’s number is 12,861
50

## Slide 59: Questions: IP Routing rules
If the network address part of the interface address and destination addresses are different, then
Pass the packet to layer 2 for delivery
Send the packet to the next-hop router by choosing the longest match in the IP routing table
Send the packet to the next-hop router by choosing the shortest match in the IP routing table
Return an ICMP “No route to host” message
60

## Slide 60: Now let’s add Layers 4-5 in IP
TCP and UDP are the two most common IP Transport protocols
In IP, recall the division between L4 and L5 is not well defined
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model

## Slide 61: Starting a TCP connection
TCP streams are always bidirectional. Either side may send data to the other side.
TCP uses a sequence number in each direction to maintain packet order
We refer to the 3 packets at the beginning of a TCP connection as the SYN, SYN-ACK, and ACK packets, hence the term 3-way handshake. SYN and ACK are flag bits in the TCP header.
This is the two sides exchanging (randomly chosen) sequence numbers to synchronize data going in both directions

## Slide 62: Three-Way Handshake
The initiator (client) sends a packet with a random sequence number and the SYN flag set
The server recognizes the packet with SYN as a request to initiate a conversation. If it accepts the conversation, it responds by
  putting the sequence number in the acknowledgment field
  setting the ACK bit.
  putting a different random sequence number in the packet
  setting the SYN bit before sending the packet to the client
The client sees the SYN packet from the server and realizes that its request has been accepted. It responds with a packet containing the server’s sequence number in the acknowledgment field, the ACK bit set, and possibly some data in the payload.
When the client or server is done transmitting, it sends a packet with the FIN bit set. This causes the other side to no longer expect to receive packets on this connection

## Slide 63: Three-way handshake in a picture

## Slide 64: Ports and connection addressing
We know how to get packets from one host to another, but how do we identify conversations?
How does one distinguish UDP and TCP traffic from different services that share the same network interface?
  On each side of a conversation, port numbers (0-65535) are used to define unique connections
  Often the destination port on the first packet is a Well-known or Registered port number
  Note that the fields are not actually ordered this way in the packet
With TCP and UDP protocols, always consider the addressing as a quadruple: (source IP, source port, destination IP, destination port)
Trick question: How are ports used in ICMP conversations?
Let's look at where that ordered quad shows up in the segment...
Source
IP
Source
Port
Destination
IP
Destination
Port
Rest of
the packet

## Slide 65: TCP (and UDP) port addressing

## Slide 66: TCP and UDP port numbers
Port numbers are used to keep track of different conversations. Both source and destination port count.
Well-known ports numbers are traditionally from 1-1023.
Numbers 1024 and above are dynamic (ephemeral) port numbers.
Registered port numbers for vendor-specific applications are now allowed above 1024.

## Slide 67: TCP and UDP port numbers
Destination ports are chosen based on the desired service
  Often chosen based on the URL prefix, e.g. http: goes to 80, https: to 443
Source ports are usually chosen by the IP stack to be unique among all open connections
That makes the ordered quad unique among open connections
  This is how we keep connections separate even though the IPs are the same

## Slide 68: A browser opens two TCP connections to a web server
If the browser is running at 193.12.1.5, and the web server is offering service on port 80 at 130.207.7.13, how does TCP keep the conversations separate?
IP does this automatically
The conversations use independent sequence numbers to disambiguate them
The conversations include a special session-identifier that disambiguates them
The browser lets the TCP stack choose a unique source port number for each connection
Today’s number is 42,123
70

## Slide 69: Conversations
When the web browser opens each connection, it doesn’t specify a source port, allowing the TCP stack to pick a source port that isn’t in use by any conversation on that host, say 31339 or 31337.
The TCP stack uses the quads (193.12.1.5, 31337 or 31339, 130.207.7.13, 80) and its reverse to distinguish the two separate conversations
Each connection gets its own sequence number, window size, etc. and is treated as a completely separate conversation by both the browser’s and the web server’s IP stacks
Browser
Web
Server
S:31339
D:80
S:80
D:31337
S:31337
D:80
S:80
D:31339
193.12.1.5
130.207.7.13

## Slide 70: Stateful Firewalls
Follow a predefined policy on which ordered quads are allowed from which direction
  Example: Allow no inbound packets; Allow all outbound packets
Records state on connections as it is opened
  Requires a local state table (called a connection table)
Compares packets to the connection table first to automatically allow return traffic
  Example: If (193.12.1.5, 31337, 130.207.7.13, 80) is put in the connection table, then return traffic from (130.207.7.13, 80, 192.12.1.5, 31337) is automatically allowed
  Any inbound traffic to other ports at 192.13.1.5 is dropped since no policy rule allows it
Can do other protocol verification to drop malicious or badly-formed traffic
Firewall
Browser
Web
Server
Inbound
Outbound
S:31337
D:80
S:80
D:31337
S:12384
D:80
Connection
Table
✓
Makes sense if we don’t offer any services
193.12.1.5
130.207.7.13

## Slide 71: Network Address Translation
Note there is confusing terminology
Types
  Static one-to-one NAT
    A mapping is configured so that source address or destination address is changed from/to the mapped address on transit; checksums are recalculated
  Dynamic one-to-one NAT
    Same as Static, but a public address from a pool isn’t mapped until a private address attempts to cross the NAT device; the public address is returned to the pool when the conversation ends
  PAT or NPAT (network and port address translation)
    Building on Dynamic NAT, both the source address and source port are mapped to an address and port from the public pool (often of size 1); return traffic is mapped by destination address and port.
  And a lot of other variants
NPAT is typically the way we share a single public IP address among multiple hosts -- another way we’ve managed the scarcity of public IP addresses

## Slide 72: Remote procedure call (RPC)
P1
P2
foo (args)
foo (args)
return
RPC
Host 1
Host 2
We create a higher-level abstraction that allows a client to call a procedure to run on another server
We simply replace the called function with a shim function that
  Packs the arguments into a network packet
  Sends the packet to the listener
  Waits for a message from the listener with the function return value
  Receives and unpacks the data into the function results value
  Returns from the call with the result value
And the function's caller never knows that the work was done elsewhere!
The listener is a process in an infinite loop
  It waits for message containing arguments
  Unpacks the arguments
  Calls the function with the arguments
  Packs the result value into a network packet
  Sends the packet back to the sender
  Repeats the loop

## Slide 73: NFS (Linux network file system)
User program
read()
NFS client
RPC layer at client
RPC layer at server
NFS server
Linux file system
Linux file system
Network
Instead of making an I/O call to local storage, the file system passes the read() call through RPC to another Linux system
The "NFS server" fulfills the function call and sends the results back
read()

## Slide 74: IPv6
Goals
  32-bit IPv4 address space was “used up” first about 1996 and then again in 2013…
  …So bigger addresses!
  More efficiently processed header
  Header changes to facilitate QoS
Why such slow adoption?

## Slide 75: Basic differences
Fixed-length 40 byte header
  Options allowed after the header
No fragmentation allowed
No broadcast, only multicast
Addresses are 128 bits; network part is always the first 64 bits
1.8x1019 subnets; 1.8x1019 hosts on each subnet
Neighbor Discovery Protocol replaces ARP
NAT is discouraged, but local addresses available (fc00::/7)
Every interface must have a link-local address (fe80::/10)
Impractical to scan a subnet for hosts

## Slide 76: IPv6 Addressing
128 bits
8 16-bit hex numbers separated by colons
A dual colon means fill in with zeroes; only one allowed
2610:0148:1F00:0000:0000:0000:0000:0001 can be written as 2610:148:1F00:0:0:0:1 or 2610:148:1F00::1
Network
Interface Identifier (Host)
64 bits
64 bits
2610:0148:1F00:0000
0000:0000:0000:0001

## Slide 77: What is the size of an IPv6 address?
32 bits
64 bits
128 bits
256 bits
80

## Slide 78: GT IPv6 Addressing Plan
So, for example, 128.61.5.0/24 is already assigned 2610:148:1f00:0500::/64
So far, only GTRI has fired up their non-legacy prefix
2610
0148
Host
000uuuuu dddddddd
dddddddd dddddddd
00011111 ssssssss
xxxxxxxx yyyyyyyy
d = unit defined
u = major business unit, e.g 00=OIT, 01=GTRI, 02=CoE, 03=CoS, 04=CoC, 1F=reserved for legacy IPv4, 20-FF reserved for future
s = existing class B:
00=128.61.0.0
01=130.207.0.0
02=143.215.0.0
x.y = last two octets of IPv4 subnet address

## Slide 79: Now let's look at the data link layer
Ethernet is a very common data link network
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model

## Slide 80: Let’s talk about Ethernet
Ethernet is a particular type of data link network
It was designed for relatively small areas, like a building, hence the term Local Area Network (LAN)
It has its very own standard (IEEE 802.3)
It’s evolved a great deal since the 1980s

## Slide 81: Terminology
Collision domain - All the NICs that share a physical ethernet; only one can transmit at a time
Broadcast domain - All the NICs that can hear an ethernet broadcast frame
-----------
Repeater/hub - layer 1 replication/amplification of bits (both sides stay in one collision domain)
Bridge/switch - layer 2 re-transmission of ethernet frames (both sides stay in one broadcast domain)
Router - layer 3 forwarding of packets based on a layer-3 (IP) routing table
Host – a computer with one or more NICs; if it forwards traffic using multiple NICs, we’re going to call it a router, not a host.

## Slide 82: Ethernet Addressing
6 bytes/48 bits
  3 bytes OUI
  3 bytes NIC specific
Examples
  Apple: 00:25:00:f4:6d:c2
  Oracle: 00-03-ba-a1-02-df
To identify the OUI
  https://www.wireshark.org/tools/oui-lookup.html
Network Interface Controller (NIC) Specific
Organizationally Unique Identifier (OUI)
0: unicast
1: multicast
0: globally unique (OUI)
1: locally administered
Every ethernet device gets a unique burned-in MAC address

## Slide 83: Ethernet Frames
To send a frame
  Wait until no one using the cable (carrier sense)
  Assert carrier signal on the cable
  Broadcast the frame to all stations on the cable
  If you detect a collision while transmitting, stop and requeue the frame for retransmission
If you hear a frame on the cable
  Accept it if the destination MAC belongs to us (or if it has a broadcast or multicast destination MAC)
  Drop it if you see a collision during its receipt or its CRC doesn't match
See where CSMA/CD term comes from?
Preamble
Destination MAC
Source MAC
802.1Q tag
Ether type/
Length
Payload
CRC
Interframe Gap
8
6
6
0-4
2
4
12
46-1500

## Slide 84: Something is Missing…
Only one station can send at a time?
Where are the IP addresses?
We'll get back to this…

## Slide 85: Ethernet Topology (some history)
Host
Host
Host
Transceiver
Terminator
Coaxial
(10base5)
cable
AUI cable
(14 wire)

## Slide 86: Ethernet Topology (some history)
Host
Host
Host
Transceiver
Terminator
Coaxial
(10base5)
cable
AUI cable
(14 wire)
Host
Host
Host
Multi-port
Transceiver
Host
Host
Host
10baseT
Hub
Cat 3/Cat 5
Twisted pair
cable
Host
Host
Host
Adaptive
Bridge
Broadcast Domain
Collision Domain
Collision Domain
10/100/1000baseT
Switch
Host
Host
Host
Collision
Domain
Collision
Domain
Collision
Domain

## Slide 87: Ethernet Topology (some history)
Host
Host
Host
Host
Host
Host
Host
Host
Host
Cat 3/Cat 5
Twisted pair
cable
Host
Host
Host
Broadcast Domain
10/100/1000baseT
Switch
Host
Host
Host
Collision
Domain
Collision
Domain
Collision
Domain
10/100/1000baseT
Switch
10/100/1000baseT
Switch
10/100/1000baseT
Switch
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain

## Slide 88: Ethernet Topology (a history)
Host
Host
Host
Host
Host
Host
Host
Host
Host
Cat 3/Cat 5
Twisted pair
cable
Host
Host
Host
Broadcast Domain
10G/40G/100G
Switch
Host
Host
Host
Collision
Domain
Collision
Domain
Collision
Domain
10G/40G/100G
Switch
10G/40G/100G
Switch
10G/40G/100G
Switch
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain
Collision
Domain

## Slide 89: Ethernet Bridging Algorithm (simplified)
When a frame enters the bridge (switch):
  If the destination MAC address is in the bridge table
    Send the frame out the port listed in the bridge table entry
  Otherwise
    Flood the frame out all ports except the ingress port
  Put the source MAC address in the bridge table, if necessary, along with the frame ingress port and mark that entry “recently used”
  Remove any “stale” entries in the bridge table
MAC Addr
Last Seen on Port
Last Used
Bridge Table
002080 00324a
FastEthernet 1/4
12 sec ago
0003ba 51733a
FastEthernet 2/9
72 sec ago
. . .
. . .
. . .

## Slide 90: Something Is Still Missing
Now more than one message can be in transit at a time
But we've only talked about MAC addresses.
Where are the IP addresses?

## Slide 91: Layer 3 (IP) packets
IP addresses appear in the Ethernet frame payload, not the header
But Ethernet hardware only examines the MAC addresses in the Ethernet frame(!)
How do we connect these two layers?
Preamble
Destination MAC
Source MAC
802.1Q tag
Ether type/
Length
Payload
CRC
Interframe Gap
8
6
6
0-4
2
4
12
46-1500
Source IP
Destination
IP
Zero
Protocol
Length
Data
4
4
1
1
2
38-1492

## Slide 92: ARP
Address Resolution Protocol
Used with Ethernet to discover IP addresses
How?
  IP stack needs to send to IP address a, but doesn’t know what destination MAC address to use.
  Broadcast an ARP-request message: “Who has IP address a?”
  Wait on unicast ARP-response: “I have IP address a.”
  Store the response in a local ARP Table, discarding entries when they become stale.
  Use the corresponding entry in the ARP table to set the destination MAC address of the frame.

## Slide 93: ARP Table Example
% arp -anl
Neighbor Linklayer Address Expire(O) Expire(I) Netif Refs
192.168.0.69 f0:18:98:b:95:42 expired expired en0 1
192.168.0.79 4c:20:b8:a9:eb:80 1m21s 1m21s en0 1
192.168.0.84 e2:3c:4f:62:bd:11 8s 15s en0 1
192.168.0.85 ee:b3:0:a5:56:f1 32s 1m17s en0 1
192.168.0.87 14:7d:da:5a:c4:24 expired 2m2s en0 1
192.168.0.88 bc:d0:74:4e:88:98 expired 38s en0 1
192.168.0.92 24:f5:a2:ab:57:15 2m34s 2m34s en0 1
192.168.0.94 b8:27:eb:a:2b:15 expired expired en0 1
192.168.0.97 9c:50:d1:11:ca:a4 expired 1m59s en0 1
192.168.0.106 d6:7d:33:61:35:6a expired expired en0 2
192.168.0.109 24:f5:a2:ab:5e:b9 2m14s 2m14s en0 1
192.168.0.110 24:f5:a2:ab:5e:e1 2m18s 2m18s en0 1
192.168.0.111 f6:62:f6:80:d6:f1 56s 56s en0 1
192.168.0.113 ee:6a:e8:e6:67:cb 1m22s 1m29s en0 1
192.168.0.115 0:88:65:26:71:4b expired expired en0 1
192.168.0.118 8e:ab:c2:75:68:5b 41s 43s en0 1
192.168.0.127 ce:7c:cf:62:b0:3d expired expired en0 1
192.168.0.140 3c:7d:a:1:31:bc expired 56s en0 1
192.168.0.158 b6:68:3:e1:dc:39 expired expired en0 1
192.168.0.160 78:af:8:72:4c:37 expired 1m12s en0 1
192.168.0.163 d2:5e:70:43:c8:f6 expired expired en0 1
192.168.0.186 c2:2b:fd:ee:74:dc expired expired en0 1
192.168.0.254 d4:4:cd:4c:5f:f0 2m55s 2m55s en0 1

## Slide 94: VLANs
Virtual LAN, a.k.a. VLAN
  A group of hosts that can communicate as if they were attached to the same broadcast domain, regardless of their physical location.
  A VLAN has the same attributes as a physical LAN, but it allows for hosts to be grouped together even if they are not connected to the same network switch.
  Network reconfiguration can be done through software instead of physically relocating devices and wires.

## Slide 95: Geographic Addressing

## Slide 96: After VLANs
Each logical VLAN is like a separate physical bridge
Switch A
Green
VLAN
Black
VLAN
Red
VLAN
Switch A - 1st floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch B - 2nd floor
Green
VLAN
Black
VLAN
Red
VLAN
Each logical VLAN is like a separate physical bridge
VLANs can span across multiple switches
College of Engineering (red)
College of Computing (black)
Classroom network (green)

## Slide 97: How Do They Do It?
Remember that optional 802.1q tag in the Ethernet frame?
We fill that with a VLAN number 1-4095, i.e. “tag the frame”.
Each edge port is labeled with a VLAN number
Switches
  Tag each frame as it comes in
  Segregate traffic carrying identical VLAN tags
  Only output tagged traffic to edge ports carrying the same VLAN tag, removing the tags on egress
But that still doesn’t explain how switches communicate…

## Slide 98: VLAN Trunks
Switch communicate via 802.1q “trunks” (sometimes called VLAN multiplexing)
Trunks are inter-switch links that simply preserve the VLAN tags on links between switches
Trunks can be configured to carry one, several, or all VLANs from one switch to another
Each VLAN in a trunk uses up switch resources so GT convention is that trunks are configured to only carry necessary VLANs

## Slide 99: Trunking
End result:
  All the green ports appear in one broadcast domain (I.e. they appear to be on the same physical Ethernet)
  The red ports appear on a different broadcast domain
  And the black ports on a third broadcast domain
VLAN tags carried by ports and trunks are all configurable in software
Switch A - 1st floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch B - 2nd floor
Green
VLAN
Black
VLAN
Red
VLAN
Trunk
Trunk

## Slide 100: Other VLAN Trivia
For computers to communicate on a VLAN
  The switch has to be configured with the VLAN and the VLAN needs to be trunked between the switches that are to carry it.
  Each edge port in the VLAN must be assigned to the VLAN.
  Each must have an IP address and a subnet mask that is consistent for that VLAN. This is the same requirement as for a physically connected network.
Remember, just because two computers are physically connected to the same switch does not mean that they can communicate.
Devices on two separate networks must communicate via a router (Layer 3), whether or not VLANs are used.

## Slide 101: Broadcast Mischief
So what happens when someone sends a “broadcast” frame to one of our ports?
Switch A - 1st floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch C - 3rd floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch B - 2nd floor
Green
VLAN
Black
VLAN
Red
VLAN
Broadcast

## Slide 102: Making a Broadcast Storm
Disaster! Every broadcast lives forever!
Loops are not healthy
Switch A - 1st floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch C - 3rd floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch B - 2nd floor
Green
VLAN
Black
VLAN
Red
VLAN
Broadcast

## Slide 103: Spanning Tree to the Rescue
So how do we get rid of loops?
Spanning tree protocol (simplified here)
  Elect a root bridge (lowest priority, lowest MAC)
  Cascade BPDU frames starting from the root
  Based on the BPDUs they pass, each switch
    Chooses the lowest cost route to the root bridge
    Blocks any other ports that can get to the root
  Recalculate when links change state

## Slide 104: No More Loops
Spanning tree blocks the link marked with an X.
Only one copy of the broadcast frame will make it to each red port.
Switch A - 1st floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch C - 3rd floor
Green
VLAN
Black
VLAN
Red
VLAN
Switch B - 2nd floor
Green
VLAN
Black
VLAN
Red
VLAN
Broadcast

## Slide 105: Now let's look at the last layer
Ethernet standards allow use of several types of physical media
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model

## Slide 106: Ethernet physical media standards
Twisted pair copper (1m – 100m reach)
  10base-T 100base-T 1000base-TX – most common today 10Gbase-T
Fiber optic (100m – 40km reach)
  1000base-SX, 1000base-LX 10Gbase-SR, 10Gbase-LR 40Gbase-SR4, 40Gbase-LR4 100Gbase-SR4, 100Gbase-SR10, 100Gbase-LR4 400Gbase-SR4, 400Gbase-LR4 800Gbase-SR8, 800Gbase-LR8 – in development and many more

## Slide 107: Manchester encoding
Ethernet coax signaling uses Manchester encoding which is a scheme that guarantees at least one voltage transition during each clock tick
0 1 1 0 0 1 0 1 1

## Slide 108: What’s in a Home Router?

## Slide 109: Now let’s look above the top layer
Let’s look at the API used in Linux/Unix to access networks
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model

## Slide 110: Network socket programming
The server sets up what's often known as a "listener" that's bound to a specific destination port
The client makes a "connect" request to the listener
The listener "accepts" the connection
Now the client and server can send data back and forth using send/recv (or write/read) system calls
socket()
setsockopt()
bind()
listen()
accept()
send()/recv()
connect()
socket()
send()/recv()
Server
Client

## Slide 111: Example server
/* A simple server in the internet domain using TCP
The port number is passed as an argument */
#include <stdio.h>
#include <sys/types.h>
#include <sys/socket.h>
#include <netinet/in.h>
void error(char *msg)
{
perror(msg);
exit(1);
}
int main(int argc, char *argv[])
{
int sockfd, newsockfd, portno, clilen;
char buffer[256];
struct sockaddr_in serv_addr, cli_addr;
int n;
if (argc < 2) {
fprintf(stderr,"ERROR, no port provided\n");
exit(1);
}
sockfd = socket(AF_INET, SOCK_STREAM, 0);
if (sockfd < 0)
error("ERROR opening socket");
bzero((char *) &serv_addr, sizeof(serv_addr));
portno = atoi(argv[1]);
serv_addr.sin_family = AF_INET;
serv_addr.sin_addr.s_addr = INADDR_ANY;
serv_addr.sin_port = htons(portno);
if (bind(sockfd, (struct sockaddr *) &serv_addr,
sizeof(serv_addr)) < 0)
error("ERROR on binding");
listen(sockfd,5);
clilen = sizeof(cli_addr);
newsockfd = accept(sockfd, (struct sockaddr *) &cli_addr, &clilen);
if (newsockfd < 0)
error("ERROR on accept");
bzero(buffer,256);
n = read(newsockfd,buffer,255);
if (n < 0) error("ERROR reading from socket");
printf("Here is the message: %s\n",buffer);
n = write(newsockfd,"I got your message",18);
if (n < 0) error("ERROR writing to socket");
return 0;
}

## Slide 112: Example client
/* A simple client in the internet domain using TCP
The server and port number are passed as arguments */
#include <stdio.h>
#include <sys/types.h>
#include <sys/socket.h>
#include <netinet/in.h>
#include <netdb.h>
void error(char *msg) {
perror(msg);
exit(0);
}
int main(int argc, char *argv[]) {
int sockfd, portno, n;
struct sockaddr_in serv_addr;
struct hostent *server;
char buffer[256];
if (argc < 3) {
fprintf(stderr,"usage %s hostname port\n", argv[0]);
exit(0);
}
portno = atoi(argv[2]);
sockfd = socket(AF_INET, SOCK_STREAM, 0);
if (sockfd < 0)
error("ERROR opening socket");
server = gethostbyname(argv[1]);
if (server == NULL)
error("ERROR, no such host");
bzero((char *) &serv_addr, sizeof(serv_addr));
serv_addr.sin_family = AF_INET;
bcopy((char *)server->h_addr,
(char *)&serv_addr.sin_addr.s_addr,
server->h_length);
serv_addr.sin_port = htons(portno);
if (connect(sockfd,(struct sockaddr *)&serv_addr, sizeof(serv_addr)) < 0)
error("ERROR connecting");
printf("Please enter the message: ");
bzero(buffer,256);
fgets(buffer,255,stdin);
n = write(sockfd,buffer,strlen(buffer));
if (n < 0) error("ERROR writing to socket");
bzero(buffer,256);
n = read(sockfd,buffer,255);
if (n < 0) error("ERROR reading from socket");
printf("%s\n",buffer);
return 0;
}
Source: https://www.cs.rpi.edu/~moorthy/Courses/os98/Pgms/client.c

## Slide 113: Performance metrics
P1
Protocol
stack
Network
P2
Protocol
stack
S
R
Tw
msg
pkt1
pkt2
pktn
…
Tf
Transmission time or end-to-end latency = S+TW+Tf+R
Message throughput = message-size/end-to-end-latency
Processing overhead at sender
Processing overhead at receiver
Wire delay
Flight time
What determines Tw?
How long it takes to put the message on the network?
Tw = message-size/network-bandwidth
Ex: 21MB at 56Kb/sec
(21 * 220 * 8) / 56000
3146 seconds

## Slide 114: Performance metrics
P1
Protocol
stack
Network
P2
Protocol
stack
S
R
Tw
msg
pkt1
pkt2
pktn
…
Tf
Transmission time or end-to-end latency = S+TW+Tf+R
Message throughput = message-size/end-to-end-latency
Processing overhead at sender
Processing overhead at receiver
Wire delay
Flight time
What determines Tf?
Basically the speed of light in the transmission medium (~0.5c to 1c)
How far is it from P1 to P2?
Queuing delay is an additional term

## Slide 115: Performance metrics
P1
Protocol
stack
Network
P2
Protocol
stack
S
R
Tw
msg
pkt1
pkt2
pktn
…
Tf
Transmission time or end-to-end latency = S+TW+Tf+R
Message throughput = message-size/end-to-end-latency
Processing overhead at sender
Processing overhead at receiver
Wire delay
Flight time
What determines S & R?
The OS implementation of the protocol stack

## Slide 116: Timeline example
100 + 100 ms
Timeline of sender
Pkt0
Pkt1
Pkt2
Pkt3
Pkt4
Pkt5
Pkt6
Pkt7
Pkt8
Pkt9
Total time for the transmission to complete
100ms latency
10 packets
Window size = 5
Wire delay (data) = 0.5ms
Wire delay (ack) = ~0
Receiver & Sender overhead = ~0
0.5 ms
0 ms
0.5 ms
4 * 0.5 ms
Ack5
Ack6
Ack7
Ack8
Ack9
0 ms
End-to-end latency for Pkt0
= S + Tw + Tf + R
0 + 0.5 + 100 + 0
100.5 ms
End-to-end latency for Ack0
= S + Tw + Tf + R
0 + 0.0 + 100 + 0
100.0 ms
Total transmission time
= 0.5 + 100 + 100 + 0 + 0.5 + 100 + 100 + 0.5 + 0.5 + 0.5 + 0.5
0.5 + 200 + 0.5 + 200 + 4 * 0.5
402.5 ms
100 + 100 ms
Ack0
Ack1
Ack2
Ack3
Ack4

## Slide 117: Timeline example
100 + 100 ms
Timeline of sender
Pkt0
Pkt1
Pkt2
Pkt3
Pkt4
Pkt5
Pkt6
Pkt7
Pkt8
Pkt9
Total time for the transmission to complete
100ms latency
10 packets
Window size = 5
Wire delay (data) = 0.5ms
Wire delay (ack) = ~0
Receiver & Sender overhead = ~0
0.5 ms
0 ms
0.5 ms
4 * 0.5 ms
Ack0
Ack1
Ack2
Ack3
Ack4
0 ms
End-to-end latency for Pkt0
= S + Tw + Tf + R
0 + 0.5 + 100 + 0
100.5 ms
End-to-end latency for Ack0
= S + Tw + Tf + R
0 + 0.0 + 100 + 0
100.0 ms
Total transmission time
= 0.5 + 100 + 100 + 0 + 0.5 + 100 + 100 + 0 + 0.5 + 0.5 + 0.5 + 0.5
0.5 + 200 + 0.5 + 200 + 4 * 0.5
403 ms
100 + 100 ms
Ack5
Ack6
Ack7
Ack8
Ack9

## Slide 118: In the expression S + Tw + Tf + R
What does TW stand for?
Tw = window-size
Tw = message-size / network-bandwidth
Tw = distance-between-endpoints / 0.5 c
Tw = sender-overhead + receiver-overhead
None of the above
Today’s number is 10,000
120

## Slide 119: Acknowledgement example
Example
A transport protocol uses a window of 10 packets.
For a message that consists of 101 packets, how many acknowledgement packets does the destination generate?
Assume no packets are lost.
101

## Slide 120: Packets and payloads
What is the maximum size of the payload in an ICMP ECHO packet, given ethernet packet size of 1500 bytes and header size of 28 bytes?
1528 bytes
1472 bytes
1500 bytes
Cannot be determined with data given
130
1500-20-8 = 1472 bytes
Default ethernet max payload = 1500 bytes
IP header = 20 bytes
ICMP header = 8 bytes

## Slide 121: Back to the network layer
Why are we back here?
Recall, IP routing happens here
We didn’t answer a question.
How does a router know where to route (i.e. who sets up the routing table)?
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer
IP
Ethernet
TCP/UDP
ARP
1000baseSX
OSI Model

## Slide 122
router
router

## Slide 123: Network layer
Routing information protocols
  Link state protocols
  Distance vector protocols
  Hierarchical routing
Addressing

## Slide 124: Intuition behind routing algorithms (link state, distance vector)
What's the latency to get to your neighbor?

## Slide 125: Distance vector in action
Uses neighbor info, local algorithm (i.e. every node only sees its neighbors)
Each node knows the cost to each of its neighbors
Each node sends its idea of routing to each of its neighbors
Known colloquially as ”routing by rumor”
For every other node, each node determines the lowest cost next-hop
Algorithm runs simultaneously on every node
How does it work?
Node E knows its costs to its neighbors:
Routes from E | A | B | C | D | F
Cost/next hop | 5/A | 1/B | 3/C | ∞/ | 1/F

## Slide 126: Distance vector in action
Node E listens to messages from its neighbors:
  A says its routes are 0/A, 5/E, 2/B, 1/C, 4/D, 4/F
  B says its routes are 0/B, 1/E, 2/C, 2/A, 5/F, 4/D
  C says its routes are 0/C, 1/A, 2/D, 5/F, 3/E, 2/B
  F says its routes are 0/F, 5/C, 1/D, 1/E, 2/B, 4/A
  D isn't heard because it isn't connected to E
Node E looks at each route from each neighbor N; it adds its cost to get to N to N's cost to get to each other node.
For each node, if the sum is lower cost than what E has in its route table, E changes its own route to run through the neighbor
Reviewing node A's message
  5+2/B, 5+1/C, 5+4/D, 5+4/F
  Only 9/D is less
  We'll set the next hop to A
Routes from E | A | B | C | D | F
Cost/next hop | 5/A | 1/B | 3/C | ∞/ | 1/F

## Slide 127: Distance vector in action
Node E listens to messages from its neighbors:
  A says its routes are 0/A, 5/E, 2/B, 1/C, 4/D, 4/F
  B says its routes are 0/B, 1/E, 2/C, 2/A, 5/F, 4/D
  C says its routes are 0/C, 1/A, 2/D, 5/F, 3/E, 2/B
  F says its routes are 0/F, 5/C, 1/D, 1/E, 2/B, 4/A
  D isn't heard because it isn't connected to E
Node E looks at each route from each neighbor N; it adds its cost to get to N to N's cost to get to each other node.
For each node, if the sum is lower cost than what E has in its route table, E changes its own route to run through the neighbor
Reviewing Node B's message
  1+2/C, 1+2/A, 1+5/F, 1+4/D
  3/A and 5/D are lower cost
  We set their next hop to B
Routes from E | A | B | C | D | F
Cost/next hop | 5/A | 1/B | 3/C | 9/A | 1/F

## Slide 128: Distance vector in action
Node E listens to messages from its neighbors:
  A says its routes are 0/A, 5/E, 2/B, 1/C, 4/D, 4/F
  B says its routes are 0/B, 1/E, 2/C, 2/A, 5/F, 4/D
  C says its routes are 0/C, 1/A, 2/D, 5/F, 3/E, 2/B
  F says its routes are 0/F, 5/C, 1/D, 1/E, 2/B, 4/A
  D isn't heard because it isn't connected to E
Node E looks at each route from each neighbor N; it adds its cost to get to N to N's cost to get to each other node.
For each node, if the sum is lower cost than what E has in its route table, E changes its own route to run through the neighbor
Reviewing Node C's message
  3+1/A, 3+2/D, 3+5/F, 3+2/B
  None are lower cost
Routes from E | A | B | C | D | F
Cost/next hop | 3/B | 1/B | 3/C | 5/B | 1/F

## Slide 129: Distance vector in action
Node E listens to messages from its neighbors:
  A says its routes are 0/A, 5/E, 2/B, 1/C, 4/D, 4/F
  B says its routes are 0/B, 1/E, 2/C, 2/A, 5/F, 4/D
  C says its routes are 0/C, 1/A, 2/D, 5/F, 3/E, 2/B
  F says its routes are 0/F, 5/C, 1/D, 1/E, 2/B, 4/A
  D isn't heard because it isn't connected to E
Node E looks at each route from each neighbor N; it adds its cost to get to N to N's cost to get to each other node.
For each node, if the sum is lower cost than what E has in its route table, E changes its own route to run through the neighbor
Reviewing Node F's message
  1+5C, 1+1/D, 1+2/B, 1+4/A
  2/D is lower cost
  We'll set the next hop to F
Routes from E | A | B | C | D | F
Cost/next hop | 3/B | 1/B | 3/C | 5/B | 1/F

## Slide 130: Distance vector in action
Node E listens to messages from its neighbors:
  A says its routes are 0/A, 5/E, 2/B, 1/C, 4/D, 4/F
  B says its routes are 0/B, 1/E, 2/C, 2/A, 5/F, 4/D
  C says its routes are 0/C, 1/A, 2/D, 5/F, 3/E, 2/B
  F says its routes are 0/F, 5/C, 1/D, 1/E, 2/B, 4/A
  D isn't heard because it isn't connected to E
Node E looks at each route from each neighbor N; it adds its cost to get to N to N's cost to get to each other node.
For each node, if the sum is lower cost than what E has in its route table, E changes its own route to run through the neighbor
Do you agree that E now knows the next hop for the lowest cost routes to the other nodes?
This of course presumed the other nodes knew their lowest cost routes
When this runs on all nodes simultaneously, they will converge on this solution in a relatively short time
Routes from E | A | B | C | D | F
Cost/next hop | 3/B | 1/B | 3/C | 2/F | 1/F

## Slide 131: Distance Vector vs Link State
Distance Vector
  Each node knows the cost to reach each of its neighbors
  Each node sends its routing table to only its neighbors
  Each node revises its own routing table every time it receives a routing table from a neighbor
Link State
  Each node advertises its neighbor links and costs to every other node in the network
  Each node collects the entire topology of the network from these advertisements
  Using a “shortest path” algorithm, each node calculates its own routing table

## Slide 132: Link state in action
Dijkstra's shortest path algorithm
Uses global info, local algorithm (i.e. every node has this graph)
n-1 iterations
One least-cost route to a destination
Runs simultaneously on each node
Iteration Count | Nodes to which least-cost routes known | B Cost/ route | C Cost/ route | D cost/ route | E Cost/ route | F Cost/ route
Init | A | 2/AB | 1/AC | 4/AD | 5/AE | ∞
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Calculating on Node A
(each node does its own calculation)

## Slide 133: Link state in action
Dijkstra's shortest path algorithm
Uses global info, local algorithm (i.e. every node has this graph)
n-1 iterations
One least-cost route to a destination
Runs simultaneously on each node
Iteration Count | Nodes to which least-cost routes known | B Cost/ route | C Cost/ route | D cost/ route | E Cost/ route | F Cost/ route
Init | A | 2/AB | 1/AC | 4/AD | 5/AE | ∞
1 | A,C | 2/AB | 1/AC | 3/ACD | 4/ACE | 6/ACF
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Calculating on Node A
(each node does its own calculation)

## Slide 134: Link state in action
Dijkstra's shortest path algorithm
Uses global info, local algorithm (i.e. every node has this graph)
n-1 iterations
One least-cost route to a destination
Runs simultaneously on each node
Iteration Count | Nodes to which least-cost routes known | B Cost/ route | C Cost/ route | D cost/ route | E Cost/ route | F Cost/ route
Init | A | 2/AB | 1/AC | 4/AD | 5/AE | ∞
1 | A,C | 2/AB | 1/AC | 3/ACD | 4/ACE | 6/ACF
2 | A,C,B | 2/AB | - | 3/ACD | 3/ABE | 6/ACF
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Calculating on Node A
(each node does its own calculation)

## Slide 135: Link state in action
Dijkstra's shortest path algorithm
Uses global info, local algorithm (i.e. every node has this graph)
n-1 iterations
One least-cost route to a destination
Runs simultaneously on each node
Iteration Count | Nodes to which least-cost routes known | B Cost/ route | C Cost/ route | D cost/ route | E Cost/ route | F Cost/ route
Init | A | 2/AB | 1/AC | 4/AD | 5/AE | ∞
1 | A,C | 2/AB | 1/AC | 3/ACD | 4/ACE | 6/ACF
2 | A,C,B | 2/AB | - | 3/ACD | 3/ABE | 6/ACF
3 | A,C,B,D | - | - | 3/ACD | 3/ABE | 4/ACDF
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
Calculating on Node A
(each node does its own calculation)

## Slide 136: Link state in action
Calculating on Node A
(each node does its own calculation)
Dijkstra's shortest path algorithm
Uses global info, local algorithm (i.e. every node has this graph)
n-1 iterations
One least-cost route to a destination
Runs simultaneously on each node
Iteration Count | Nodes to which least-cost routes known | B Cost/ route | C Cost/ route | D cost/ route | E Cost/ route | F Cost/ route
Init | A | 2/AB | 1/AC | 4/AD | 5/AE | ∞
1 | A,C | 2/AB | 1/AC | 3/ACD | 4/ACE | 6/ACF
2 | A,C,B | 2/AB | - | 3/ACD | 3/ABE | 6/ACF
3 | A,C,B,D | - | - | 3/ACD | 3/ABE | 4/ACDF
4 | A,C,B,D,E | - | - | - | 3/ABE | 4/ACDF
5 | A,C,B,D,E,F | - | - | - | - | 4/ACDF

## Slide 137: A host using link state routing protocol
Knows only about the routes of its neighbors
Knows the topology of the entire local network
Uses a breadth-first search to calculate distances to other hosts
Uses less CPU time than a distance vector protocol host would
140

## Slide 138: Hierarchical routing algorithms
Network of networks
Very large scale, frequent state changes
Compartmentalize so routing information protocol issues don't spread and cause widespread outages
What better example than the Internet itself!
Autonomous Systems (AS)
  It is a collection of IP routing prefixes under the control of common administrative policy that presents a common, clearly defined routing policy to the internet.
  Gateway nodes connect to other AS gateway nodes for inter-AS routing

## Slide 139: Hierarchical routing algorithms
Gateway nodes use BGP to interconnect Autonomous Systems
Nodes within an AS use LS or DV or some other routing protocol
We use BGP as the internet inter-AS routing protocol
ASs are assigned numbers by IANA/ARIN
Nodes within an AS use LS or DV (or other) routing protocol

## Slide 140: Border Gateway Protocol (BGP)
BGP is a path-vector protocol. (We’re not going into much detail about that.)
The gateway routers send path-vector messages to advertise the reachability of networks.
Each router that receives a path vector message must verify the advertised path according to its policy.
If the message is compliant, the router modifies its routing table and the message before sending the message to the next neighbor.
  It modifies the routing table to maintain the autonomous systems that are traversed in order to reach the destination system.
  It modifies the message to add its AS number and to replace the next router entry with its identification.

## Slide 141: Routing at GT
The GT campus network is AS 2367
There are two Juniper routers that function as Gateway Routers and run BGP
The rest of the campus network runs OSPF (a link-state protocol)

## Slide 142: Remember this slide?
Now consider an email from Joe to his grandmother
Atlanta
Yuba City, CA
Atlanta
Sacramento
So just where is this so-called “core”

## Slide 143: There really is no internet core …
Instead there are dozens of Internet Exchange Points (IXPs) where groups of Internet Service Providers (ISPs) interconnect their networks

## Slide 144: There really is no internet core …
The ISPs peer using BGP such that all the gateway routers know multiple routes to every regional ISP
You can begin to see that the Internet has a highly distributed ”core” created by multiple IXPs
There are at least four IXPs in Atlanta; GT participates in and operates an ISP, SoX, which provides network access for about 3 dozen southeastern universities and research centers
The diagram on the next page shows just the IXPs in which SoX participates. Note that traffic is allowed to traverse SoX networks to get from one ISP to another.
The diagram doesn’t show the SoX peering with other entities such as Google, AT&T, NASA, Dept of Energy, and Comcast

## Slide 146: Reviewing Internet Addressing
Recall IP addressing
  A network part
  A host part
What do we need to tell how many networks are in this diagram?
We need a mask of course
If you know that the mask is /24 or 255.255.255.0, how many IP networks are present?
There are three with the network numbers 128.61.22.0/24, 128.61.21.0/24, and 128.61.23.0/24

## Slide 147: Where is the core of the internet located?
Washington, DC
Stanford University, Palo Alto, CA
Columbia University, New York City
Salt Lake City, UT
Not any one place
150

## Slide 148: Network Layer Summary
Network Terminology | Definition/Use
Circuit switching | A network layer technology used in telephony. Reserves the network resources (link bandwidth in all the links from source to destination) for the duration of the call; no queuing or store-and-forward delays
Packet switching | A network layer technology used in wide area Internet. It supports best effort delivery of packets from source to destination without reserving any network resources en route.
Message switching | Similar to packet switching but at the granularity of the whole message (at the transport level) instead of packets.
Switch/Router | A device that supports the network layer functionality. It may simply be a computer with a number of network interfaces and adequate memory to serve as input and output buffers.
Input buffers | These are buffers associated with each input link to a switch for assembling incoming packets.
Output buffers | These are buffers associated with each outgoing link from a switch if in case the link is busy.
Routing table | This is table that gives the next hop to be used by this switch for an incoming packet based on the destination address. The initial contents of the table as well as periodic updates are a result of routing algorithms in use by the network layer.

## Slide 149: Network Layer Summary
Network Terminology | Definition/Use
Delays | The delays experienced by packets in a packet-switched network
Store and forward | This delay is due to the waiting time for the packet to be fully formed in the input buffer before the switch can act on it.
Queuing | This delay accounts for the waiting time experienced by a packet on either the input or the output buffer before it is finally sent out on an outgoing link.
Packet loss | This is due to the switch having to drop a packet due to either the input or the output buffer being full and is indicative of traffic congestion on specific routes of the network.
Service Model | This is the contract between the network layer and the upper layers of the protocol stack. Both the datagram and virtual circuit models used in packet-switched networks provide best effort delivery of packets.
Virtual Circuit (VC) | This model sets up a virtual circuit between the source and destination so that individual packets may simply use this number instead of the destination address. This also helps to simplify the routing decision a switch has to make on an incoming packet. (ATM and X.25)
Datagram | This model does not need any call setup or tear down. Each packet is independent of the others and the switch provides a best effort service model to deliver it to the ultimate destination using information in its routing table. (IP)

## Slide 150: Summary
Sockets, http
RPC
TCP
TCP
IP
Ethernet
Wired, wireless hardware
Data
Data
Data
Segments
Packets
Frames
Bits
Application
Network Process to Application
Presentation
Data Representation
and Encryption
Session
Interhost Communication
Transport
End-to-End Connections
and Reliability
Network
Path Determination
and IP (Logical Addressing)
Data Link
MAC and LLC
(Physical addressing)
Physical
Media, Signal, and
Binary Transmission
7
6
5
4
3
2
1
Data
Layer

## Slide 151: A brief history of electronic communication
You won't be responsible for the following slides, but you may find them interesting
Wikipedia is a great place to look for more detail on these events
Credit goes to Prof. Kishore Ramachandran for providing them

## Slide 152: From Telephony to Computer Networking
1875 Telephone invented…analog system
1960 Telephone infrastructure goes digital

## Slide 153: From Telephony to Computer Networking
1940's Mainframe computers developed
1960's Transition
  Batch-oriented card-input/output
  CRT I/O and timesharing

## Slide 154: From Telephony to Computer Networking

## Slide 155: From Telephony to Computer Networking
EXTRA!!!!!
1960 AT&T
INTRODUCES
DATAPHONE
First Commercial
Modem!
Short for Modulator/Demodulator

## Slide 156: From Telephony to Computer Networking
1968/9 Carterphone decision allowed devices which were beneficial and not harmful to the network to be connected to the Public Switched Telephone Network (PSTN).
Allowed non-Bell system equipment to be connected and paved the way for computers to communicate using the telephone switching infrastructure.

## Slide 157: Evolution of the Internet
1965 DoD DARPA plans first computer network
1969 ARPANET connects 4 computers using packet switched network
  Stanford Research Institute, UCLA, UC Santa Barbara, and the University of Utah
  Networking luminary Leonard Kleinrock, is credited with successfully sending the first network "message" from UCLA to Stanford.

## Slide 158: Evolution of the Internet
"Router" in the network was called Interface Message Processor (IMP), built by a company called BBN (which stands for Bolt, Beranak, and Newman Inc.).
  IMP system architecture required a careful balance of the hardware and software that would allow it to be used as a store-and-forward packet switch among these computers.
  IMP's used modems and leased telephone lines to connect to one another.
1971 The ARPANET grows to 23 hosts connecting universities and government research centers around the country.

## Slide 159: Evolution of the Internet
1973 Robert Metcalfe and David Boggs invent the Ethernet networking system at the Xerox Palo Alto Research Center.

## Slide 160: Evolution of the Internet
1973 The ARPANET goes international

## Slide 161: Evolution of the Internet
1975 Internet operations transferred to the Defense Communications Agency
1978 Hayes Microcomputer Products releases the first mass-market modem, transmitting at 300 bps (0.3K).
1980 John Shoch at Xerox creates the first "worm" program, with the capacity to travel through networks.
1981 Ungermann-Bass ships the first commercial Ethernet network interface card.

## Slide 162: Evolution of the Internet
1981 ARPANET has 213 hosts. A new host is added approximately once every 20 days.
1982 The term 'Internet' is used for the first time.
1983 TCP/IP becomes the universal language of the Internet. Developed by Vinton Cerf and Robert Kahn
1984 CISCO founded
Early 80's Unix and IBM OS included TCP/IP

## Slide 163: Evolution of the Internet
Late 90's Internet becomes household term
  Needed PC
  Needed "Killer app" i.e. WWW & browsers

## Slide 164: PC and the arrival of LAN
1971 Intel introduces the first microprocessor - the Intel 4004.
1971 The Kenbak-1, the first microcomputer, is introduced in Scientific American, selling a total of 40 units in 2 years.
  Used 130 IC's with a 256 byte memory and 8-bit words, processed 1000 instructions per second, and cost $750.

## Slide 165: PC and the arrival of LAN
1972 Intel launches the 8-bit 8008 - the first microprocessor which could handle both upper and lowercase characters.
1972 Xerox develops the Xerox Alto - the first computer to use a Graphic User Interface.
The Alto consists of four major parts: the graphics display, the keyboard, the graphics mouse, and the disk storage/processor box. Each Alto is housed in a beautifully formed, textured beige metal cabinet that hints at its $32,000 price tag (1979US money). With the exception of the disk storage/processor box, everything is designed to sit on a desk or tabletop

## Slide 166: PC and the arrival of LAN
1974 Intel introduces the 8080 microprocessor
  5 times faster than the 8008.
  And the heart of the future Altair 8800.
1975 MITS markets the Altair 8800 - the first mass-market microcomputer, launching the Personal Computer Revolution.
1975 Bill Gates and Paul Allen form the Microsoft company to create software for the new Altair 8800.

## Slide 167: PC and the arrival of LAN
1976 Apple Computer is formed by Steve Jobs, Steve Wozniak, and Ron Wayne, and launches the Apple Computer.
1977 Tandy Radio Shack ships its first personal computer - the TRS-80. It sells over 10,000 units, tripling expectations.
1977 Apple Computer launches the Apple II, which sets new standards for sophisticated personal computer systems.

## Slide 168: PC and the arrival of LAN
1978 The C programming language is completed at AT&T Bell Laboratories, offering a new level of programming.
1978 Apple and Tandy ship PCs with 5.25" floppy disks, replacing cassette tape as the standard storage medium for PCs.
1978 Hayes Microcomputer Products releases the first mass-market modem, transmitting at 300 bps (0.3K).

## Slide 169: PC and the arrival of LAN
1978 Intel ships the Intel 8086 microprocessor, with 29,000 transistors, and running at 4.77 megahertz.
1979 Personal Software creates VisiCalc for the Apple II, the first electronic spreadsheet program, selling over 100,000 copies.
1979 Intel develops the 8088 microprocessor, which would later become the heart of the IBM PC.

## Slide 170: PC and the arrival of LAN
1979 Motorola develops the Motorola 68000 microprocessor, offering a new level of processing power.
1979 Robert Metcalf founded 3COM
1980 Seagate Technology introduces the first microcomputer hard disk, capable of holding 5 megabytes of data.
1980 Philips introduces the first optical laser disk, with many times the storage capacity of floppy or hard disks.

## Slide 171: PC and the arrival of LAN
1980 Xerox creates Smalltalk - the first object-oriented programming language.
1981 Ungermann-Bass ships the first commercial Ethernet network interface card.
1981 Xerox introduces the Xerox Star 8010, the first commercial Graphic User Interface computer, for $16,000-$17,000.

## Slide 172: PC and the arrival of LAN
1981 Microsoft supplies IBM with PC-DOS (which it would also sell as MS-DOS), the OS that would power the IBM PC.
1981 IBM brings to market the IBM PC, immediately establishing a new standard for the world of personal computers.

## Slide 173: Evolution of LAN
Thicknet
  Coaxial cable/Vampire taps
  10base5 (10 Mbits/sec, baseband, 500 meters)
  1979-1985

## Slide 174: Evolution of LAN
Thinnet
  Coaxial cable/BNC connectors
  10base2 (10 Mbits/sec, baseband, 200 meters)
  1985-1993

## Slide 175: Evolution of LAN
Fast Ethernet
  Move "ethernet" into the box
  100baseT (T for twisted pair)
  RJ45 Connectors