## Slide 1: Processor
CS 2200 Fall 2023

## Slide 2: Meet Someone New Around You
Exchange with each other …
  Name
  Major
  Year
  Where you are from?
  Who or what inspires you the most? Why?
You have 5 minutes.

## Slide 3: Meet Today's Attendance Quiz
Look on Canvas in Assignments for
  Attendance Quiz 8-22 (for practice)
You can take it during the lecture
You'll find the answers in the lecture
You might need this number: 49,283

## Slide 4: Moving forward
Instruction set design from HLL constructs
  Expressions, assignments => ALU instructions
  Data abstraction => Addressing modes
  Conditional & loop statements => Branch inst
  Procedure calls/returns => stack management
Please note the reading assignments in the schedule: Today you should have started chapter 2

## Slide 5: Simple Machine Model
Processor
Memory
Devices
Remember the LC-3? It used a greatly simplified ARM instruction set
Now we'll be introducing the LC-2200 which is a greatly simplified MIPS instruction set
So prepare yourself for an architecture that's similar, but not the same as the LC-3.

## Slide 6: Simple Machine Model
Processor
Memory
Devices
Let's consider the execution of a HLL
a = a + 1 c = a + b if (c == d) { … }

## Slide 7: How to Design an Instruction Set?
Start thinking like a compiler writer
  What instructions are needed for each HLL construct?
Processor
Memory
Devices

## Slide 8: Arithmetic/Logical Expressions
Start thinking like a compiler writer
   What instructions are needed for each HLL construct?
  c = a + b
  becomes
  add c, a, b
  memory operands
  memory addressing mode
What do you call these?
Where are they?
Processor
Memory
Devices

## Slide 9: Arithmetic/Logical Expressions
Start thinking like a compiler writer
   What instructions are needed for each HLL construct?
  c = a + b  add c, a, b
  Keep adding to repertoire
  c = a – b  sub c, a, b
  c = !(a & b)  nand c, a, b
Processor
Memory
Devices

## Slide 10: Arithmetic/Logical Expressions
Start thinking like a compiler writer
   What instructions are needed for each HLL construct?
  c = a + b  add c, a, b
Processor
Memory
Devices
Is there a downside to operands in memory?
A trip to memory is EXPENSIVE!
How can we address that?

## Slide 11: Operands?
Processor
Memory
Devices
ALU
Registers
  c = a + b  add c, a, b
  How about Load/Store instructions?
  ld r1, a
  st c, r2
Is this different from LC3?

## Slide 12: Load/Store Instructions
Processor
Memory
Devices
ALU
Registers
  ld r1, a
  st c, r2
  We’ve got operands in registers
  Register addressing mode!
  So how do we compile c = a + b now?

## Slide 13: Register Operands
Processor
Memory
Devices
ALU
Registers
  Old way:
  add c, a, b
  New way:
  ld r1, a
  ld r2, b
  add r3, r1, r2
  st c, r3

## Slide 14: Compiling with Register Operands
Processor
Memory
Devices
ALU
Registers
  Old way:
  add c, a, b 1 instruction
  New way:
  ld r1, a
  ld r2, b
  add r3, r1, r2
  st c, r3
This looks dumb!
4 instructions
Not really. Why?
We can re-use the values in registers!

## Slide 15: Keep Frequently Used Tools Nearby!
http://search.coolclips.com/m/vector/vc017870/Businesswoman-of-many-trades/

## Slide 16: Reusing Values
Processor
Memory
Devices
ALU
Registers
  c = a + b
  d = a * b + c
  if (c == d) {
  …
  }
With operands left in registers, we can save three memory accesses here!

## Slide 17: Question
Why would we consider loading values into registers before computing with them? Doesn’t that use more instructions?
Yes it does, but it doesn’t matter how many instructions it takes.
No it doesn’t. You counted wrong.
Yes it does, but it saves memory accesses because we can re-use the values
Yes it does and it’s a terrible design trade-off.
Today’s number is 49,283
10

## Slide 18: Structs in HLL
struct { int b; int c; } a;
Elements of a struct are contiguous in memory
How do we load a.b and a.c into registers?
Let’s say &a is already in register r1
MEMORY
b
c
a
100
104

## Slide 19: Accessing Struct Members
struct { int b; int c; } a;
Let’s say &a is already in register r1
To load a.b: R2 <- memory[R1+0]
To load a.c: R3 <- memory[R1+4]
MEMORY
b
c
a
100
104

## Slide 20: Base + Offset Address Mode
struct { int b; int c; } a;
Let’s say &a is already in register r1
ld ri, offset(rbase)
To load a.b & a.c:
ld r2, 0(r1) ld r3, 4(r1)
MEMORY
b
c
a
100
104

## Slide 21: Review Questions
An instruction set…
  Serves as a level of abstraction between software and hardware
  Provides the details of the machine implementation
  Deals with the datapath and control of the processor
  None of the above
20

## Slide 22: Review Questions
Addressing mode…
  Refers to the kinds of opcodes supported in an architecture
  Refers to the way the operands are specified in an instruction
  Refers to the granularity of the memory element that can be addressed in an instruction
  Refers to the datapath width
  None of the above
30

## Slide 23: Operand Granularity
char  8 bits  byte short  16 bits  half word int  32 bits*  word long  64 bits*
*depends on the word size of the architecture: int=16,long=32 and others can happen
We need some instruction variants:
ldb, ldh, ldl, … store & ALU instructions are similar

## Slide 24: Operand Alignment
struct { char a; char b[3]; } s;

## Slide 25: Dense Packing
b[2]
a
b[0]
b[1]
103 102 101 100
struct { char a; char b[3]; } s;
• We’re packing operands to save space.
• ISA may support ld/st with different precision!

## Slide 26: A Different Struct
struct { char a; int b; } s;
If we have a 32-bit path to memory, how are we going to load b?
100
104
a
blsb
bmsb
b…
b…
+0
+1
+2
+3

## Slide 27: Why Alignment Rules Matter
struct { char a; int b; } s;
This is one of many space/time tradeoffs that ISA designers must address.
100
104
a
blsb
bmsb
It’s OK to waste this space
b…
b…
+0
+1
+2
+3
Now, how to load s.b is obvious

## Slide 28: Accessing Array Operands
.
.
.
.
100
104
108
112
128
132
a[0]
a[1]
a[2]
a[3]
a[7]
a[8]
.
.
.
.
int a[100];
One approach, use base+offset
r1 = 100; // i.e. r1 = a;
To load a[8]
ld r8, 32(r1)
Is this the best we can do?

## Slide 29: Typical Array Use
• How do we typically use arrays?
loop c[i] = a[i] … i = i + 1 end loop
• Looks like it’s time for a new addressing mode
• Let’s implement base+index addressing
Very often, our subscript is a variable!

## Slide 30: Accessing Array Operands
.
.
.
.
100
104
108
112
128
132
a[0]
a[1]
a[2]
a[3]
a[7]
a[8]
.
.
.
.
int a[100];
With base+index mode
r1 = 100 r2 = i * 4
To load a[8]
ld r8, r2(r1)
Using base + index
Why?

## Slide 31: Endianness
Say we have a 32-bit register, R1, that contains the value 1 in twos-complement.
We store that register in an (aligned) memory location
ST R1,Mem[100]
The value is stored in addresses 100-103 (of course).
Which byte contains the 1? (The other 3 will be zero, right?)
100
101
102
103
Or this one?
This one?

## Slide 32: Endianness
Tip: Endianness often shows up in byte-addressable memories because we can lift single bytes out of longer data types
Little Endian  addresses the LSB of the word
int b = 0x11223344;
Big Endian  addresses the MSB of the word
100
104
a
blsb
bmsb
b…
b…
+0
+1
+2
+3
11
22
33
44
44
33
22
11

## Slide 33: So What’s the Difference
The difference shows up when taking a “word” apart (in this case, loading 8 bits from a 32-bit integer)
ldb r1, Mem[104]
Big Endian  loads 0x11 into r1
Little Endian  loads 0x44 into r1
100
104
a
b…
b…
b…
b…
+0
+1
+2
+3
11
22
33
44

## Slide 34: So What’s the Difference
• The difference shows up when taking a word apart
• Let’s store 0x11223344 (a 32-bit integer) at location 104
b…
b…
b…
b…
104
105
106
107
11
22
33
44
 | # of Bits Loaded | Little Endian Result Value | Big Endian Result Value
ldb r1, Mem[104] | 8 | 0x44 | 0x11
ldh r1, Mem[104] | 16 | 0x3344 | 0x1122
ldw r1, Mem[104] | 32 | 0x11223344 | 0x11223344
44
33
22
11
Big Endian
Little Endian
Note that when we load the same number of bits as in the original data type, there is no difference in result!

## Slide 35: So, about the LC-3
Was it Big Endian or Little Endian?
Think carefully…
There’s no way to tell!
There are no instructions that manipulate more or fewer than 16 bits
Thus, there is no way to see (or exploit) this implementation detail!
Was this accidental or on purpose?

## Slide 36: Recap
Software | Hardware
Expressions & assignments | ALU instructions
Variable reuse | register addressing mode ld/st instructions
Data abstraction • struct • array | base + offset addr mode base + index addr mode
Granularity of operands | ldb/ldh/ldw instructions addressability (byte, word)
Packing operands | Memory alignment (space/time tradeoff)
Endianness 0x11223344 | Little (first byte is 0x44) / Big (first byte is 0x11)

## Slide 37: Review Questions
Endianness of an architecture…
  Is a key determinant of processor performance
  Is a key determinant of how the compiler lays out data structures in memory
  Matters if one declares a datatype of a particular precision and accesses it as another precision
  Has to do with the end of the semester party for completing this course
  None of the above
  Today’s number is 29,291
40

## Slide 38: What do we need for…
Conditional statements
Switch statements
Loops
Procedure calls
Other considerations for ISA

## Slide 39: Compiling Conditional Statements
In what order are program statements normally executed?
How do we know what instruction to execute next?
How can we handle this type high-level language construct:
if(x == y) z = 7;

## Slide 40: What Do We Need to Do?
Evaluate predicate
Break the sequential flow of instructions
Rejoin control path
Predicate
if part
else part
true
false

## Slide 41: Implementing a Conditional
Evaluate predicate
  ALU Op
Break sequential flow
  Need to know where we are
     PC
  Need a new instruction
     BEQ r1, r2, offset
    if r1 == r2 then PC = PC + offset else do nothing
     PC relative addressing mode!

## Slide 42: Implementing a Conditional
Evaluate predicate
  ALU Op
Break sequential flow
  Need to know where we are
     PC
  Need a new instruction
    BEQ r1, r2, offset
Rejoin control flow
   need an unconditional jump

## Slide 43: An Example
C
  if(a == b)
  c = d + e;
  else
  c = f + g;
Assembly
  beq r1, r2, then
  add r3, r6, r7
  beq r1, r1, skip*
  then add r3, r4, r5
  skip …
  * Effectively an unconditional branch
Assuming
r1 = a
r2 = b
r3 = c
r4 = d
r5 = e
r6 = f
r7 = g

## Slide 44: Upshot of Conditional Statements
Introduction of PC
One new instruction BEQ r1, r2, offset
One new addressing mode: PC-relative
(optional) an Unconditional Jump J rn ; PC <- rn
Do we really need an unconditional jump??

## Slide 45: Compiling Switch Statements
if (n==0)
x=a;
else if (n==1)
x=b;
else if (n==2)
x=c;
else
x=d;
switch (n) {
case 0:
x=a;
break;
case 1:
x=b;
break;
case 2:
x=c;
break;
default:
x=d;
}
Do these produce
essentially equivalent
assembly code?
They can, but they don’t have to!

## Slide 46: Switch Can Use a Jump Table
Code for
Case 0
Code for
Case 1
Code for
Case 2
….
….
…
…
J
…
…
J
…
…
J
Jump table
Address for
Case 0
Address for
Case 1
Address for
Case 2
…….
…….
…….
Think of a C array of pointers to the individual cases
To do this we need an indirect addressing mode
  J @r1
 PC <- Mem[r1]

## Slide 47: Loops
Do we need anything new in the ISA?
Not really.

## Slide 48: Compiling Loops
C
  while(j ! = 0)
  {
  /* loop body */
  t = t + a[j--];
  }
Assembly
  loop beq r1,r0,done
  ; loop body
  …
  beq r0, r0, loop
  done …

## Slide 49: Summary
Software | Hardware
Expressions & assignments | ALU instructions, LD/ST instructions
Data abstraction • struct • array | register addr mode base + offset addr mode base + index addr mode
Conditionals & Loops | PC-relative addr mode branch/jump instruction (register or PC-relative) Indirect addr mode (optional)

## Slide 50: How Do We Compile Function Calls?
int main() int foo(formal-parameters)
{ {
<decl local-variables> <decl local-variables>
return-value = foo(actual-parms); /* code for function foo */
/* continue upon return(<value>);
* returning from foo }
*/
}
State of Caller
Pass parameters Remember return addr Jump to procedure
Allocate space for local vars
Pass result to caller Return to caller
Caller
Callee
Save the result
Continue the program

## Slide 51: Remembering the Return Address
Have we needed to do this before?
Add a Jump & Link instruction
  JALR rtarget, rlink ; rlink <= PC, PC <= rtarget
Recall J rtarget ; PC <= rtarget
Do we need this instruction any more?

## Slide 52: Control Flow
main() {
.
.
foo();
.
.
}
foo() {
}
Call
Return
JALR rtarget, rlink

## Slide 53: Control Flow
main() {
.
.
foo();
.
.
}
foo() {
}
Call
Return
Save state (before)
Restore state (after)
 Pass in parameters
 Return result

## Slide 54: Another Way to Save State
Register
set
Shadow
Register
set
Save prior to Procedure call
Restore upon Procedure return

## Slide 55: Shadow Register Sets
Register
set
Shadow
Register
set 1
Shadow
Register
set 2
Shadow
Register
set 3
Shadow
Register
set 4
……..
foo
bar
baz
….
foo() calls bar() who calls baz(), etc.
The Big Deal: No memory accesses! (but we need lots of extra registers)
Another form of this is called register renaming

## Slide 56: Saving State
If we don’t have shadow registers, where are we going to save all that state?
(Cue drum roll!)
A stack (Cue cymbal crash!)
Where are we going to put the stack?
In memory
But in small cases, could we hold the state in a few extra registers? (another space/time tradeoff)

## Slide 57: Use a Stack to Communicate
main() {
.
.
foo();
.
.
}
foo() {
}
Save/restore state
Pass parameters
Return results
What else is needed in ISA?
Nothing new..

## Slide 58: Saving Registers During a Procedure
We can have the caller save all the registers -or- We can have the callee save all the registers
What's wrong with those choices?
Right! Not everything needs to be saved every time…

## Slide 59: Saving Registers During a Procedure
If we split the assignment of the registers, then most of the time, the caller and callee can each save fewer registers based on what they actually need to use
In the LC-2200 case, we'll functionally divide the working register set
  s0-s2 registers which the callee must preserve if it wants to use them
  t0-t2 registers which the caller must preserve if it wants their values to persist over a function call
This division of responsibility saves memory accesses.

## Slide 60: Stack as Communication Area
Saving/restoring state over a procedure call
Who does it?
 Split between Caller and Callee

## Slide 61: Stack as Communication Area
Returning results
Do we really need to put them on the stack?
 Use registers (We'll call this register v0)

## Slide 62: Stack as Communication Area
Parameter Passing
Do we really need to put them on the stack?
 Use registers (We'll call these registers a0-a2)

## Slide 63: Your action items for this week
Homework 1 (due next Tuesday)
Project 1 (due in less than 3 weeks)
Attendance Quizzes 8-25 and 8-27
Make sure you have read Chapter 2 in R&L
You should be well into Chapter 3 by this time next week

## Slide 64: Stack as Communication Area
Will we need the stack at all for parameters and results?
What if we run out of registers?
We use the stack if we run out
Here we're trading time for complexity

## Slide 65: Moral of the Story
Use the stack sparingly
  LD/ST instructions are expensive (i.e. memory access is slow)
Software calling convention
  Used by the compiler to keep track of the use of the stack and registers
  Better have one!

## Slide 66: Software Convention for LC-2200
  Registers s0-s2 are the caller's s registers
  Registers t0-t2 are the temporary registers
  Registers a0-a2 are the parameter passing registers
  Register v0 is used for return value
  Register ra is used for return address (rlink)
  Register at is used for target address (rtarget)
  Register sp is used as a stack pointer
Use: Program Data
Use:
Bookkeeping

## Slide 67: Question?
Saving and restoring of registers on a procedure call…
  Is always done by the caller
  Is always done by the callee
  Is never done since hardware magically takes care of it
  Is done on a need basis partly by the caller and partly by the callee
  What is a caller/callee?
50

## Slide 68
We store some values in registers during a procedure call. Why?
Because we can.
Because it keeps us from having to reference memory as often.
It makes the stack shorter so there is less danger of overflow.
The calling sequence is improved because it is more complex.
60

## Slide 69: Question?
On the LC-2200, how are actual parameters passed to a function?
  On the stack
  On the heap
  Up to 3 in registers, the rest on the stack
  Up to 6 in registers, the rest on the stack
  None of the above.
65

## Slide 70: Activation Record
Also known as a Stack Frame
It’s the space used by the caller and callee during the execution of a procedure call
Used to store…
  Caller saved registers
  Additional parameters
  Additional return values
  Return address
  Callee saved registers
  Local variables

## Slide 71: Stack Conventions
Stack grows toward lower memory addresses
Decrement, then push
Pop, then increment
Top of Stack points to last item placed in it
Stack
Pointer
STACK
Low address
High address
Stack is initially empty

## Slide 72
Step 1.
Caller saves any of registers t0-t2 on the stack (if it needs the values in them upon return).
Stack
Pointer
STACK
From t registers
Saved t Registers

## Slide 73
Step 2.
Caller places the parameters in a0-a2 (using the stack for additional parameters if needed).
Stack
Pointer
Saved t Registers
Additional parameters
STACK
From function call

## Slide 74
Step 3.
Caller allocates space for any additional return values on the stack
Stack
Pointer
STACK
Additional return values
Saved t Registers
Additional parameters

## Slide 75
Step 4.
Caller saves previous return address currently in ra
Stack
Pointer
Prev Return address
STACK
Additional return values
From ra
Saved t Registers
Additional parameters
Why?

## Slide 76
Step 5.
Caller executes JALR at, ra
(no effect on stack)
Stack
Pointer
STACK
Prev Return address
Additional return values
Saved t Registers
Additional parameters

## Slide 77
Step 6.
Callee saves any of registers s0-s2 that it plans to use during its execution on the stack.
Stack
Pointer
Saved s Registers
STACK
Prev Return address
Additional return values
From s
registers
Saved t Registers
Additional parameters

## Slide 78
Step 7.
Callee allocates space for any local variables on the stack
Stack
Pointer
Local variables
STACK
Saved s Registers
Prev Return address
Additional return values
Saved t Registers
Additional parameters

## Slide 79
Step 8.
Prior to return, Callee restores any saved s0-s2 registers from the stack
Stack
Pointer
STACK
Saved s Registers
Prev Return address
Additional return values
To S
registers
Saved t Registers
Additional parameters

## Slide 80
Step 9.
Callee executes jump to ra
No change to stack.
Stack
Pointer
STACK
Prev Return address
Additional return values
Saved t Registers
Additional parameters

## Slide 81
Step 10.
Upon return, Caller restores previous return address to ra
Stack
Pointer
STACK
Prev Return address
Additional return values
To ra
Saved t Registers
Additional parameters

## Slide 82
Step 11.
Caller stores additional return values as desired
Stack
Pointer
STACK
Additional return values
As desired
Saved t Registers
Additional parameters

## Slide 83
Step 12.
Upon return, Caller moves stack pointer to discard additional parameters
Stack
Pointer
STACK
Saved t Registers
Additional parameters

## Slide 84
Step 13.
Upon return, Caller restores any saved t0-t2 registers from the stack
Stack
Pointer
STACK
To t
registers
Saved t Registers

## Slide 85: Question?
Local variables in a procedure...
  Are usually allocated on the stack
  Are usually kept in processor registers
  Are usually kept in a special hardware
  Are usually allocated in the heap space of the program
  Are usually allocated in the static (global) data space of the program
  None of the above
67

## Slide 86: A Stack of Activation Records
Stack
Pointer
Activation
Stack
Frame for
baz
Activation
Stack
Frame for
bar
Activation
Stack
Frame for
foo
Activation
Stack
Frame for
main
Local variables
Saved s Registers
ra
Additional return values
Saved t Registers
Additional parameters
main ()  foo()  bar()  baz()
Callee
Caller

## Slide 87: Recursion
Does recursion require any additional instruction set architecture items?

## Slide 88: One More Thing: Frame Pointer
During execution of given module it is possible for the stack pointer to move.
Since the location of all items in a stack frame is based on the stack pointer it useful to define a fixed point in each stack frame and maintain the address of this fixed point in a register called the frame pointer
This necessitates storing the old frame pointer in each stack frame (i.e caller’s frame pointer)

## Slide 89: Why Do We Need a Frame Pointer?
This code will cause us a problem:
foo(int p) { int a = 1, b = 3; if (a != p) { int c[p]; c[p – 1] = b + a; … } b++; a++; ; … }
Let's look in detail at the stack
A and b are no longer at the same offset from SP

## Slide 90: Let’s Start at Step 7 To See What Our Function Does
Stack
Pointer
Local variables
Saved s Registers
Prev Return address
Additional return values
Saved t Registers
Additional parameters
int a = 1, b = 3; if (a != p) { int c[p]; c[p-1] = b + a; … } b++; a++;

## Slide 91: Slide The Stack Diagram Down
Stack
Pointer
Local variables
Saved s Registers
Prev Return address
int a = 1, b = 3; if (a != p) { int c[p]; c[p-1] = b + a; … } b++; a++;

## Slide 92: When Our Function Runs
Stack
Pointer
a
Saved s Registers
Prev Return address
b
c[p-1]
c[0]
Stack
Pointer
…
int a = 1, b = 3; if (a != p) { int c[p]; c[p-1] = b + a; … } b++; a++;
This "b" is at SP + 0
This "b" is at SP + p
This "b" is at SP + 0



This “a” is at SP + p + 1
This ”a” is at SP + 1
This ”a" is at SP + 1

## Slide 93: Let's Revise foo()'s Stack Frame
We're going to add one more item to the stack: Prev Frame Pointer because we'll need to save/restore our Frame Pointer register.
And that's where we'll point our Frame Pointer register.
Stack
Pointer
Local variables
Prev Frame Pointer
Saved s Registers
Prev Return address
Frame
Pointer

## Slide 94: Addressing Local Variables with FP
Stack
Pointer
a
Prev Frame Pointer
Saved s Registers
Prev Return address
b
c[0]
c[p-1]
Frame
Pointer
…
int a = 1, b = 3; if (a != p) { int c[p]; c[0] = b + a; … } b++; a++;
This "b" is at FP - 3
This "b" is at FP - 3
This "b" is at FP - 3

## Slide 95
New Step 5.5.
Callee stores previous frame pointer then copies contents of stack pointer into frame pointer.
Frame
Pointer
Prev Frame
Pointer
STACK
Return address
Additional return values
*Stack pointer may change during procedure execution
Saved t Registers
Additional parameters
Stack
Pointer*
From FP

## Slide 96
Step 6 (revised).
Callee saves Frame Pointer on the stack and sets Frame Pointer to the Stack Pointer
Frame
Pointer
Prev Frame
Pointer
STACK
Return address
Additional return values
*Stack pointer may change during procedure execution
Saved t Registers
Additional parameters
Stack
Pointer*

## Slide 97
Step 7 (revised).
Callee saves any of registers s0-s2 that it plans to use during its execution on the stack.
Stack
Pointer
Prev Frame Pointer
Saved s Registers
STACK
Prev Return address
Additional return values
From s
registers
Saved t Registers
Additional parameters
Frame
Pointer

## Slide 98
Step 8 (revised).
Callee allocates space for any local variables on the stack
Stack
Pointer
Saved s Registers
Local Variables
STACK
Prev Frame Pointer
Prev Return address
Additional return values
Saved t Registers
Additional parameters
Frame
Pointer

## Slide 99
Step 9 (revised).
Prior to return, Callee restores any saved s0-s2 registers from the stack
Stack
Pointer
STACK
Prev Frame Pointer
Prev Return address
Additional return values
To s
registers
Saved t Registers
Additional parameters
Saved s Registers
Local variables
Frame
Pointer

## Slide 100
Step 10 (revised).
Callee replaces the value in SP with the value from FP to pop the Local Variables and Saved s Registers off the stack
Stack
Pointer
STACK
Prev Frame Pointer
Prev Return address
Additional return values
Saved t Registers
Additional parameters
Frame
Pointer
To FP

## Slide 101
Step 11 (revised).
Callee executes jump to ra
No change to stack.
Note that Frame Pointer is now pointing to caller's activation record and we proceed as we did without a frame pointer
Stack
Pointer
STACK
Prev Return address
Additional return values
Saved t Registers
Additional parameters

## Slide 102
Step 12 (revised).
Upon return, Caller restores previous return address to ra
Stack
Pointer
STACK
Prev Return address
Additional return values
To ra
Saved t Registers
Additional parameters

## Slide 103
Step 13 (revised).
Caller stores additional return values as desired
Stack
Pointer
STACK
Additional return values
As desired
Saved t Registers
Additional parameters

## Slide 104
Step 14 (revised).
Upon return, Caller moves stack pointer to discard additional parameters
Stack
Pointer
STACK
Saved t Registers
Additional parameters

## Slide 105
Step 15 (revised).
Upon return, Caller restores any saved t0-t2 registers from the stack
Stack
Pointer
STACK
To t
registers
Saved t Registers

## Slide 106: Upshot of Stack Evolution
The offset with respect to the stack pointer for referencing variables on the stack changes as the stack grows and shrinks
 A pain for the compiler writer  Burdens the code with complicated local variable address calculations
How to reduce this pain?
 Have a fixed harness on the stack for referencing local variables
 Frame Pointer (FP)

## Slide 107: Differences from the LC-3 Stack
The caller must save any t registers it wants preserved over the call
The first 3 arguments and return value are passed in registers
The caller must save the return address in ra after saving/pushing the arguments
The frame pointer points to the saved old frame pointer, not the first local variable.
The callee pushes saved s registers before allocating the local variables

## Slide 108: Example Stack Frames
main ()  foo()  bar()  baz()
Does not use s registers;
Uses t registers
Does not use s registers; no local variables; accepts 1 parameter; returns 1 value
Uses s registers;
Uses t registers; has local variables

## Slide 109: Registers and the Stack Frame
Stack
Pointer
Activation
Stack
Frame for
baz
Activation
Stack
Frame for
bar
Activation
Stack
Frame for
foo
Activation
Stack
Frame for
main
Prev Frame Pointer
Saved s Registers
ra
Additional return values
Saved t Registers
Additional parameters
main ()  foo()  bar()  baz()
no yes no
Local variables
Sometimes (determined by baz())
Sometimes (determined by bar())
Always
Callee
Caller

## Slide 110: baz() Stack Frame
Stack
Pointer
Activation
Stack
Frame for
baz
Activation
Stack
Frame for
bar
Activation
Stack
Frame for
foo
Activation
Stack
Frame for
main
Prev Frame Pointer
ra
main ()  foo()  bar()  baz()
no yes no
Frame
Pointer
Saved t Registers

## Slide 111: bar() Stack Frame
Stack
Pointer
Activation
Stack
Frame for
baz
Activation
Stack
Frame for
bar
Activation
Stack
Frame for
foo
Activation
Stack
Frame for
main
Prev Frame Pointer
Saved s Registers
ra
Saved t Registers
main ()  foo()  bar()  baz()
no yes no
Local variables
Frame
Pointer

## Slide 112: Question
What do we do if there are no s registers to be saved during a procedure call?
Put a marker on the stack to indicate there are no saved s registers
Increment the stack pointer to leave room in case the s registers need to be saved later
Push a word of zero for every s register not saved
Nothing
Today’s number is 77,131.
68

## Slide 113: Question
We keep track of a frame pointer because
It’s faster to access a variable through the frame pointer than it is to access through the stack pointer.
I can’t explain why we waste one of our valuable registers doing this.
It was done in the first RISC machine and so we always do it the same way.
It gives us a single, consistent, constant offset to reference the local variables in a stack frame.
69

## Slide 114: Moving forward
Making design choices
  Additional instruction attributes
  Addressing modes
  Architecture styles
  Instruction formats
The LC-2200
  Instructions
  Registers
  Stack frame

## Slide 115: We Have to Make Many Choices…
Specific set of arithmetic and logic instructions
Addressing modes
Architectural style
Memory layout of the instruction (instruction format)
Drivers of these decisions
  Technology trends
  Implementation feasibility
  Goal of elegant/efficient support for high-level language constructs.

## Slide 116: Additional Register Instruction Attributes
MIPS
  Special instructions exist for extracting bytes
DEC Alpha
  Instructions for loading and storing different sizes
Some architectures have predefined values in registers
  e.g. 0, 1, etc.
DEC VAX (32-bit follow-on to the PDP-11), ARM
  Single instruction to load or store all registers

## Slide 117: More Addressing Modes
All those we've seen
  Register
  PC-relative
  Base+offset
  Base+index
Additional modes
  Indirect addressing
  ld @ra
Pseudo-direct addressing
  Address is formed from first 6 bits of PC and last 26 bits of instruction

## Slide 118: Architecture Styles
Accumulator oriented
  Early digital computers
Stack oriented
  Burroughs
Register-Memory oriented
  IBM s/360, DEC VAX, et al
  Intel x86
Register-Register oriented
  MIPS, Alpha, ARM, Power PC, CDC 6600

## Slide 119: Instruction Formats
Zero Operand Instructions
  Halt, NOP
  Stack machines: Add, Sub
One Operand Instructions
  Inc, Dec, Neg, Not
  Accumulator machines: Load M, Add M
Two Operand Instructions
  Add r1, r2 (i.e. r1 = r1 + r2)
  Mov r1, r2
Three Operand Instructions
  Add r1, r2, r3
  Load rd, rb, offset

## Slide 120: Instruction Format
Fixed Length Instructions
Pros
  Simplifies implementation
  Can start interpreting instructions immediately
Cons
  May waste space
  May need additional logic in datapath
  Limits instruction set designer
Variable Length Instructions
Pros
  No wasted space
  Less constraints on designer
  More flexibility with opcodes, addressing modes and operands
Cons
  Complicates implementation

## Slide 121: Some History
Hardware Expensive
Memory Expensive
Accumulators (1-2)
EDSAC
IBM 701
UNIVAC I
Hardware Cheaper
Memory Expensive
Registers (8-16)
Register-Memory
IBM 360
DEC PDP-11
Univac 1108
Register-Register
CDC 6600
Stack
Burroughs B-5000
Hardware Cheap
Memory Cheap
Microprocessors
Compilers getting good
CISC
DEC VAX
Motorola 68000
Intel 80x86
RISC
Berkeley RISCSparc
Dave Patterson
Stanford MIPS SGI
John Hennessy
IBM 801
ARM
RISC-V
1940
1960
1980

## Slide 122: We’ve Made Some Choices
The LC-2200
RISC
Register-register style
Fixed-length, 32-bit, MIPS-like instructions
32-bit words, word addressable
16 registers
Initially we define a very sparse set of instructions so there are still more choices to make

## Slide 123: Question
The LC-2200 is a 32-bit word-addressable ISA. Why is it not byte-addressable?
Byte-addressable memories are an artifact from the past and aren’t used in modern CPU ISAs.
Using a byte as the addressable unit makes the implementation more complex.
In C and Java, we never need to address data objects smaller than registers.
Since the LC-2200 uses fixed-length 32-bit instructions, it has no need for byte-addressable memory
69

## Slide 124: LC-2200 Instruction set
R-type instructions (add, nand):
bits 31-28: opcode
bits 27-24: reg X; bits 23-20: reg Y
bits 19-4: unused (should be all 0s); bits 3-0: reg Z
I-type instructions (addi, lw, sw, beq):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: Imm. Offset
J-type instructions (jalr):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: unused
O-type instructions (halt):
bits 31-28: opcode; bits 27-0: unused

## Slide 125: LC-2200 Register convention
Reg # | Name | Use | callee-save?
0 | $zero | always zero (by hardware) | n.a.
1 | $at | reserved for assembler | n.a.
2 | $v0 | return value | no
3-5 | $a0-$a2 | arguments | no
6-8 | $t0-$t2 | temporaries | no
9-11 | $s0-$s2 | saved registers | YES
12 | $k0 | reserved for OS/traps | n.a.
13 | $sp | stack pointer | no
14 | $fp | frame pointer | YES
15 | $ra | return address | no
Only if your function body code will change them!
Always save
So, what does that do to our calling convention?
Save if you want to preserve them across a function call

## Slide 126: LC-2200 example mnemonics
Mnemonic Example | Format | Opcode | Action Register Transfer Language
add add $v0, $a0, $a1 | R | 0 00002 | Add contents of reg Y with contents of reg Z, store results in reg X. RTL: $v0  $a0 + $a1
addi addi $v0, $a0, 25 | I | 2 00102 | Add OFFSET to the contents of reg Y and store the result in reg X. RTL: $v0  $a0 + 25
lw lw $v0, 0x42($fp) | I | 3 00112 | Load reg X from memory. The memory address is formed by adding OFFSET to the contents of reg Y. RTL: $v0  MEM[$fp + 0x42]

## Slide 127: LC-2200 example mnemonics
Mnemonic Example | Format | Opcode | Action Register Transfer Language
nand nand $v0, $a0, $a1 | R | 1 00012 | Add contents of reg Y with contents of reg Z, store results in reg X. RTL: $v0  ~($a0 & $a1)
sw sw $v0, 0x42($fp) | I | 4 01002 | Load reg X from memory. The memory address is formed by adding OFFSET to the contents of reg Y. RTL: MEM[$fp + 0x42]  $v0

## Slide 128
Mnemonic Example | Format | Opcode | Action Register Transfer Language
beq beq $a0, $a1, done | I | 5 01012 | Compare the contents of reg X and reg Y. If they are the same, then branch to the address PC+1+OFFSET, where PC is the address of the beq instruction. RTL: if($a0 == $a1) PC  PC+1+OFFSET
Note: For programmer convenience (and implementer confusion), the assembler computes the OFFSET value from the number or symbol given in the instruction and the assemblers idea of the PC. In the example, the assembler stores done-(PC+1) in OFFSET so that the machine will branch to label "done" at run time. |  |  | 

## Slide 129
Mnemonic Example | Format | Opcode | Action Register Transfer Language
jalr jalr $at, $ra | J | 6 01102 | First store PC+1 into reg Y, where PC is the address of the jalr instruction. Then branch to the address now contained in reg X. Note that if reg X is the same as reg Y, the processor will first store PC+1 into that register, then end up branching to PC+1. RTL: $ra  PC+1; PC  $a0

## Slide 130: Addition to the textbook instructions
lea lea $v0, 0x10 | I | 9 10012 | Load reg X from with PC-relative address. The effective address is formed by adding OFFSET to the contents of the incremented PC. RTL: $v0  PC + 1 + 0x10
blt, bgt blt $a0, $a1, done bgt $a0, $a1, done | I | 8 10002 10 10102 | Compare the contents of reg X and reg Y. If X is less than Y (greater than), then branch to the address PC+1+OFFSET, where PC is the address of the blt (bgt) instruction. RTL: if ($a0 < $a1) PC  PC+1+OFFSET

## Slide 131: Question
What is true about register $v0?
It can only be set and copied; it cannot be used for intermediate arithmetic operations nor can it store the return address during a JALR instruction
It is stored in physical register number 00102.
Based on our calling convention, it holds the value being returned from a function unless the value is longer than 32 bits
B and C only
A and B only
None are true
80

## Slide 132: Issues Influencing Processor Design
Instruction Set
Applications
Other
  Operating system
  Support for modern languages
  Memory system
  Parallelism
  Debugging
  Virtualization
  Fault Tolerance
  Security

## Slide 133: Instruction Set
Over-arching concern: Compiling high level language constructs into efficient machine code
But other factors are in play
  Market pressure
  Performance
  Technology workarounds

## Slide 134: Influence of Applications on Instruction Set Design
Number crunching requires efficient floating point
  Development of floating point hardware
Media applications deal with streaming data
  Intel MMX extensions
Gaming requires sophisticated graphic processing
  High end games now include GPU chips

## Slide 135: Other Issues Driving Processor Design
Operating system
Modern languages: Java, C++ and C#
Memory system
Parallelism
Debugging
Virtualization
Fault tolerance
Security