## Slide 1: Data Paths
CS 2200 Fall 2023

## Slide 2: Topics
Logic design review
Data paths
Finite State Machines

## Slide 3: Architecture vs. Organization
Architecture – the abstraction involving programmer-visible details of a computer system, such as
  Instruction set
  Memory layout
Organization – the details of the implementation of a particular architecture, involving many details that are not directly visible to a programmer, such as
  Register implementation
  Bus structure
  Memory hierarchy and bank organization
There is some gray area, just like most definitions in CS

## Slide 4: The terminology!
I blithely presumed the architecture and organization terms meant the same thing they've meant for 45 years since I took this course in about 1975.
Then I asked "the Google" what it thought.
To my surprise, the first three postings I saw (quora, stackoverflow, javatpoint) had the definitions reversed or decidedly muddied. Did I fall into an alternate universe? How could it be allowed on the Internet if it's not true?
Then I looked at several academic sites which all confirmed the definition I learned 45 years ago!

## Slide 5: So where do these words fit?
Architecture
  ISA (instruction set architecture)
  Instruction set
  Machine language
  Machine abstraction
Organization
  Processor implementation
  Microarchitecture
Perhaps think of architecture as "the API" and organization as "the code implementing the API"

## Slide 6: Processor Implementation
Implementation for a given an instruction set
Instruction-set is not a description of the implementation of the processor
  Contract between hardware and software
  Allows a compiler writer to generate code for different high-level languages to execute on a processor that implements this contract
Can there be different implementations of the same instruction set?

## Slide 7: IBM System/360: One architecture, many implementations
Model | Announced | Shipped | Scien-tific perform-ance (kIPS) | Commer-cial perform-ance (kIPS) | CPU Band-width (MB/sec) | Memory band-width (MB/sec) | Memory size (in KB)
360/30 | Apr 1964 | Jun 1965 | 10.2 | 29 | 1.3 | 0.7 | 8-64
360/40 | Apr 1964 | Apr 1965 | 40 | 75 | 3.2 | 0.8 | 16-256
360/50 | Apr 1964 | Aug 1965 | 133 | 169 | 8.0 | 2.0 | 64-512
360/20 | Nov 1964 | Mar 1966 | 2.0 | 2.6 |  |  | 4-32
360/91 | Jan 1966 | Oct 1967 | 1,900 | 1,800 | 133 | 164 | 1,024-4,096
Rasp-berry Pi 2 | 2014 | 2014 | 4,744 | 4,744 |  | 1,200 | 1,024-4,096
AMD Ryzen 3990X | 2020 | 2020 | 2,345,230 | 2,345,230 |  | 95,000 | 16,000-128,000

## Slide 8: Architecture versus Implementation
Why?
Market demands (different price points)
Parallel hardware and software development
Maintain compatibility for legacy software compatibility

## Slide 9: What is involved in Processor Implementation?
Organization of the electrical components (ALUs, buses, registers, etc.) commensurate with the expected price/performance characteristic of the processor.
Thermal and mechanical aspects including cooling and physical geometry for placement in mother boards.
Super Computers | Servers | Desktops & PCs | Embedded
High performance primary objective | Intermediate performance and cost | Low cost primary objective | Small size, low cost, and low power consumption primary objectives

## Slide 10: Let’s Review Digital Circuits
Combinational logic
  For a given set of inputs there is one unique output
Sequential logic
  Circuits contain elements that remember state
  Outputs depends on combinational logic that considers circuit inputs and previous state

## Slide 11: Hardware resources of the datapath
Memory
ALU
Register file
Program Counter
Instruction Register

## Slide 12: Logic triggering
Level Triggering
Outputs change based on inputs whenever clock is high
Memory will be considered to be level triggered (for cost reasons)
Edge Triggering
Outputs change based on inputs only when clock transitions
Positive edge-triggered logic when leading edge cause triggering
Negative edge-triggered when trailing edge causes triggering
inputs
outputs
clock

## Slide 13: Registers
register
input
output
clock

## Slide 14: Master-Slave Flip Flop
Gated D Latch
Gated D Latch
Master
Slave
Remember our Gated D Latch?

## Slide 15: Clock Edges and Master-Slave
Write
Enable
Slave register outputs its inputs.
Master register outputs what was recorded when WE rose to 1.
Slave register outputs what was recorded when WE fell to 0.
Master register outputs its inputs.
Slave register records what is presented on its input.
Master register records what is presented on its input.
Now we just connect Write Enable to the clock....

## Slide 16: Registers and Clocks
Rising
edge
Falling
edge
Output stabilizes
Content of register changes to what is presented on input
(rising edge triggered)
Input stabilizes

## Slide 17: How Many Clock Cycles from Input to Output?
register
register
register
Input
Output

## Slide 18: Register File
Input
Output
Address
Clock
R/W
.
.
.
0
1
2
13
14
15

## Slide 19: Register File
Input
Output
Address
(0-15)
Clock
R/W (0-1)
.
.
.
0
1
2
13
14
15

## Slide 20: Dual Ported Register File
Input
Port 1 Output
Port 1 Address
.
.
.
0
1
2
13
14
15
Port 2 Output
Port 2 Address
Clock
Lets us read two registers in one clock cycle
Dest Address
Write
If high at end of clock, write input to the Dest address

## Slide 21: Memory (DRAM)
memory
Read
Data out
Data in
Address
Write
Works differently from a register
  Not clocked
  Level triggered logic
    Why is this?
Each cell is a single transistor and capacitor (instead of 6 transistors needed for a flip-flop)

## Slide 22: A Typical ALU
Combinational circuit
Two inputs
One output
Function select which selects which functional unit is presented on the output
ALU
A
B
OUT
SEL

## Slide 23: What's Inside an ALU?
A
B
OUT
SEL
How many lines needed for SEL?
How many bits wide are the data paths?
Gisselquist Technology, Inc. https://zipcpu.com/zipcpu/2017/08/11/simple-alu.html

## Slide 24: Review Components
Clock signal
Register – edge triggered
Register file – read: level triggered write: edge triggered
Memory – read: level triggered (in LC-2200) write: edge triggered
ALU – Level triggered

## Slide 25: Connecting the Datapath Elements
PC
Memory
Addr Din
Dout
IR
Register-file
ALU

## Slide 26: Connecting the Datapath Elements
PC  ADD rx, ry, rz
rx <= ry + rz
Work done: PC  Mem  IR  Reg File  ALU  Reg File
PC
Memory
Addr Din
Dout
IR
Register-file
ALU
ADD rx, ry, rz
Bits from IR connect to 3 Reg File Inputs
Supply ry and rz
Computed ry + rz
Write into rx

## Slide 27: How Can We Tell?
PC  Mem  IR 
Comb + Level
Reg File  ALU  Reg File
Comb + Level
PC
Memory
Addr Din
Dout
IR
Register-file
ALU
Rising Edge

## Slide 28: Two Clock Cycles
PC  memory  IR
 Reg File  ALU  Reg File
First clock cycle
Second clock cycle
IR Written
rx Written
The wrinkle is that we read the reg file first and then write to it.

## Slide 29: How Many Clock Cycles?
How many clock cycles did it take to execute PC  Mem  IR  Reg File  ALU  Reg File
One
Two
Three
Four
Five
None of the above
Today’s number is 51,112
10

## Slide 30: Delays
Register Input
  Setup (before clock edge)
  Hold (after clock edge)
Output stable
  (before it can be used)
Propagation
  (wire)
ALU op
  (combinational logic)
Register
ALU

## Slide 31: Clock Width
PC  memory  IR 
Reg File  ALU  Reg File
PC
Memory
Addr Din
Dout
IR
Register-file
ALU

## Slide 32: Example Delay Parameters
Example 3: Given the following parameters (all in picoseconds),
determine the minimum clock width of the system.
Dr-ouput-stable (PC output stable) - 20 ps
Dwire-PC-Addr (wire delay from PC to Addr of Memory) - 250 ps
Dmem-read (Memory read) - 1500 ps
Dwire-Dout-IR (wire delay from Dout of Memory to IR) - 250 ps
Dr-setup (setup time for IR) - 20 ps
Dr-hold (hold time for IR) - 20 ps
Dwire-IR-regfile (wire delay from IR to Register file) - 250 ps
Dregfile-read (Register file read) - 500 ps
Dwire-regfile-ALU (wire delay from Register file to input of ALU) - 250 ps
DALU-OP (time to perform ALU operation) - 100 ps
Dwire-ALU-regfile (wire delay from ALU output to Register file) - 250 ps
Dregfile-write (time for writing into a Register file) - 500 ps

## Slide 33: Question
How wide should a clock cycle be?
Ask Intel
Magic
Add all the data path delays between edge-triggered devices and then take the maximum
Set it arbitrarily and hope it works
20

## Slide 34: Calculating Clock Width
PC  memory  IR 
Reg File  ALU  Reg File
max(green time, blue time)
PC
Memory
Addr Din
Dout
IR
Register-file
ALU
Split circuits at edge-triggered devices

## Slide 35: Which Are Edge-Triggered?
Level-triggered devices
  Memory read (this is different from LC-3)
  Register file read
  ALU
  Other register reads
  Muxes
  Decoders
Edge-triggered devices
  Memory write
  Register file write
  Other register writes

## Slide 36: Calculating Clock Minimums
 | Delay (ps) | Green bracket | Blue bracket 1 | Blue brackets 2-5 | 
Dr-ouput-stable | 20 | 20 |  |  | (PC output stable)
Dwire-PC-Addr | 250 | 250 |  |  | (wire delay from PC to Addr of Memory)
Dmem-read | 1500 | 1500 |  |  | (Memory read)
Dwire-Dout-IR | 250 | 250 |  |  | (wire delay from Dout of Memory to IR)
Dr-setup | 20 | 20 |  |  | (setup time for IR)
Dr-hold | 20 |  | 20 |  | (hold time for IR)
Dwire-IR-regfile | 250 |  | 250 |  | (wire delay from IR to Register file)
Dregfile-read | 500 |  | 500 |  | (Register file read)
Dwire-regfile-ALU | 250 |  | 250 |  | (wire delay from Register file to input of ALU)
DALU-OP | 100 |  | 100 |  | (time to perform ALU operation)
Dwire-ALU-regfile | 250 |  |  | 250 | (wire delay from ALU output to Register file)
Dregfile-write | 500 |  |  | 500 | (time for writing into a Register file)
PC
Memory
IR
Register-file
ALU

## Slide 37: Calculating Clock Minimums
 | Delay (ps) | Green bracket | Blue bracket 1 | Blue brackets 2-5 | 
Dr-ouput-stable | 20 | 20 |  |  | (PC output stable)
Dwire-PC-Addr | 250 | 250 |  |  | (wire delay from PC to Addr of Memory)
Dmem-read | 1500 | 1500 |  |  | (Memory read)
Dwire-Dout-IR | 250 | 250 |  |  | (wire delay from Dout of Memory to IR)
Dr-setup | 20 | 20 |  |  | (setup time for IR)
Dr-hold | 20 |  | 20 |  | (hold time for IR)
Dwire-IR-regfile | 250 |  | 250 |  | (wire delay from IR to Register file)
Dregfile-read | 500 |  | 500 |  | (Register file read)
Dwire-regfile-ALU | 250 |  | 250 |  | (wire delay from Register file to input of ALU)
DALU-OP | 100 |  | 100 |  | (time to perform ALU operation)
Dwire-ALU-regfile | 250 |  |  | 250 | (wire delay from ALU output to Register file)
Dregfile-write | 500 |  |  | 500 | (time for writing into a Register file)
 |  | 2040 |  |  | 
PC
Memory
IR
Register-file
ALU

## Slide 38: Calculating Clock Minimums
 | Delay (ps) | Green bracket | Blue bracket 1 | Blue brackets 2-5 | 
Dr-ouput-stable | 20 | 20 |  |  | (PC output stable)
Dwire-PC-Addr | 250 | 250 |  |  | (wire delay from PC to Addr of Memory)
Dmem-read | 1500 | 1500 |  |  | (Memory read)
Dwire-Dout-IR | 250 | 250 |  |  | (wire delay from Dout of Memory to IR)
Dr-setup | 20 | 20 |  |  | (setup time for IR)
Dr-hold | 20 |  | 20 |  | (hold time for IR)
Dwire-IR-regfile | 250 |  | 250 |  | (wire delay from IR to Register file)
Dregfile-read | 500 |  | 500 |  | (Register file read)
Dwire-regfile-ALU | 250 |  | 250 |  | (wire delay from Register file to input of ALU)
DALU-OP | 100 |  | 100 |  | (time to perform ALU operation)
Dwire-ALU-regfile | 250 |  |  | 250 | (wire delay from ALU output to Register file)
Dregfile-write | 500 |  |  | 500 | (time for writing into a Register file)
 |  | 2040 | 1120 | 750 | 
PC
Memory
IR
Register-file
ALU

## Slide 39: Calculating Clock Minimums
 | Delay (ps) | Green bracket | Blue bracket 1 | Blue brackets 2-5 | 
Dr-ouput-stable | 20 | 20 |  |  | (PC output stable)
Dwire-PC-Addr | 250 | 250 |  |  | (wire delay from PC to Addr of Memory)
Dmem-read | 1500 | 1500 |  |  | (Memory read)
Dwire-Dout-IR | 250 | 250 |  |  | (wire delay from Dout of Memory to IR)
Dr-setup | 20 | 20 |  |  | (setup time for IR)
Dr-hold | 20 |  | 20 |  | (hold time for IR)
Dwire-IR-regfile | 250 |  | 250 |  | (wire delay from IR to Register file)
Dregfile-read | 500 |  | 500 |  | (Register file read)
Dwire-regfile-ALU | 250 |  | 250 |  | (wire delay from Register file to input of ALU)
DALU-OP | 100 |  | 100 |  | (time to perform ALU operation)
Dwire-ALU-regfile | 250 |  |  | 250 | (wire delay from ALU output to Register file)
Dregfile-write | 500 |  |  | 500 | (time for writing into a Register file)
 |  | 2040 | 1120 | 750 | 
 |  |  |  | 1850 | 
PC
Memory
IR
Register-file
ALU

## Slide 40: Calculating Clock Minimums
 | Delay (ps) | Green bracket | Blue bracket 1 | Blue brackets 2-5 | 
Dr-ouput-stable | 20 | 20 |  |  | (PC output stable)
Dwire-PC-Addr | 250 | 250 |  |  | (wire delay from PC to Addr of Memory)
Dmem-read | 1500 | 1500 |  |  | (Memory read)
Dwire-Dout-IR | 250 | 250 |  |  | (wire delay from Dout of Memory to IR)
Dr-setup | 20 | 20 |  |  | (setup time for IR)
Dr-hold | 20 |  | 20 |  | (hold time for IR)
Dwire-IR-regfile | 250 |  | 250 |  | (wire delay from IR to Register file)
Dregfile-read | 500 |  | 500 |  | (Register file read)
Dwire-regfile-ALU | 250 |  | 250 |  | (wire delay from Register file to input of ALU)
DALU-OP | 100 |  | 100 |  | (time to perform ALU operation)
Dwire-ALU-regfile | 250 |  |  | 250 | (wire delay from ALU output to Register file)
Dregfile-write | 500 |  |  | 500 | (time for writing into a Register file)
 |  | 2040 | 1120 | 750 | 
 |  |  |  | 1870 | 
PC
Memory
IR
Register-file
ALU
Clock must be >=2040 ps

## Slide 41: What Other Connections Do We Need?
R-type instructions (add, nand):
  Opcode, x, y, z
I-type instructions (addi, lw, sw, beq):
  Opcode, x, y, offset
J-type instructions (jalr):
  Opcode, x, y
O-type instructions (halt):
  Opcode
PC
Memory
Addr Din
Dout
IR
Register-file
ALU

## Slide 42: Adding Connections for Our LC-2200 ISA
Memory to Reg File input for LW
Reg File output to Memory for SW
ALU Out to PC for JALR
IR to ALU In to carry offset
In other words, lots more wires
Is it possible to share some of them?

## Slide 43: Towards bus-based design
In principle we must make connections between circuit elements for every instruction
Numerous connections are expensive and take up valuable space
Have a set of wires that all elements can connect to and share in order to transfer information

## Slide 44: Concept of a Bus
Functional
Unit
Drive
CLK
Functional
Unit
Drive
CLK
Functional
Unit
Drive
CLK
So what's that "Drive" thing?
It's another term for a Tri-state Buffer

## Slide 45: A Two-Bus Design
PC
memory
Addr Din
Dout
IR
Register-file
(DPRF)
ALU

## Slide 46: Clock Cycle
PC
memory
Addr Din
Dout
IR
Register-file
(DPRF)
ALU
PC  MEM  IR

## Slide 47: Clock Cycle
PC
memory
Addr Din
Dout
IR
Register-file
(DPRF)
ALU
IR  Reg File (SR1,SR2&DR)  ALU  Reg File

## Slide 48: Two Busses: How Many Clock Cycles?
Using just two busses, how many clock cycles does it take to execute PC  Mem  IR  Reg File (SR1,SR2,DR)  ALU  Reg File
One
Two
Three
Four
Five
None of the above
30

## Slide 49: First Clock Cycle
PC
memory
Addr Din
Dout
IR
Register-file
(DPRF)
ALU
First: PC  MEM  IR

## Slide 50: Second Clock Cycle
PC
memory
Addr Din
Dout
IR
Register-file
(DPRF)
ALU
Second: IR  Reg File (SR1,SR2,DR)  ALU  Reg File

## Slide 51: Single Bus Design
PC
Memory
Addr Din
Dout
Register-file
(DPRF)
ALU
MAR
IR

## Slide 52: Single Bus Design w/o DPRF
PC
Memory
Addr Din
Dout
Register-file
(SPRF)
ALU
MAR
IR
A
B
This is pretty close to the LC-2200 data path we’ll be using

## Slide 53
Using a single-ported register file, what is the minimum number of cycles it will take to prepare the ALU for a two-operand calculation?
0
1
2
3
Today’s number is 82,864
40

## Slide 54: Topics
Logic design review
Data paths
Finite State Machines

## Slide 55: Simple FSM Example
S1
S2
S3

## Slide 56: Garage Door
up
down
1
3
0
2
Transition No | Current State | Clicker | D Output | U Output | Next State
0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
2 | 0 | 1 | 0 | 1 | 1
3 | 1 | 1 | 1 | 0 | 0

## Slide 57: Garage Door Controller
clicker
state
CLK
D
Combinational logic
Down
motor
Up
motor
DownControl
UpControl
Up
Q
NextState
Down
Q
Inputs
Outputs

## Slide 58: Combinational Logic
DOutput = CurrentState&Clicker
UOutput = CurrentState’&Clicker
NextState = CurrentState&Clicker’ | CurrentState’&Clicker
Transition No | Current State | Clicker | D Output | U Output | Next State
0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
2 | 0 | 1 | 0 | 1 | 1
3 | 1 | 1 | 1 | 0 | 0

## Slide 59: Can We Replace Logic with a ROM?
Since we can describe combinational logic as boolean expressions, circuits, truth tables, what if we could replace a combinational circuit with a hardware truth table?
Think of a properly programmed ROM as a literal truth table describing an FSM
  The address represents the input bits (including state)
  The contents of the ROM produce the output bits (including the next state)
Have you seen this somewhere before?

## Slide 60: From FSM to ROM
ROM: 3 bit word x 4 words  3 data lines, 2 address lines
Transition No | Current State | Clicker | D Output | U Output | Next State
0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
2 | 0 | 1 | 0 | 1 | 1
3 | 1 | 1 | 1 | 0 | 0
DOutput | UOutput | NextState
0 | 0 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
A
D
D
R
E
S
S
00
01
10
11

## Slide 61: Replacing Discrete Logic with a ROM
clicker
state
CLK
D
Up
Q
Down
Q
DOutput | UOutput | NextState
0 | 0 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
Down
motor
Up
motor
A
D
D
R
E
S
S
00
01
10
11
ROM

## Slide 62
If you have a truth table with 4 input, 3 state bits, and 4 outputs, what size ROM should you use to encode it?
27 words of 7 bits
24 words of 4 bits
28 words of 7 bits
24 words of 8 bits
50
4 output lines
3 next state lines
23+4= 128 words

## Slide 63: Checkpoint
Basics of logic design
  Combinational
  Sequential
Elements of the datapath
  Registers & register file
  ALU
  Mux
  Decoders
  Finite state machine
  Clock & clock width

## Slide 64: Levels of Abstraction
Application (Algorithms expressed in High Level Language)
System software (Compiler, OS, etc.)
Computer Architecture (ISA)
Machine Organization (Datapath and Control)
Sequential and Combinational Logic Elements
Logic Gates
Transistors
Solid-State Physics (Electrons and Holes)

## Slide 65: Levels of Abstraction
Application (Algorithms expressed in High Level Language)
System software (Compiler, OS, etc.)
Computer Architecture (ISA)
Machine Organization - Control
Machine Organization - Datapath
Sequential and Combinational Logic Elements
Logic Gates
Transistors
Solid-State Physics (Electrons and Holes)

## Slide 66: LC-2200 Instruction Set
R-type instructions (add, nand):
bits 31-28: opcode
bits 27-24: reg X; bits 23-20: reg Y
bits 19-4: unused (should be all 0s); bits 3-0: reg Z
I-type instructions (addi, lw, sw, beq):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: Imm. Offset
J-type instructions (jalr):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: unused
O-type instructions (halt):
bits 31-28: opcode; bits 27-0: unused
Opcode
Reg X
Reg Y
Unused
Reg Z
31
28 27
24 23
20 19
4 3
0
Opcode
Reg X
Reg Y
Signed Offset
31
28 27
24 23
20 19
0
Opcode
Reg X
Reg Y
Unused
31
28 27
24 23
20 19
0
Opcode
Unused
31
28 27
0

## Slide 67: Question
Addressing mode…
Refers to the kinds of opcodes supported in an architecture
Refers to the way the operands are specified in an instruction
Refers to the granularity of the memory element that can be addressed in an instruction
Refers to the datapath width
None of the above
60

## Slide 68: LC-2200 Addressing Modes
R-type instructions (add, nand):
bits 31-28: opcode
bits 27-24: reg X; bits 23-20: reg Y
bits 19-4: unused (should be all 0s); bits 3-0: reg Z
I-type instructions (addi, lw, sw, beq):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: Imm. Offset
J-type instructions (jalr):
bits 31-28: opcode; bits 27-24: reg X
bits 23-20: reg Y; bits 19-0: unused
O-type instructions (halt):
bits 31-28: opcode; bits 27-0: unused
Opcode
Reg X
Reg Y
Unused
Reg Z
31
28 27
24 23
20 19
4 3
0
Opcode
Reg X
Reg Y
Signed Offset
31
28 27
24 23
20 19
0
Opcode
Reg X
Reg Y
Unused
31
28 27
24 23
20 19
0
Opcode
Unused
31
28 27
0
Register
PC-Relative Base + Offset
Immediate
Register
None

## Slide 69: We’ve Got a Datapath for LC-2200!
WrREG
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
232 x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
IR
LdIR
Z
LdZ
=0?
32
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
1
1
IR[3..0]
IR[23..20]
IR[27..24]
RX
RY
RZ
What else do we need??
00
01
10
regno
4
4
4
4
2
M
U
X
RegSel

## Slide 71: A Control Unit!
In one clock cycle:
State reg  ROM  Drive datapath (which does the work)  Store Next State  Back to the start
Datapath
regsel
2

## Slide 72: What’s in the ROM?
 | Drive Signals |  |  |  |  | Load Signals |  |  |  |  |  | Write Signals |  |  | 
Current State | PC | ALU | Reg | MEM | OFF | PC | A | B | MAR | IR | Z | MEM | REG | func | RegSel
Recognize all these as the control signals to drive the datapath You will find each one on the datapath diagram!

## Slide 73: The Next State is Stored in the ROM, Too!
 | Drive Signals |  |  |  |  | Load Signals |  |  |  |  |  | Write Signals |  |  |  | 
Current State | PC | ALU | Reg | MEM | OFF | PC | A | B | MAR | IR | Z | MEM | REG | func | RegSel | Next State
... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
In addition to being the Current State, this is also necessarily the address of the word in the ROM

## Slide 74: This Means the ROM Contents Are…
 | Drive Signals |  |  |  |  | Load Signals |  |  |  |  |  | Write Signals |  |  |  | 
Current State | PC | ALU | Reg | MEM | OFF | PC | A | B | MAR | IR | Z | MEM | REG | func | RegSel | Next State
00000 | 1 |  |  |  |  |  | 1 |  | 1 |  |  |  |  |  |  | 00001
... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Our Microprogram!
For short, we might write this microinstruction as 00000: DrPC LdMAR LdA next=00001

## Slide 75: A Familiar State Diagram?
Fetch
Decode
Execute
What state diagram do you think a CPU implementer might be concerned with?
Is a processor implementation a Finite State Machine?
What happens in each state?
What resources are needed to execute each instruction?

## Slide 76: Implementing the LC-2200 ISA
R-type instructions
  Sequence of machine states are similar
  Only the ALU op changes
J-type instructions
  Straightforward
I-type instructions (LW, SW, ADDI)
  Straightforward
I-type instructions (BEQ)
  May take some thought…
  Let’s do BEQ first

## Slide 77: So How Do We Handle BEQ?
BEQ has the following semantics:
  if RegX == RegY then PC  PC + 1 + signed-offset
  else nothing
  Read values of RegX and RegY
  & perform comparision
  Just exactly how do we do that?
Opcode
Reg X
Reg Y
Signed Offset
31
28 27
24 23
20 19
0

## Slide 78: Implementing BEQ
WrREG
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
232 x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
IR
LdIR
Z
LdZ
=0?
32
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
1
1
IR[3..0]
IR[23..20]
IR[27..24]
RX
RY
RZ
Subtract and check for equality
Circuit for equality check
00
01
10
regno
4
4
4
4
2
M
U
X
RegSel

## Slide 79: Implementing BEQ
WrREG
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
232 x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
IR
LdIR
Z
LdZ
=0?
32
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
1
1
IR[3..0]
IR[23..20]
IR[27..24]
RX
RY
RZ
Subtract and check for equality
A 1-bit register
00
01
10
regno
4
4
4
4
2
M
U
X
RegSel

## Slide 80
At this point, what do we know?

## Slide 81: Decision Time
BEQ has the following semantics:
  if RegX == RegY then PC  PC + 1 + signed-offset
  else nothing
Opcode
Reg X
Reg Y
Signed Offset
31
28 27
24 23
20 19
0
BEQ rx, ry, target PC <inst1>
…
target <instN>
i.e. go back to fetch the next instruction (e.g. <inst1>)
Need to do this if branch is taken (e.g. next instruction is <instN>

## Slide 82
If Z==0  go to ifetch1
If Z==1  compute target address

## Slide 83
Presume we’ve taken the branch
Next state will be ifetch1

## Slide 84: And We Can Fill in Most ROM Values
 | Drive Signals |  |  |  |  | Load Signals |  |  |  |  |  | Write Signals |  |  |  | 
Current State | PC | ALU | Reg | MEM | OFF | PC | A | B | MAR | IR | Z | MEM | REG | func | Reg Sel | Next State
beq1 |  |  | 1 |  |  |  | 1 |  |  |  |  |  |  |  | 00 | beq2
beq2 |  |  | 1 |  |  |  |  | 1 |  |  |  |  |  |  | 01 | beq3
beq3 |  | 1 |  |  |  |  |  |  |  |  | 1 |  |  |  | 10 | beq4 or ifetch1
beq4 | 1 |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  | beq5
beq5 |  |  |  |  | 1 |  |  | 1 |  |  |  |  |  |  |  | beq6
beq6 |  | 1 |  |  |  | 1 |  |  |  |  |  |  |  | 00 |  | ifetch1

## Slide 85: But How Do We Handle that Decision?
The steps in the ROM only allow for one “Next State”…
So we’re going to have to come up with some way to modify that Next State if we want to branch
What if we expand the ROM address to 6 bits so we can prepend a zero or one bit to the Next State if we want to test Z? (It doubles the ROM size, though.)
For example, if Next State was 01000, we’d output 001000 UNLESS we wanted to test Z. Then we’d either output 101000 or 001000 by sending the value in Z as the first bit of our next-state ROM address
How can we do that?

## Slide 86: We Have One Additional Decision …
In a few minutes, we’re also going to have to decide how to choose the right next-state based on our opcode in IR; let’s solve that at the same time
We’ll handle that with a similar hardware mod: we’ll expand the ROM address from 6 to 10 bits
Then when we want to make that decision, we’ll use the opcode as the top 4 bits of the ROM address
That means if the opcode is 0010 and next-state is 00011, then if we use the opcode bits, we would use 00100 00011 as the next state so the microcode to execute 0010 would start at that address
This gives us a many-way branch.

## Slide 87: We’re Going to Tweak the Control Unit
DrPC, DrALU, DrREG,
DrMEM, DrOFF
LdPC, LdA, LdB, LdMAR,
LdIR, LdZ, WrREG, WrMEM
func
RegSel
T
Datapath
So what are we adding?
Add a T bit to the ROM
AND the T bit and the Z reg
become the 6th address bit
Add an M bit to the ROM
AND the M bit and the OP from bits IR[31:28] to become
the 10th-7th address bits
M, T
clock
5
8
2
2
ROM
State
Register
5
2
Next
State
24
Z
OP
4
1
10
2
2
M
O
D
I
F
I
E
R
5
TM Register
2
Note that the TM register is a small correction to the diagram in the book.
5

## Slide 88: What’s in MODIFIER?
Í
Z
OP
2
Top 5 bits of Next State
T
M
5
Value of Z if T-bit is set in the current state
Value of OP in IR (4 bits) if the M-bit is set in the current state
M and T from TM Register

## Slide 89: Question
The two-way modifier bit T is enabled…
In the last microstate of the Fetch state
In the middle of BEQ execution after operand comparison
Always
Never
Today’s number is 95,969
70

## Slide 90: Question
The Z bit input to the Modifier
Is always zero
Is the output of the ROM itself
Is the output of the Z register in the datapath
Is 1 if the instruction is BEQ
No clue
80
clock
5
8
2
2
ROM
State
Register
5
2
Next
State
24
Z
OP
4
1
10
2
2
M
O
D
I
F
I
E
R
5
TM Register
2
5

## Slide 91: So We Need to Set T in the Microcode
 | Drive Signals |  |  |  |  | Load Signals |  |  |  |  |  | Write Signals |  |  |  |  |  | 
Current State | PC | ALU | Reg | MEM | OFF | PC | A | B | MAR | IR | Z | MEM | REG | func | Reg Sel | M | T | Next State
010000 |  |  | 1 |  |  |  | 1 |  |  |  |  |  |  |  | 00 |  |  | 10001
010001 |  |  | 1 |  |  |  |  | 1 |  |  |  |  |  |  | 01 |  |  | 10010
010010 |  | 1 |  |  |  |  |  |  |  |  | 1 |  |  |  | 10 |  | 1 | 10011
110011 | 1 |  |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  | 1 | 10100
110100 |  |  |  |  | 1 |  |  | 1 |  |  |  |  |  |  |  |  | 1 | 10101
110101 |  | 1 |  |  |  | 1 |  |  |  |  |  |  |  | 00 |  |  |  | 00000
010011 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Here we need to fill in the contents of ROM location ifetch1. Why?

## Slide 92: What’s the Problem with the Z Branch?
beq1
beq2
beq3
ifetch1
…
Z = 0
beq4
beq5
beq6
Z = 1
010000
010001
010010
110011
110100
110101
000000
010011

## Slide 93: An Old Microcode Trick!
beq1
beq2
beq3
ifetch1
…
Z = 0
beq4
beq5
beq6
Z = 1
010000
010001
010010
110011
110100
110101
000000
010011
Ifetch1-clone
We duplicate ifetch1 at the appropriate ROM address (so its clone does exactly the same thing). The clone transfers to the same next-state as the original!

## Slide 94: FETCH macro-state
Need to do
  We need to send PC to the memory
  Read the memory contents
  Bring the memory contents read into the IR
  Increment the PC
  (And decode the opcode by branching to the right execution state)
Microstates to accomplish
  ifetch1
    PC  MAR
  ifetch2
    MEM[MAR]  IR
  ifetch3
    PC  A
  ifetch4
    A+1  PC

## Slide 95: FETCH state (Simplifying)
ifetch1
  PC  MAR
  PC  A
ifetch2
  MEM[MAR]  IR
ifetch3
  A+1  PC

## Slide 96: FETCH state: Adding in control signals
ifetch1
  PC  MAR
  PC  A
  Control signals needed:
    DrPC
    LdMAR
    LdA
ifetch2
  MEM[MAR]  IR
  Control signals needed:
    DrMEM
    LdIR
ifetch3
  A+1  PC
  Control signals needed:
    func = 11
    DrALU
    LdPC

## Slide 97: Before ifetch1
WrREG
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
232 x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
IR
LdIR
Z
LdZ
=0?
32
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
1
1
IR[3..0]
IR[23..20]
IR[27..24]
RX
RY
RZ
00
01
10
regno
4
4
4
4
2
M
U
X
RegSel

## Slide 98: Implementing ifetch1 (end of clock 1)
WrREG
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
232 x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
IR
LdIR
Z
LdZ
=0?
32
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
1
1
IR[3..0]
IR[23..20]
IR[27..24]
RX
RY
RZ
00
01
10
regno
4
4
4
4
2
M
U
X
RegSel
PC
PC
PC+B
M[PC]
PC
DrPC
LdMAR
LdA
Others=0

## Slide 99: Implementing ifetch2 (end of clock 2)
WrREG
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
232 x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
IR
LdIR
Z
LdZ
=0?
32
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
1
1
IR[3..0]
IR[23..20]
IR[27..24]
RX
RY
RZ
00
01
10
regno
4
4
4
4
2
M
U
X
RegSel
PC
PC
PC+B
M[PC]
M[PC]
DrMem
LdIR
Others=0

## Slide 100: Implementing ifetch3 (end of clock 3)
WrREG
32
PC
LdPC
A
LdA
B
LdB
MAR
LdMAR
memory
232 x
32 bits
DrMEM
DrALU
DrPC
ALU:
00: ADD
01: NAND
10: A
-
B
11: A + 1
func
=11
2
WrMEM
Addr
Din
Dout
registers
16x
32 bits
DrREG
Din
Dout
4
regno
IR
LdIR
Z
LdZ
=0?
32
DrOFF
sign
extend
IR[31..0]
20
IR[19..0]
1
1
IR[3..0]
IR[23..20]
IR[27..24]
RX
RY
RZ
00
01
10
regno
4
4
4
4
2
M
U
X
RegSel
PC
PC
PC+1
M[PC]
M[PC]
func=11
DrALU
LdPC
Others=0
PC+1
PC+1

## Slide 101: DECODE State
Decode is a MULTIWAY branch!
We can’t encode this in Next State!
Actually, we can, given the modification to the Control Unit we made for BEQ
Fetch
R-Type
I-Type
J-Type
O-Type

## Slide 102: DECODE State
We’ll use the same trick we used for BEQ
On the last step of ifetch, we’ll set the top 4 bits of our ROM address to the opcode that’s in IR[31:28]!
OK. How do we do that?
Fetch
R-Type
I-Type
J-Type
O-Type

## Slide 103: We’re Going to Tweak the Control Unit
clock
DrPC, DrALU, DrREG,
DrMEM, DrOFF
LdPC, LdA, LdB, LdMAR,
LdIR, LdZ, WrREG, WrMEM
func
5
8
2
2
ROM
State
Register
5
2
RegSel
Next
State
24
Z
OP
4
1
10
2
T
2
M
O
D
I
F
I
E
R
5
Datapath
So what are we adding?
Add a T bit to the ROM
AND the T bit and the Z reg
become the 6th address bit
Add an M bit to the ROM
AND the M bit and the OP from bits IR[31:28] to become
the 10th-7th address bits
M, T
TM Register
2
5

## Slide 104: Let’s Encode the 3 ifetch States
 | Drive Signals |  |  |  |  | Load Signals |  |  |  |  |  | Write Signals |  |  |  |  |  | 
Current State | PC | ALU | Reg | MEM | OFF | PC | A | B | MAR | IR | Z | MEM | REG | func | Reg Sel | M | T | Next State
0000000000 | 1 |  |  |  |  |  | 1 |  | 1 |  |  |  |  |  |  |  |  | 00001
0000000001 |  |  |  | 1 |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 00010
0000000010 |  | 1 |  |  |  | 1 |  |  |  |  |  |  |  | 11 |  |  |  | 10000
So how do we make it take that multi-way branch?
Just set the M bit at 0000000010!
1

## Slide 105: Next State After the Last State of Fetch
Fetch
ADD
NAND
JALR
HALT
0000
10000
0001
10000
0110
10000
0111
10000
. . . . . .
Base address from ROM in Next State
0
0
0
0

## Slide 106: ROM Contents
ROM
. . . .
. . . .
ifetch1
ifetch2
ifetch3
add1
add2
add3
beq1
beq2
beq3
ifetch1-clone
Start of exec sequence
ADD
NAND
…
Base
beq4

## Slide 107: EXECUTE state: ADD instruction
RX  RY + RZ

## Slide 108: EXECUTE state: ADD instruction
add1
  Ry  A
  Control signals needed:
    RegSel = 01
    DrREG
    LdA
add2
  Rz  B
  Control signals needed:
    RegSel = 10
    DrREG
    LdB
add3
  A+B  Rx
  Control signals needed:
    func = 00
    DrALU
    RegSel = 00
    WrREG
add1
add2
add3
ifetch1
.
.
.

## Slide 109: EXECUTE state: ADD instruction
What must be changed in ADD to implement NAND?

## Slide 110: EXECUTE state: JALR instruction
JALR instruction does the following:
  RY  PC + 1
  PC  RX
jalr1
  PC  Ry
  Control signals needed:
    DrPC
    RegSel = 01
    WrREG
jalr2
  Rx  PC
  Control signals needed:
    RegSel = 00
    DrREG
    LdPC

## Slide 111
When all of the control signals are zero in the LC-2200 datapath, what value is being presented by the ALU to DrALU?
A+B
The value of one of the registers
Zero
Floating
90

## Slide 112: Alternative Style of Control Unit Design
A number of different approaches may be used to implement the Control Unit

## Slide 113: Microprogrammed Control
As presented our design works
Problem: Slower than a combinational logic control
  Solution: Pre-fetch the next microinstruction
Problem: Too much memory required
  Solution: OR the opcode with the next state value 10000 instead of pre-pending it
  Solution: Use more than one ROM
    One set of ROMs for which state comes next
    One for what the control outputs should be in the state
  Solution: More sophisticated Decode/BEQ logic

## Slide 114: 3-ROM Microsequencer
Main
ROM
2m entries
m-bit state register
Z ROM 2 entries
Opcode ROM
2n m-bit entries
(n is # of opcode bits)
S1
S0
00
01
10
Other control signals
(DrREG, DRMEM, LdPC, etc.)
IR[31:28]
Z
MUX
m
19
m
m
m

## Slide 115: Space/Time Tradeoff
Flat ROM
  More space (since we increased the ROM by a factor of 32 for the occasional address modifiers, but have extra ROM space)
  Faster since only one ROM access in each microinstruction
Micro sequencer (3-ROM control unit)
  Less space (main ROM much smaller than Flat ROM)
  Slower since additional ROM access in every clock cycle

## Slide 116: Hardwired Control
State machine can be represented as sequential logic truth table
Thus the state machine can be implemented using normal combinational logic or FPGA

## Slide 117
Control Regime | Pros | Cons | Comment | When to use | Examples
Micro-programmed | Simplicity, maintainability, flexibility Rapid prototyping | Potential for space and time inefficiency | Space inefficiency may be mitigated with vertical microcode Time inefficiency may be mitigated with prefetching | For complex instructions, and for quick non-pipelined prototyping of architectures | PDP 11 series, IBM 360 and 370 series, Motorola 68000, complex instructions in Intel x86 architecture
Hardwired | Amenable for pipelined implementation Potential for higher performance | Potentially harder to change the design Longer design time | Maintainability can be increased with the use of structured hardware such as PLAs and FPGAs | For High performance pipelined implementation of architectures | Most modern processors including Intel x86 series, IBM PowerPC, MIPS

## Slide 118: 3.6.3 Choosing between the two control design styles
Control Regime | Microprogrammed | Hardwired
Pros | Simplicity, maintainability, flexibility. Rapid prototyping | Amenable for pipelined implementation. Potential for higher performance
Cons | Potential for space and time inefficiency | Potentially harder to change the design. Longer design time
Comments | Space inefficiency may be mitigated with vertical microcode. Time inefficiency may be mitigated with pre-fetching | Maintainability can be increased with the use of structured hardware such as PLAs and FPGAs
When to use | For complex instructions, and for quick non-pipelined prototyping of architectures | For high performance pipelined implementation of architectures
Examples | PDP 11 series, IBM 360 and 370 series, Motorola 68000, complex instructions in Intel x86 architecture | Most modern processors including Intel Pentium series, IBM PowerPC, MIPS