## Slide 1: Memory Management
Ramachandran & Leahy, Chapters 7 & 8

## Slide 2: So far
Software | Hardware
High level language + compiler + linker | ISA, addressing modes, stack, registers
Program discontinuities (INT handler in OS) | Interrupt support, processor implementation (simple + pipeline)
OS process scheduler + loader | Process as an abstraction, context switching
OS memory management | Hardware support for memory management

## Slide 3: A “small” laptop’s workload
    4 applications
123 processes!
1208MB of 2GB memory in use

## Slide 4: Goals of memory management
What functionalities do we want to provide?
Improved resource utilization
Independence and protection
Liberation from resource limitations
Sharing of memory by concurrent processes
So far there’s no hardware in the LC-2200 to “manage” memory

## Slide 5: Nothing in LC-2200 to manage memory
CPU
Memory
Address
Data
Memory bus

## Slide 6: What’s missing in LC-2200?
Nothing to protect the OS, P2, and P3 from P1
No way to move P1 – it knows where it is loaded in memory
Can’t run more processes than we have memory for
Memory use is exclusive to a process
CPU
OS
Memory bus
P1
P2
P3
P1 is running

## Slide 7: To manage memory…
CPU
B
R
O
K
E
R
Memory
CPU generated
Address
Memory
Address
Combination: management (a.k.a policy)  software mechanism  hardware
Introduce a broker
So is the broker hardware or software??

## Slide 8: Simple management
Hardware mechanism
(new register in hardware: FENCE)
CPU
Memory
CPU generated
Address
Memory
Address
>
Fence register
Trap
Y
N
Kernel
User
Low
High
One user process at a time
Separation needed between OS and user program
But modern operating systems are multiprogrammed!

## Slide 9: Fence register example
CPU
Memory
CPU generated
Address
Memory
Address
>
Fence register
0x2FFF
Trap
Y
N
Kernel
User
Low
High
Provide protection for the OS
Performed by hardware without help from the CPU
0x2FFF
If the CPU is in “kernel” state, execute the memory operation
Else if address is >= 0x3000, execute the memory operation
Else cause a “memory protection violation” trap

## Slide 10: Multiprogrammed OS
CPU
Memory
CPU
Address
Memory
Address
>
Lower bound
Trap
Y
N
Kernel
Low
High
Upper bound
<
Trap
N
Y
P2
P1
Pn
.
.
.
.
Separation of address space for each process
Hardware mechanism
(new registers: LB, UB)
P1 is running
LBP1
UBP1

## Slide 11: Bounds registers example
CPU
Memory
CPU
Address
Memory
Address
>
Lower bound
0x2FFF
Trap
Y
N
Kernel
Low
High
Upper bound
0x3101
<
Trap
N
Y
P2
P1
Pn
.
.
.
.
Separation of address space for each process
P1 is running
0x2FFF
0x3101
If the CPU is in “user” state and address is <= 0x2fff and
address is >= 0x3101, trap on address violation
Else execute the memory operation

## Slide 12: Multiprogrammed OS
CPU
Memory
CPU
Address
Memory
Address
>
Lower bound
Trap
Y
N
Kernel
Low
High
Upper bound
<
Trap
N
Y
P2
P1
Pn
.
.
.
.
Separation of address space for each process
Hardware mechanism
(new registers: LB, UB)
P2 is running
LBP2
UBP2

## Slide 13: Bounds registers example
CPU
Memory
CPU
Address
Memory
Address
>
Lower bound
0x2FFF
Trap
Y
N
Kernel
Low
High
Upper bound
0x3101
<
Trap
N
Y
P2
P1
Pn
.
.
.
.
Separation of address space for each process
P1 is running
0x2FFF
0x3101
If the CPU is in “user” state and address is <= 0x2fff and
address is >= 0x3101, trap on address violation
Else execute the memory operation

## Slide 14: Bounds registers example
CPU
Memory
CPU
Address
Memory
Address
>
Lower bound
0xD9FF
Trap
Y
N
Kernel
Low
High
Upper bound
0xE801
<
Trap
N
Y
P2
P1
Pn
.
.
.
.
Separation of address space for each process
P2 is running
0xD9FF
0xE801
If the CPU is in “user” state and address is <= 0xD9ff and
address is >= 0xE801, trap on address violation
Else execute the memory operation

## Slide 15
What needs to happen to ensure that LB and UB correspond to the currently running process?
Restore LB and UB to the system stack
Restore LB and UB to values defined in the source code file
Restore LB and UB to values from the PCB
Calculate LB and UB from the process-id
The number of the day is 36,040.
10

## Slide 16: PCB
enum state_type {new, ready, running, waiting, halted};
typedef struct control_block_type {
enum state_type state;
address PC;
int reg_file[NUMREGS];
struct control_block *next_pcb;
int priority;
address memory_footprint; ????
….
….
} control_block;

## Slide 17: PCB
enum state_type {new, ready, running, waiting, halted};
typedef struct control_block_type {
enum state_type state;
address PC;
int reg_file[NUMREGS];
struct control_block *next_pcb;
int priority;
address LB;
address UB;
….
….
} control_block;

## Slide 18: “Management” by the OS
At load time (loader)
  Place P1 in memory
  Set LB and UB in the PCB
At context switch time (dispatcher)
  Load LB and UB from the PCB into the new CPU registers
P1
P1
LB
UB
Mem

## Slide 19: Limits of “bounds register” mechanism?
Relocation isn’t possible
Swapping-in can be a problem
OS
P1
P2
1000
2000
3000
swap
dormant

## Slide 20: Limits of “bounds register” mechanism?
Relocation isn’t possible
Swapping in is a problem
OS
P3
P2
1000
2000
3000
P1
P1 swapped out
P2 finishes

## Slide 21: Limits of “bounds register” mechanism?
Relocation isn’t possible
Swapping in is a problem
OS
P3
1000
2000
3000
P1
P1 swapped out
We need to bring P1 back into memory
Where?
We have an empty spot…
Will this work?
P1

## Slide 22: Can we move an LC-2200 process?
When do we lock-in memory addresses?
  At assembly/link time  called static relocation
  P1 can only be in memory between 1000 & 2000
  That gives us poor memory utilization
  i.e. not dynamically relocatable
So the program must be loaded into the address range into which it was linked. There’s no way we could move it later.
How about we forbid absolute addresses in our program code?
  It would be relocatable at load time

## Slide 23: Can we make P1 dynamically relocatable?
Don’t hard code addresses in executable
Set memory bounds at load time rather than link time
This implies making all addresses relative to some base register or the PC
But what happens when we execute
  LEA
  JALR
… Memory addresses get saved in registers!
  Where can they be copied or modified from there?
  Can we find them so we can fix them?
  This is why we’d say the LC-2200 code is not dynamically relocatable
  You still can’t move LC-2200 code once it’s started to run
IBM did this in System/360, but the CDC 6600 didn’t…

## Slide 24: But there’s a hardware solution…
CPU
Memory
CPU
Address
Memory
Address
+
Base
Kernel
Low
High
Limit
<
Trap
N
Y
P1
P2
Pn
.
.
.
.
Dynamically relocatable multiprogrammed OS
Hardware mechanism
(new registers: BASE, LIMIT)
P1 is running
BASEP1
LIMITP1
3000
4000

## Slide 25: But there’s a hardware solution…
CPU
Memory
CPU
Address
Memory
Address
+
Base
Kernel
Low
High
Limit
<
Trap
N
Y
P1
P2
Pn
.
.
.
.
Dynamically relocatable multiprogrammed OS
Hardware mechanism
(new registers: BASE, LIMIT)
P2 is running
BASEP2
LIMITP2
3000
4000
12000
13000

## Slide 26: Base & limit register example
CPU
Memory
CPU
Address
Memory
Address
+
Base
3000
Kernel
Low
High
Limit
4000
<
Trap
N
Y
P1
P2
Pn
.
.
.
.
If CPU is in user state, add Base to address
  If address < Limit, execute the operation
P1 is running
3000
4000
Program 1 uses addresses
0 - 1000
607
3607
3607

## Slide 27: Base & limit register example
CPU
Memory
CPU
Address
Memory
Address
+
Base
12000
Kernel
Low
High
Limit
13000
<
Trap
N
Y
P1
P2
Pn
.
.
.
.
If CPU is in user state, add Base to address
  If address < Limit, execute the operation
P2 is running
12000
13000
Program 2 uses addresses
0 - 1000
607
12607
12607

## Slide 28: PCB
enum state_type {new, ready, running, waiting, halted};
typedef struct control_block_type {
enum state_type state;
address PC;
int reg_file[NUMREGS];
struct control_block *next_pcb;
int priority;
address memory_footprint; ????
….
….
} control_block;

## Slide 29: PCB
enum state_type {new, ready, running, waiting, halted};
typedef struct control_block_type {
enum state_type state;
address PC;
int reg_file[NUMREGS];
struct control_block *next_pcb;
int priority;
address BASE;
address LIMIT;
….
….
} control_block;

## Slide 30: The previous example with BASE + LIMIT
Now all of P1 and P2’s addresses appear to start at zero
This is our first instance of a virtual address where the process sees memory addresses different from the physical addresses we’ve been working with so far!
OS
P1
P2
1000
2000
3000
swap
dormant
P1 sees virtual addresses 0 – 999
P1 uses physical addresses 1000-1999

## Slide 31: The previous example with BASE + LIMIT
Now all of P1 and P2’s addresses appear to start at zero
This is our first instance of a virtual address where the process sees memory addresses different from the physical addresses we’ve been working with so far!
OS
P3
P2
1000
2000
3000
P1
P2 finishes

## Slide 32: The previous example with BASE + LIMIT
Now all of P1 and P2’s addresses appear to start at zero
This is our first instance of a virtual address where the process sees memory addresses different from the physical addresses we’ve been working with so far!
OS
P3
1000
2000
3000
P1
We need to bring P1 back into memory
Where?
We have an empty spot…
Will this work?
It will if we set BASE & LIMIT to 2000 & 3000
P1 sees virtual addresses 0 – 999
P1 uses physical addresses 2000-2999

## Slide 33
To support dynamic relocation on the LC-2200, we would need…
Fence register
Base + Limit registers
Bounds registers
LC-2200 works just fine as it is
Today’s number is 24,987
20

## Slide 34: Recap
Hardware | Software
Fence register | User/kernel split
Bounds register | Static relocation
Base + limit register | Dynamic relocation
Next
Allocation policies
Paging

## Slide 35: Memory allocation by OS
Fixed size partition
Variable size partition
Both use the hardware base + limit registers

## Slide 36: Fixed size partitions
5K
8K
OS memory manager allocation table
Occupied bit
Partition Size
Process
0
5K
---
0
8K
---
memory
Struct AT_entry {
int occupied;
int size;
int pid;
};

## Slide 37: P1 needs 6K of memory
5K
Allocation table
Occupied bit
Partition Size
Process
0
5K
---
1
8K
P1
Memory
6K
2K

## Slide 38: P1 needs 6K of memory
5K
Allocation table
Table size is fixed = number of partitions
Occupied bit
Partition Size
Process
0
5K
---
1
8K
P1
Memory
6K
2K
Needs only 6K

## Slide 39: Another process needs 6K memory
5K
Internal fragmentation = size of partition – actual used
Allocation table
Occupied bit
Partition Size
Process
0
5K
---
1
8K
P1
Memory
6K
2K
Needs only 6K
Wasted
(internal fragmentation)

## Slide 40: Another process needs 6K memory
5K
Do we have it?
Memory manager has only a 5K partition…
Not possible
Allocation table
Occupied bit
Partition Size
Process
0
5K
---
1
8K
P1
Memory
6K
2K

## Slide 41: External fragmentation
1K
Consider P3 that needs 4K of memory
Is it possible to allocate?
Memory is available, but not contiguous
Allocation table
Occupied bit
Partition Size
Process
1
1K
P1
Memory
3K
2K
0
2K
---
1
3K
P2
0
2K
---
2K
External fragmentation
= ∑ All non-contiguous free memory partitions
And we have 4K of non-continuous memory here
Which gives us 4K of external fragmentation

## Slide 42: Fragmentation
Internal fragmentation
  Size of partition – actual memory used
External fragmentation
  ∑ All non-contiguous free partitions
  If there is only one free partition, we say the external fragmentation is zero

## Slide 43: Fixed size partition memory management
Virtues
  Simplicity
Bad news
  Fragmentation
    Internal
    External

## Slide 44
Total internal fragmentation is…
2K
3K
5K
8K
23
2K
Allocation table
Occupied bit
Partition Size
Process
1
5K
P2 (need 2k)
1
8K
P1 (need 6K)
Memory
6K
2K
3K

## Slide 45
Total external fragmentation is…
0K
2K
5K
8K
27
2K
Allocation table
Occupied bit
Partition Size
Process
1
5K
P2 (need 2k)
1
8K
P1 (need 6K)
Memory
6K
2K
3K

## Slide 46: Overcoming internal fragmentation
Allocate exactly what is needed
Variable size partitions

## Slide 47: Variable size partitions
13K
Memory manager allocation table
Start address
Size
Process
0
13K
FREE
memory
Struct AT_entry {
int start;
int size;
int pid;
};

## Slide 48: Partition table a little while later
Allocation table
Start address
Size
Process
0
2K
P1
Memory
2K
6K
P2
8K
3K
P3
11K
2K
FREE
11K
2K
Grows and shrinks as partitions get created and released

## Slide 49: P1 exits
Allocation table
Start address
Size
Process
0
2K
P1 -> FREE
Memory
2K
6K
P2
8K
3K
P3
11K
2K
FREE
9K
2K
2K
New request:
P4 needs 4K
Possible?
External fragmentation

## Slide 50: P2 exits
Allocation table
Start address
Size
Process
0
2K
FREE
Memory
2K
6K
P2 -> FREE
8K
3K
P3
11K
2K
FREE
9K
2K
2K

## Slide 51: Coalescing two free areas
Allocation table
Start address
Size
Process
0
8K
FREE
Memory
8K
3K
P3
11K
2K
FREE
3K
2K
8K

## Slide 52: Reducing external fragmentation
First fit algorithm
  A little quicker
Best fit algorithm
  A little better memory utilization
Next fit algorithm
  A little less space efficient in the average case
  A little quicker than first-fit

## Slide 53: Compaction
Allocation table
Start address
Size
Process
0
8K
FREE
Memory
8K
3K
P3
11K
2K
FREE
3K
2K
6K
2K
Request for 9K

## Slide 54: Compaction
Allocation table
Start address
Size
Process
0
3K
P3
Memory
3K
10K
FREE
3K
10K
Relocate P3
Create contiguous space
Note this is a rather expensive action

## Slide 55
With variable size partition memory management there is …
No external fragmentation
No internal fragmentation
No fragmentation
Both internal and external fragmentation
30

## Slide 56: External fragmentation with variable size partitions
Can limit full usage of memory resources
Compaction is too expensive

## Slide 57: How might we solve the external fragmentation problem?
Our memory footprint looks like this:
What’s the main limiting assumption?
That the process address space is contiguous!
Code
Data
Heap
Stack
High
Low
0
4K

## Slide 58: How might we solve the external fragmentation problem?
What if we could store our memory footprint in discontinuous memory locations?
But how can we implement this?
1K
2K
3K
4K
5K
6K
7K
8K
9K
10K
11K
Code
Data
Heap
Stack
High
Low
0
4K
2
0
3
1
2K

## Slide 59: Could the broker help?
What if we could store our memory footprint in discontinuous memory locations?
But how can we implement this?
1K
2K
3K
4K
5K
6K
7K
8K
9K
10K
11K
Code
Data
Heap
Stack
High
Low
2
0
3
1
Broker
contiguous
discontiguous
0
4K
2K

## Slide 60: Broker for paging
This broker maps
  Virtual address (VA) from the CPU
  to
  Physical address (PA) to memory
CPU
B
R
O
K
E
R
Memory
Virtual
Address
Physical
Address

## Slide 61: Broker for paging
How does Broker map VA to PA?
Perhaps like a phone directory?
  Who sets it up?
  Who looks it up?
CPU
B
R
O
K
E
R
Memory
Virtual
Address
Physical
Address
Page
Table
 The OS
 The hardware, on every access

## Slide 62: How big is this table?
At the lower size limit, we could map the whole program
  There would be only one entry in the page table
  That’s the same as Base + Limit, no?
At the upper size limit, we could map every word
  The table would be the size of the address space times the address size in words
  Not very practical
So in between, we choose a page size to map
  Bigger pages get us more internal fragmentation (average is ½ of the last page)
  Smaller pages get us a bigger page table and take more CPU time to manage it

## Slide 63: Choosing a page size
When memory was expensive (and small)
  Page sizes were 512 to 2048 bytes
These days
  4 KB up to 1 GB
  Often it’s settable per process
Page size is always a power of 2
  The power of two allows us to split the VA into virtual page number (VPN) and offset within the page at a bit boundary
  If the page size is 2n, the lower n bits are the offset and bit n and up are the virtual page number

## Slide 64: Splitting up a virtual address
Say we have a 4KB page size and a 32 bit virtual address space
  4KB is 212, so the bottom 12 bits are offset and the top 20 bits are VPN
For example, for virtual address 0x00004FFF
00004
FFF
0
11
31
12
4
Offset
VPN
4095

## Slide 65: Page table in use
Page 3
Page 2
Page 1
Page 0
User’s view
15
12
52
35
52
35
15
12
Page Table
Physical
Memory
LOW
HIGH

## Slide 66: Address translation
CPU
Memory
Virtual
Address
Physical
Address
VPN
Page table
Page offset
PFN
PFN
Page offset

## Slide 67: Examples
Consider a memory system with a 32-bit virtual address. Let us assume the pagesize is 8K Bytes.
How big is the page table?
8k = 213
VPN is 19 bits, so page table is 219 or 524,288 entries
VPN
offset
0
12
31
13
13 bits
19 bits

## Slide 68: Examples
Consider a memory system with 32-bit virtual addresses and 24-bit physical memory addresses. Assume that the pagesize is 4K Bytes.
  How many page frames can be in memory?
    PFN bits = 24 – 12 = 12; 212 frames
  How big is the page table?
    VPN bits = 32 – 12 = 20; 220 entries

## Slide 69: Example
CPU
Physical
Memory
4K page = 212 bytes
VPN
offset
0
11
31
12
12 bits
20 bits
220 page table entries
PFN
Page table
PFN
offset
0
11
24
12
12 bits
12 bits
32-bit Virtual Address
24-bit Physical Address
Offset will be the same
212 page frames

## Slide 70: Important facts about paging
Virtual (process) address space
Physical memory space
VA
PA
VPN
offs
PFN
offs
Virtual
pages
Page frames
2nv virtual pages
Determined by ISA
Virtual page size
2np physical page frames
Determined by physical mem
Physical frame size
VP start
PF start
offset
offset
1400
5400
Rarely equal
Always equal
VPN=1
offs=400
PFN=5
offs=400
translation
0
Highest address
np
nv

## Slide 71: So exactly where is the page table?
Hardware!
But it’s not a special device
It’s in physical memory!
CPU
B
R
O
K
E
R
Memory
CPU generated
Address
Memory
Address
PT

## Slide 72: How many page tables are there?
Process 1, 2, 3, …, n in memory
We’ll need n page tables!
We need as many page tables as the number of processes!
CPU
B
R
O
K
E
R
Memory
CPU generated
Address
Memory
Address
PT

## Slide 73: What hardware assist does LC-2200 need?
Just one new register: PTBR
This holds the base physical address of the page table for the running process
And, of course, hardware in the broker to look up the PFN from the page table for each memory reference
Kernel
Space
Physical Memory
User Pages
Low
High
OS/Memory
manager
PTPn
…
PTP2
PTP1
Page frames for user programs
Frame table
Disk maps

## Slide 74: What hardware assist does LC-2200 need?
Just one new register: PTBR
This holds the base physical address of the page table for the running process
And, of course, hardware in the broker to look up the PFN from the page table for each memory reference
PFN
PFN
PFN
PFN
PFN
PFN
Page Table
PTBR

## Slide 75: PCB
enum state_type {new, ready, running, waiting, halted};
typedef struct control_block_type {
enum state_type state;
address PC;
int reg_file[NUMREGS];
struct control_block *next_pcb;
int priority;
address PTBR;
….
….
} control_block;

## Slide 76: Paged memory allocation
Allocate all at once at load time?
Allocate on demand?
 Not good: slow
 Better utilization

## Slide 77: Demand paging
Valid
PFN
PTE
Valid
PFN
Valid
PFN
Valid
PFN
Valid
PFN
Valid
PFN
Page Table
Page Table Entry
Is the page in memory?
0/1
PTBR

## Slide 78: Ramification of demand paging
IF
ID/RR
EX
MEM
RW
Instruction
in
Instruction
out
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
Potential page faults
I1
I2
I3
I4
I5
Where can a page
fault hit us?
Let I1 complete
Squash I2-I5
Trap to page fault handler,
saving PC of I2 for restart
after page fault is serviced
Page fault trap
I-fetch
Data access
As some of you guessed, we’ll need to make the original PC value part of the pipeline buffers

## Slide 79: Page fault handler
Find a free page frame
Load the faulting virtual page from disk into the page frame
Give up the CPU while waiting for the paging I/O to complete
Update the page table entry for the faulting page
Place the PCB of the process back in the ready_q of the scheduler
Call the scheduler

## Slide 80: Frame Table
<P2, 20>
free
<P5, 15>
<P1, 32>
free
<P3, 0>
<P4, 0>
free
<PID, VPN>
PFN
0
1
2
3
4
5
6
7
Page table maps forward; Frame table maps in reverse
We need this for evicting pages
Number of entries =
number of physical
memory page frames
struct frametbl {
int state;
ADDR pid;
ADDR vpn;
};

## Slide 81: Free list for page fault handler
…
Pframe 52
Pframe 20
Pframe 8
freelist
Pframe 200
struct pframe { address PFN; … pframe *next; };
8
20
52
200
Use a linked list
Or link free frame table entries together

## Slide 82: Disk Map
Swap space
P1
…..
P2
pn
disk address
VPN
0
1
2
3
4
5
6
7
Disk map for P1
disk address
disk address
disk address
disk address
disk address
disk address
disk address

## Slide 83: Physical memory layout
OS/Memory
manager
PTPn
…
PTP2
PTP1
Kernel
Space
Physical Memory
Page frames for user programs
User Pages
Low
High
Data structures of memory manager: page tables, frame table, etc.
For P2
For P1
Frame table
Page Frame 0
Page Frame 1
Page Frame 2
Page Frame 3
Page Frame 99
Page Frame 100
Page Frame 101
Page Frame 102
Page Frame 103
Page Frame 104
Page Frame 105
Page Frame n-1
…
…
Disk maps

## Slide 84: Physical memory layout
Physical Memory
Low
High
Data structures of memory manager: page tables, frame table, etc.
Page Frame 0
Page Frame 1
Page Frame 2
Page Frame 3
Page Frame 99
Page Frame 100
Page Frame 101
Page Frame 102
Page Frame 103
Page Frame 104
Page Frame 105
Page Frame n-1
…
…
Each frame 0-103 is marked “wired” in the Frame Table. Page replace-ment never touches them!
Each frame 104-n-1 is marked “free” in the Frame Table
OS/Memory
manager
PTPn
…
PTP2
PTP1
Page frames for user programs
Frame table
Disk maps

## Slide 85: Virtual memory manager data structures
Per process | PCB | Holds saved PTBR register
Per process | Page table | VPN  PFN mapping Dual role: Memory manager uses it for setup Hardware uses on each memory access
Per system | Free list | Free page frames in physical memory
Per system | Frame table | PFN to <PID, VPN> mapping needed for evicting pages from physical memory
Per process | Disk map | VPN to disk block mapping needed for bringing missing pages from disk to physical memory

## Slide 86: PCB
enum state_type {new, ready, running, waiting, halted};
typedef struct control_block_type {
enum state_type state;
address PC;
int reg_file[NUMREGS];
struct control_block *next_pcb;
int priority;
address PTBR;
disk_address *disk_map;
….
….
} control_block;

## Slide 87: Example
process P1 page fault at VPN = 20.
free-list is empty.
selects page frame PFN = 52 as the victim.
frame currently houses VPN = 33 of process P4

## Slide 88: Before
Missing page at VPN=20 for P1
Currenly PFN=52 in use by P4
Page replacement algorithm chooses PFN=52 as victim

## Slide 89: After

## Slide 90
With paged memory management there can be
External fragmentation
Internal fragmentation
No fragmentation
Both internal and external fragmentation
Today’s number is 36,050
40

## Slide 91
CPU
Hardware
CPU scheduler
…
PCB1
PCB2
ready_q
Kernel
Program 1
Program 2
Program n
……….
User level
Memory Manager
Timer interrupt
Page fault
Process dispatch
…
freelist
Pframe
Pframe
PT1
PT2
.
.
DM1
DM2
.
.
FT

## Slide 92: FIFO Page Replacement
<PID, VPN>
Circular queue
<PID, VPN>
…..
<PID, VPN>
Head
Tail
free
Full

## Slide 93: FIFO example
free
Circular queue
free
free
Head
Tail
Full = false
Consider a string of page references by a process:
Reference number: 1 2 3 4 5 6 7 8 9 10 11 12 13
----------------------------------------------------------
Virtual page number: 9 0 3 4 0 5 0 6 4 5 0 5 4
Assume there are 3 physical frames.

## Slide 94
9
free
free
Head
Tail
Full = false
Reference #1 (PF)
9
0
free
Head
Tail
Full = false
Reference #2 (PF)
9
0
3
Head
Tail
Full = true
Reference #3 (PF)
4
0
3
Head
Tail
Full = true
Reference #4 (PF)
4
0
3
Head
Tail
Full = true
Reference #5 (HIT)
4
5
3
Head
Tail
Full = true
Reference #6 (PF)
Ref: 1 2 3 4 5 6
VPN: 9 0 3 4 0 5

## Slide 95: Using the Frame Table as a Queue
In real life, there is very little reason to have time stamps or a separate queue for FIFO page replacement.
That’s because the Frame Table will serve that purpose nicely and not take up any extra space!
So in your mind, you can think of a queue ordered by timestamp for implementing FIFO, but it’s never actually implemented that way.
How? When the system starts up
  Point the Head pointer to the first Frame Table entry; you don’t really need the Tail pointer or Full flag
  Treat the end of the Frame Table as the limit of the circular queue after which the queue wraps around
  As you fill in the pages, they will naturally be ordered by time so when you wrap around, you will be considering the first-in pages first!

## Slide 96
9
free
free
Head
Reference #1 (PF)
9
0
free
Head
Reference #2 (PF)
9
0
3
Head
Reference #3 (PF)
4
0
3
Head
Reference #4 (PF)
4
0
3
Head
Reference #5 (HIT)
4
5
3
Head
Reference #6 (PF)
Ref: 1 2 3 4 5 6
VPN: 9 0 3 4 0 5

## Slide 97: Frame Table as FIFO Queue
If you read carefully, the textbook implies that this is the way to implement FIFO replacement, but it never makes that statement crystal clear
Also, you should be able to see that our Head pointer is acting like a “clock hand,” pointing to each frame in turn
We’ll use that term a bit later when we implement a version of LRU paging (which will still be based on this FIFO algorithm!)

## Slide 98: Size of the FIFO queue
3
Number of physical page frames
Number of virtual pages
No clue

## Slide 99: Belady’s Min
Consider a string of page references by a process:
Reference number: 1 2 3 4 5 6 7 8 9 10 11 12 13
----------------------------------------------------------
Virtual page number: 9 0 3 4 0 5 0 6 4 5 0 5 4
Theoretically the best algorithm
As the victim page, choose the page with the longest time to its next reference
Merely requires us to predict the future
If we had pages 0-9 in memory, which pages should we evict first?
(1, 2, 7, 8) can go first. Then 6, 5, 4, 3, 0, 9

## Slide 100
Why do we not implement Belady’s Min as a page replacement algorithm?
The CPU time required by the algorithm is excessive
The hardware required to support the implementation is too expensive
The algorithm is patented in the US and we’d have to obtain a license and pay royalties
It would require a component that we don’t know how to build
Today’s number is 10202
50

## Slide 101: LRU
<PID, VPN>
Push down stack
<PID, VPN>
…..
<PID, VPN>
top
bottom
free
Use the past as a predictor of the future.
Most recent reference
Least recent reference
Data structure in memory manager
Each element corresponds to a page frame

## Slide 102: LRU example
free
stack
free
free
top
bottom
Consider a string of page references by a process:
Reference number: 1 2 3 4 5 6 7 8 9 10 11 12 13
----------------------------------------------------------
Virtual page number: 9 0 3 4 0 5 0 6 4 5 0 5 4
Assume there are 3 physical frames.

## Slide 103
9
Reference #1 (PF)
free
free
Top
Bottom
0
Reference #2 (PF)
9
free
Top
Bottom
3
Reference #3 (PF)
0
9
Top
Bottom
4
Reference #4 (PF)
3
0
Top
Bottom
0
Reference #5 (HIT)
4
3
Top
Bottom
5
Reference #6 (PF)
0
4
Top
Bottom
Ref: 1 2 3 4 5 6
VPN: 9 0 3 4 0 5

## Slide 104
How many entries are needed for a complete LRU “stack”
1
Number of virtual pages
Number of physical page frames
No clue
60

## Slide 105: Problems with LRU
Memory references are known to the hardware, but memory management (i.e. victim selection) is in software
One possibility: make the stack shared by HW & SW
  Implement stack in hardware
  Let hardware update stack on each reference
  Let software (OS) use this stack as a data structure
Will it work?
Still, no. The size of the stack is the number of page frames and a memory write is required for each memory reference

## Slide 106: Ways to approximate LRU
Use a small hardware register stack
  Remember the last 16 or 32 references?
Reference bit per physical frame
  Add a “referenced” bit to each PTE
  Set it each time the hardware uses the PTE to translate a memory reference
  If it’s already set, don’t set it again.
Valid
PFN
Valid
PFN
Valid
PFN
Page Table
Ref
Ref
Ref

## Slide 107: Approximate LRU with ref bits
0
31
Per page
Frame
Reference
bits
0/1
0/1
Counter for Page frame 0
Counter for Page frame 1
0/1
…………
0/1
Counter for Page frame n
Keep ref bits in PT
  Set bit when page referenced  done by hardware
Paging daemon  background OS process
  Flush ref bits to software “counters” periodically counter = (ref << 31 | counter >> 1)
  Clear ref bits
Victim?
 The page with the counter that has the lowest value

## Slide 108: Second chance page replacement using reference bits
Initially clear all the referenced bits
As the process runs, set referenced bits on each page referenced
If a page has to be evicted, the memory manager selects a page in a FIFO manner
If the chosen victim's referenced bit is set, the manager clears the referenced bit and moves to the next page
The victim is the first page that doesn't have the referenced bit set

## Slide 109: Second chance replacement
1
1
Pointer
1
1
1
0
0
1
10
1
5
7
8
3
4
9
FIFO order
FIFO candidate
Try page 7
Its reference bit is set, so move on to page 8
Reference bit
(in Page Table)
Frame
Table
0
1
2
3
4
5
6
7

## Slide 110: Second chance replacement
1
1
Pointer
1
0
1
0
0
1
10
1
5
7
8
3
4
9
FIFO order
Try page 8
Its reference bit is set, so move on to page 3
Reference bit
(in Page Table)
Frame
Table
0
1
2
3
4
5
6
7

## Slide 111: Second chance replacement
1
1
Pointer
1
0
0
0
0
1
10
1
5
7
8
3
4
9
FIFO order
Try page 3
Its referenced bit is not set, so it is the victim
Reference bit
(in Page Table)
Frame
Table
0
1
2
3
4
5
6
7

## Slide 112: Second chance replacement
1
1
Pointer
1
0
0
0
0
1
10
1
5
7
8
3
4
9
FIFO order
Page out page 3
Page in page 2
Reference bit
(in Page Table)
Frame
Table
0
1
2
3
4
5
6
7

## Slide 113: Second chance replacement
1
1
Pointer
1
0
0
0
0
1
10
1
5
7
8
2
4
9
FIFO order
Page out page 3
Page in page 2
Reference bit
(in Page Table)
Frame
Table
0
1
2
3
4
5
6
7

## Slide 114: Second chance replacement
1
1
Pointer
1
0
0
0
0
1
10
1
5
7
8
2
4
9
FIFO order
Next FIFO candidate
Move the pointer past the just-read page 2
Wait for the next page fault…
Reference bit
(in Page Table)
Frame
Table
0
1
2
3
4
5
6
7

## Slide 115: Page replacement algorithms
ALGORITHM | HARDWARE ASSIST | COMMENTS
FIFO | None | Could lead to performance anomalies
Belady’s MIN | An oracle | Provably optimal; not realizable in hardware; useful as a standard
True LRU | Push down stack | Expected performance close to optimal; infeasible
Approximate LRU #1 | A small hardware stack | Expected performance close to optimal; worst-case performance may be similar to FIFO
Approximate LRU #2 | Reference bit per page | Expected performance close to optimal; moderate hardware complexity
Second chance replacement | Reference bit per page | Expected performance better than FIFO; memory manager implementation simplified compared to LRU schemes

## Slide 116: Page Table Entry (PTE) Example
Valid | PFN | Referenced (optional) | Dirty (optional) | Read-only (optional) | Other info
1 | 12 | 0 | 0 | 1 | 
1 | 16 | 0 | 0 | 0 | 
0 | 14 | 0 | 0 | 0 | 
1 | 36 | 1 | 0 | 0 | 
1 | 9 | 1 | 0 | 0 | No execute
0
1
2
3
4
VPN

## Slide 117: Oops!

## Slide 118: Back to our pipelined processor
With virtual memory…
Every memory access requires two memory accesses!
  PTE
  Actual memory word
This is bad news for the pipeline
At least one bubble for every instruction
IF
ID/RR
EX
MEM
RW
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
B
U
F
F
E
R
I1
I2
I3
I4
I5

## Slide 119: Speeding up address translation
CPU
Memory
Virtual
Address
Physical
Address
VPN
Page table
Page offset
PFN
PFN
Page offset
The entire page table won't fit in registers
But a subset can!
What if we add a small table into this process?
Small
Table

## Slide 120: Why will this work?
The locality of a program
  Sequential instructions
  Contiguous data structures
The set of pages being referenced at a given time is called the Working Set
CPU
Memory
Virtual
Address
Physical
Address
VPN
Page table
Page offset
PFN
PFN
Page offset
Small
Table

## Slide 121: TLB (translation lookaside buffer)
USER/KERNEL | VPN | PFN | VALID/INVALID
U | 0 | 122 | V
U | XX | XX | I
U | 10 | 152 | V
U | 11 | 170 | V
K | 0 | 10 | V
K | 1 | 11 | V
K | 3 | 15 | V
K | XX | XX | I
It will look something like the following table
It is an associative memory, which means it can search on a match on the first two columns and output the corresponding last two columns in one cycle

## Slide 122: Speeding up address translation
CPU
Memory
Virtual
Address
Physical
Address
VPN
Page table
Page offset
PFN
PFN
Page offset
The entire page table won't fit in registers
But a subset can!
What if we add a small table into this process?
Small
Table

## Slide 123: Speeding up address translation
CPU
Memory
Virtual
Address
Physical
Address
VPN
Page table
Page offset
PFN
PFN
Page offset
A TLB hit
Fast path
No bubbles
TLB

## Slide 124: Speeding up address translation
CPU
Memory
Virtual
Address
Physical
Address
VPN
Page table
Page offset
PFN
PFN
Page offset
A TLB miss
Slow path
Bubbles
TLB

## Slide 125: TLB
USER/KERNEL | VPN | PFN | VALID/INVALID
U | 0 | 122 | V
U | XX | XX | I
U | 10 | 152 | V
U | 11 | 170 | V
K | 0 | 10 | V
K | 1 | 11 | V
K | 3 | 15 | V
K | XX | XX | I
Specific to each process
Same for all processes
What's the implication of the U entries for a context switch?
 We'll need to flush the U entries on context switch
I
I
I
I

## Slide 126: Another new instruction
The LC-2200 is going to need
  Purge TLB
  or TLB flush
Who can execute this instruction?
  It can only be executed by the kernel

## Slide 127
Upon a context switch…
The entire TLB is flushed
Only the kernel portion of the TLB is flushed
Only the user portion of the TLB is flushed
No change to the TLB
Is class over yet?
Today’s number is 30,332
70

## Slide 128: Given the nature of a process
We want to increase multiprogramming to keep the CPU busy doing useful work
This is what we want to see:
CPU
I/O
Degree of multiprogramming
CPU utiliza-
tion

## Slide 129: Extending the utilization curve
Degree of multiprogramming
CPU Utilization
What's going on here??
Too many processes asking for memory
This is overcommitment of memory
We have a bigger working set than physical memory can hold
Nobody is getting any useful work done
Thrashing
Paging is implicit I/O on behalf of a process
 System becomes I/O bound
 Throughput drops precipitously
CPU utiliza-
tion

## Slide 130: Working set of a program
Working set is the set of pages needed to keep a process from paging
Working set size: number of page frames needed to hold working set
Virtual page number (VPN)

## Slide 131: Working set of a program
The working set changes over time
WSt3-t4 = { p1, p2 }
Virtual page number (VPN)
WSt7-t8= { p4, p1 }

## Slide 132: Memory pressure
P1, P2, P3, … are processes in memory each with a working set WSSi
The count of active processes signifies the degree of multiprogramming
How do we control the degree of multiprogramming
  ∑WSS > total physical memory
       swap out some processes
  ∑WSS < total physical memory
       increase degree of multiprogramming

## Slide 133: Controlling thrashing
# physical frames per process
Page faults
High water
mark
Low water
mark
Too many page faults
 lower mp
Too few page faults
 raise mp
Sweet spot!

## Slide 134: Page faults are disruptive…
… from a process point of view  implicit I/O
… from a CPU-utilization perspective  overhead that doesn’t contribute to work
We need to limit impact of page faults to improve system performance

## Slide 135
We can tell a system is thrashing when
It has too few page faults per second
It has too many page faults per second
The ratio of I/O operations to CPU operations is not optimal
The combined working set of all processes is greater than the number of available page frames
80
If only it were as easy as B! Thrashing implies too many page faults, but too many page faults don’t always imply thrashing! Applications can be changing the pages in use without changing their working set size, for instance.
In RL, to diagnose thrashing, you’d look for a high paging rate, low CPU utilization, and several processes waiting on paging I/O for several seconds. Those metrics together are a good clue.
Today’s number is
81,818

## Slide 136
We can reduce thrashing by
Using a medium-term scheduler that suspends processes until the condition improves
Reducing the physical memory size
Adding additional processes to increase the multiprogramming factor
Reducing the page size
90
Of course this begs the question of how the medium-term scheduler is going to figure out that the system is thrashing…

## Slide 137: Optimizations
freelist
Pframe 52
Dirty
Pframe 22
Clean
Pframe 200
Clean
….
Keep a (small) pool of free frames
  Overlap I/O with processing
  Don’t wait to start page replacement algorithm on a page fault
Page replacement
  Background activity of OS when CPU is not in use
  If I/O is not busy, write out a “dirty” page which makes it “clean”
victim
Skip
(look for a clean one)

## Slide 138: Reverse mapping to page table
freelist
Pframe 52
Dirty
Pframe 22
Clean
Pframe 200
Clean
….
<P4, 33>
<P1, 12>
<P2, 43>
  Gives a “third” chance for reuse of a page before being kicked out
  Record the PID and VPN when the page is put on the free list
  Example: P4 is running and page faults on VPN=33
  No need to go to disk!
  Just remap PFN=52 into PT for P4, VPN=33 and take it out of the freelist

## Slide 139: Linux VM and kswapd
Kswapd
  Paging daemon
  Runs when “free” memory is low (about 2% of memory)
  Uses a modified version of second-chance replacement
  Links victim pages into the free list and sets their “invalid” PTE bits, writing it out if it’s dirty
Page fault handler:
  If the target page is still on the free list, it is reclaimed by removing it from the free list and marking its PTE bit “valid”
  Otherwise, the first frame on the Free List is removed, the target page is read into it, and the target page’s PTE is modified to point to it and “valid” is set
$ free -h
total used free shared buffers cached
Mem: 15G 7.1G 8.5G 164K 703M 2.4G
…
-/+ buffers/cache: 4.0G 11G
Swap: 2.0G 26M 1.9G

## Slide 140: Segmented virtual memory
Segmentation is a system allowing a process's memory space to be subdivided into chunks of memory each associated with some aspect of the overall program
Segmented virtual memory came first, ca. 1960, see Burroughs B5500.
Segmentation isn’t transparent like paging, but it is much more aware of program and data structures
It’s visible to the ISA, so it doesn’t work as a retrofit to ISAs with contiguous memory models. IBM couldn’t use it in the 1970s because they had already committed to upper/lower bound register memory management and a contiguous address space.
Hence, we have paging which could be transparently slipped under existing memory management. Other manufacturers followed suit because paging didn’t require their applications to be aware of paging.

## Slide 141: Segmented virtual memory
Segmentation is a system allowing a process's memory space to be subdivided into chunks of memory each associated with some aspect of the overall program
Segments can be different sizes
Segmented virtual memory came first, but it’s visible to the ISA, so it doesn’t work as a retrofit to ISAs with contiguous memory models
Typical segments
  Code segments (up to 1 per function)
  Global data
  Heap (perhaps arrays in separate segments)
  Stack (perhaps arrays in separate segments)

## Slide 142: Segmented virtual memory
Process address space divided up into n distinct segments based on the program organization
Each segment has
  A number
  A size
Each segment starts at its own address 0 and goes up to its size – 1.
Segment addressing

## Slide 143: Segmented virtual memory example

## Slide 144: Hardware for segmentation
What’s different from paged virtual memory?
An opportunity for external fragmentation?

## Slide 145: 64-bit Virtual Addresses?
Page tables can be BIG and we need one for each process in memory
For example a 64-bit virtual address with 4KB pages means the VPN is 64 - 12 = 52 bits long.
If a page table entry is 64 bits, how much space does one use?
252 entries* 23 bytes = 255 bytes = 215 * 240 bytes
  = 32768 Terabytes(!)
And we still need one for each process!
Is there a problem here?

## Slide 146: Paged segmentation
Segment number
Page number
Offset
Descriptor base register
Segment descriptor
Segment descriptor
Segment descriptor
Segment descriptor
Segment descriptor
Segment descriptor
Segment descriptor
Segment descriptor
S
P
W
S
P
W
Virtual Address
Descriptor for s
Page Table for p
Virtual Page
PT base for s
Limit
PTE
PTE
PTE for p
PTE
Segment Descriptor
Table
Intel x86-64 uses a scheme like this (but with 4 levels and all tables having 512 entries)
So did MULTICS in the 70s

## Slide 147: 64-bit Physical Addresses?
How many bytes can you address with 64 bits?
Obviously, 264, right? Which is how big?
1.84 x 1019 or 1,840 followed by 15 zeros. That’s 1,840,000 terabytes or 1.84 exabytes
Largest Intel/AMD memory supported today is 16 TB
Do we need all 64 physical address bits?
48 bits (248) will get us 281 TB. That should be enough for current chips to become obsolete.

## Slide 148: Intel’s X86-64 4-layer Page Tables

## Slide 149
Which of these is False?
Variable length partitions have internal but no external fragmentation
Paged memory systems have internal but no external fragmentation
Segmented memory systems have external but no internal fragmentation
Paged segmented memory systems have internal but no external fragmentation
100